## Slide 1: JVET-N00278: AHG17/AHG15: On VVC HLS relevant to MPEG requirements on immersive media delivery and access (N18134)
Jill Boyce

## Slide 2: Introduction
Proposal for VVC high level syntax to address some of the issues raised in M46578, “On the decoding interface for Immersive Media”
Include bitstream and decoder support for multiple independent layers in first VVC version
7-bit nuh_layer_id syntax element in the two-byte NAL Unit header
Introduce Video Parameter Set (VPS)
    Indication of the maximum number of layers
    Flag to indicate that all layers are independent, using “reserved” name
    Tool constraint flags in the general_constraint_info( ) syntax structure signalled once in the VPS and applied to all layers in the bitstream, rather than signalled per layer in the profile_tier_level( ) syntax structure
    v2 version of document adds a loop of syntax elements vps_included_layer_id[i]
    Possibly combine with the DPS
-v2 version updates sub-bitstream extraction process to extract single layer for target nuh_layer_id value, LIdTarget

## Slide 3: Background on HEVC
HEVC has a Video Parameter Set (VPS)
  Allows multiple bitstream layers to be included within the same bitstream
  Distinguishes between a Coded Layer-wise Video Sequence (CLVS) and a Coded Video Sequence (CVS)
HEVC has a two byte NAL unit header, which includes a nuh_layer_id syntax element.
  Contains a note to indicate possible future expansion based on highest nuh_layer_id value of 63. (HEVC allocated 6 bits to nuh_layer_id.)
HEVC version 1 required nuh_layer_id to be equal to 0
INBLD process specified in Annex F to allow decoding of independent layers with non-zero values of nuh_layer_id

## Slide 4: Proposal: Include bitstream and decoder support for multiple independent layers in VVC first version
An independent layer is considered to be an independently decodable and fully conformant sub-bitstream, similar to an HEVC CLVS for either a base layer or an independent non-base layer
Non-zero values of nuh_layer_id would be supported, either as the only layer in a bitstream or if multiple layers are contained within the same bitstream.
Sub-bitstream extraction process updated to extract single layer for target nuh_layer_id value, LIdTarget

## Slide 5: Proposal: 7-bit nuh_layer_id syntax element in the two-byte NAL Unit header
VVC NUH has 7 reserved bits, use them for nuh_layer_id
Allows up to 126 layers
Reserve nuh_layer_id value 127 to allow expansion of nuh_layer_id length
nal_unit_header( ) { | Descriptor
forbidden_zero_bit | f(1)
nal_unit_type | u(5)
nuh_temporal_id_plus1 | u(3)
nuh_reserved_zero_7bits | u(7)
nuh_layer_id | u(7)
} | 

## Slide 6: Proposal: Video Parameter Set (VPS)
Proposed VPS is similar to but simpler than HEVC’s VPS extension
VPS could be combined with the Decoding Parameter Set proposed in JVET-M0101 and recommended by the HLS BoG
Include a syntax element to indicate the maximum number of layers in the bitstream
Include a flag to indicate whether all layers are independent
  In the initial version of this specification, this flag will be required to be set, as inter-layer predictive coding is not yet supported, using “reserved” name
The –v2 version of document includes vps_included_layer_id[ i ] for i in 0 .. vps_max_layers_minus1

## Slide 7
video_parameter_set_rbsp( ) { | Descriptor
vps_ parameter_set_id | u(4)
vps_max_layers_minus1 | u(8)
for( i = 0; i < vps_max_layers_minus1; i++ ) { | 
vps_included_layer_id[ i ] | u(7)
vps_reserved_zero_1bit | u(1)
general_constraint_info( ) | 
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 

## Slide 8: Proposal: general_constraint_info( ) in VPS
VVC Draft 4 contains tool constraint flags and syntax elements in the general_constraint_info( ) syntax structure, which is part of the profile_tier_level( ) syntax structure.
Include the general_constraint_info( ) syntax structure once in the VPS, to be applied to all layers in the bitstream
  Remove general_constraint_info( ) from the profile_tier_level( ) syntax structure, which is sent for each independent layer
Noted that JVET-N0276 separately proposes the inclusion of a sub_profile_idc syntax element in the profile_tier_level( ) syntax structure, which would be sent for each independent layer

## Slide 9: Sub-bitstream extraction process update
Inputs to this process are a bitstream and a target highest TemporalId value tIdTarget and a target nuh_layer_id value LIdTarget.
Output of this process is a sub-bitstream.
It is a requirement of bitstream conformance for the input bitstream that any output sub-bitstream that is the output of the process specified in this clause with the bitstream, tIdTarget equal to any value in the range of 0 to 6, inclusive, and LIdTarget equal to any value in the range of 0 to 126, inclusive, and that satisfies the following condition shall be a conforming bitstream:
– The output sub-bitstream contains at least one VCL NAL unit with TemporalId equal to tIdTarget and nuh_layer_id equal to LIdTarget..
NOTE – A conforming bitstream contains one or more coded tile group NAL units with TemporalId equal to 0.
The output sub-bitstream is derived as follows:
– Remove all NAL units with TemporalId greater than tIdTarget.
– Remove all NAL units with nuh_layer_id not equal to LIdTarget.

## Slide 10: What is missing from this design?
The decoding process to be updated to be repeatedly invoked for each layer with nuh_layer_id equal to vps_included_layer_id[ i ] for i in 0 .. max_num_layers_minus1
  When the decoder is decoding a single layer, the NAL units in layers other than the target layer can be ignored
HRD CPB and DPB operation will require further study
  How to treat the bitrate of the non-target layer NAL units?

## Slide 11: Conclusion
Support for multiple independent (simulcast) layers can be added to the first version of VVC with very little modification to the specification or decoder complexity impact
Some of the issues raised in M46578 are addressed
  Contribution does not provide means to signal a profile_tier_level conformance point for the total combined layers or other combinations of the layers
Alternate term other than “layer” can be used if the term is seen as too related to scalability, which is not supported