## Slide 1: CE4-related: Simplified coding of the BPWA index
JVET-N0286
March. 2019
F. Le Léannec, Y. Chen, T. Poirier, A. Robert

## Slide 2: JVET-N0286
  VTM-4.0
    The Gbi index signals the weight value in set
      {-2/8,3/8,4/8,5/8,10/8} for low-delay pictures
      {3/8, 4/8, 5/8} for non-low-delay pictures
    TR binarized bin string with cMax=4 or 2 and cRiceParam=0
    Each bin is context-based coded
Table 9‑15 – Assignment of ctxInc to syntax elements with context coded bins

## Slide 3: JVET-N0286
  Proposal
    Code first bin in context-based mode as in VTM-4.0
    Code other bins in bypass mode => as for merge_idx
Table 9‑15 – Assignment of ctxInc to syntax elements with context coded bins

## Slide 4: JVET-N0286
  Results
    RA: 0.00%
    LDB: 0.00%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.03% | 0.01% | 103% | 102%
Class A2 | -0.01% | -0.02% | 0.06% | 102% | 103%
Class B | 0.01% | -0.02% | 0.02% | 100% | 99%
Class C | 0.00% | -0.05% | 0.00% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.03% | 0.02% | 101% | 101%
Class D | 0.01% | -0.04% | -0.06% | 99% | 101%
Class F (optional) | 0.00% | -0.02% | -0.02% | 101% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.14% | 0.05% | 106% | 89%
Class C | -0.03% | 0.23% | 0.05% | 102% | 95%
Class E | 0.01% | 0.30% | -0.33% | 102% | 99%
Overall | 0.00% | 0.09% | -0.05% | 103% | 93%
Class D | 0.00% | 0.11% | -0.31% | 102% | 97%
Class F (optional) | -0.03% | 0.07% | 0.14% | 101% | 93%

## Slide 5: JVET-N0286
  Conclusion
    Propose to signal GBi index with 1 context-based bin and 1-to-3 bypass bins
    3 less bins coded in context-based mode compared to VTM-4.0
    No impact on coding efficiency
    Suggestion: Adopt in VTM-5