## Slide 1: JVET-N0291 CE9: Results of DMVR related Tests CE9-1.2
S. Sethuraman
Ittiam Systems

## Slide 2: CE9-1.2
First proposed in JVET-L0174
Proposes to use bit-depth of 8 at the output of bilinear interpolation independent of input bit-depth
  Reduces the internal buffer needs (from the current fixed 10-bit depth to 8-bits)
All SAD cost computations will happen with 8-bit depth
  Accumulators require 2 less bits
  Gate-count can be reduced
  Better SIMD support on most instruction set for 8-bit SAD

## Slide 3: Results of CE9-1.2
No impact on BD-RATE (actually, a small gain)
SAD computed at 8-bits is scaled by 4 before comparing with the early exit threshold
EncT/DecT can be reduced further if 8-bit SIMD intrinsics are applied for SAD computations
Cross-checker EncT/DecT show 100%; 101% shown in the above table could be due to computational load being low on the cluster at the time of reference generation
Checked also with input bit depth of 8-bits and BDRATE impact was negligible

## Slide 4: Proposed draft text

## Slide 5: Supplemental result
Intermediate output in the 2-D separable interpolation case is also made 8-bits in this experiment.
  Reduces the horizontal interpolation output line buffers from 10-bits to 8-bits
Again, no BD-RATE impact

## Slide 6: Proposed draft text

## Slide 7: Conclusions
This CE experiment proposes to make the bilinear interpolation output for refinement maintained at 8-bits instead of the current 10-bits
  Reduces the internal memory needs
  Reduces the hardware gate-count
  Has better support on most SIMD instruction sets
No BD-RATE impact with the proposed change; in fact, a small gain is seen implying that the LSBs tend to be noisy and hence do not add much value while assessing match between L0 and L1.
Supplementary results presented for a method that restricts intermediate horizontal interpolation output also to 8-bits.
It is requested that CE9-1.2 simplification be considered for adoption into VTM

## Slide 8: Thanks to Sharp & Qualcomm for Cross-checking!