## Slide 1: JVET-N0296 CE9-related: DMVR costs based early termination for BDOF in CE9-2.6
S. Sethuraman
Ittiam Systems

## Slide 2: Proposed Method
In CE9-2.6, BDOF is applied using the same partitioning approach as DMVR
  If cu_width > max_sb_width, sbWidth = max_sb_width, else sbWidth = cu_width
  If cu_height > max_sb_height, sbHeight = max_sb_height, else sbHeight = cu_height
It also disables all early termination checks for BDOF
  Average decoding time increases by 5%
Proposed method when CU applies both DMVR and BDOF
  Use costs computed for DMVR using bilinear interpolated samples to perform early termination for BDOF
    Case when the delta MV falls on the boundary of the refinement range
      Use the evaluated SAD cost corresponding to this search point
    Case when parametric error surface based refined MV is obtained
      Compute a derived cost using the same parameteric error surface using the following:
        Where E(x,y) are the evaluated integer delta MV SAD costs, (x0, y0) corresponds to the sub-pixel delta MV obtained using error surface

## Slide 3: Benefits
No need for a dedicated SAD computation unit for BDOF
Non-DMVR BDOF cases do not perform early termination check
BDOF can be clock-gated in hardware based on DMVR cost
  Average power reduction
Software implementations get almost the same savings as with earlier two-level early exit check

## Slide 4: Results
Very little BD-RATE impact
4% reduction in average decoding time
So, performance is nearly on par with earlier DCTIF predited samples based early exit check

## Slide 5: Conclusions
There are other similar proposals at this meeting
  Key difference is that the error surface based cost estimate is used in this experiment
  Results are reported on top of CE9-2.6 which harmonizes DMVR and BDOF application block sizes
Results indicate that there is negligible BD-RATE impact with a good average decoding time reduction (on par with earlier 2-level early termination check)
Allows saving average power as decision is known ahead of time in hardware
It is requested that this method be further studied in CE

## Slide 6: Thanks to Panasonic for Cross-checking!