## Slide 1: JVET-N0299: On Luma Dependent Chroma Residual Scaling of In-loop Reshaper
Jie Zhao, Seung Hwan Kim
LG ELECTRONICS

## Slide 2: Introduction
In the reshaper tool of VTM4.0, Chroma residual scale factor is calculated from the average of luma block in reshaped domain.
This proposal proposes two methods to simplify the process to obtain the Chroma residual scale factor index.
.

## Slide 3: Background
Existing approach in VTM4 to obtain the Chroma scale factor:
Calculate average luma value of a block in reshaped domain. avgY'
  If intra mode, compute average of luma values
  If inter mode, perform forward reshaping of the block, then compute average of forward reshaped inter predicted luma values -- avgY'
Find index (idxS) where the average luma value belongs to in the inverse PWL mapping. This requires an iterative operation ( a for loop).
for( idxS = 0, idxFound = 0; idxS <= MaxBinIdx; idxS++ ) { if( (S < ReshapePivot[ idxS + 1 ] ) { idxFound = 1 break } }
Find scale factor from the index S = cScaleInv[idxS]

## Slide 4: Proposed method 1
Currently in VTM4 | Proposed Method 1
Find avgY’ in reshaped domain If intra mode, compute average of intra predicted luma values If inter mode, perform forward reshaping of the block, then compute average of forward reshaped inter predicted luma values -- avgY' Find index idxS where avgY'_TU belongs to inverse mapping PWL. This is done by a for loop, S = cScaleInv[idxS] | Find avgY’ in reshaped domain If intra mode, compute average of intra predicted luma values If inter mode, perform averaging of the luma block, then map the one average luma value to reshaped domain. Find index idxS where avgY'_TU belongs to inverse mapping PWL. This is done by a for loop, S = cScaleInv[idxS].
Switch the order of averaging and mapping. In this way, only need to do the mapping on one luma value instead of on a block.

## Slide 5: Proposed Method 2
Propose to use luma value in original domain to obtain the Chroma scale factor.
Reason: in original domain, the pixel value are linearly distributed, and the number of pieces are power of 2, so which piece a luma value belongs to can be easily found by a shift.
In contrary, in reshaped domain, the pixel values are not linearly distributed, therefore to find the piece index, it has to go through a for loop.
Finding index in original domain or reshaped domain are actually equivalent. Except some cases near pivot points, the indices found are the same.

## Slide 6: Proposed method 2
Currently in VTM4 | Proposed Method 2
Find avgY’ in reshaped domain If intra mode, compute average of intra predicted luma values If inter mode, perform forward reshaping of the block, then compute average of forward reshaped inter predicted luma values -- avgY' Find index idxS where avgY'_TU belongs to inverse mapping PWL. This is done by a for loop, for( idxS = 0, idxFound = 0; idxS <= MaxBinIdx; idxS++ ) { if( (S < ReshapePivot[ idxS + 1 ] ){ idxFound = 1 break } } S = cScaleInv[idxS] | Find avgY in original domain If intra mode, compute average of intra predicted luma values, and map the one average luma value to original domain; If inter mode, compute average of inter predicted luma values --- avgY. The index idxS where avgY_TU belongs to can be easily found by idxS = avgY >> nShift, S = cScaleInv[idxS] Note: nShift equals to log2 of the reshaper piece length. This is already known. For 10bit input and 16 pieces PWL mapping, nShift equals to 6 .

## Slide 7: Proposed method 2
There is at most one extra mapping operation which can be done by a LUT, while it eliminates the iterative for loop during piece index identification.
Otherwise, if use luma value in reshaped domain, the for loop can not be avoided.
Map to original domain if not
Get piece index with a simple shift
One luma value
Map to reshaped domain if not
Get piece index with a for loop
One luma value
Piece index
Piece index
VTM
Proposed

## Slide 8: Result
There is no loss by this simplification.
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.11% | -0.03% | 100% | 99% |  |  |  |  | 
Class A2 | 0.00% | -0.07% | -0.02% | 100% | 99% |  |  |  |  | 
Class B | 0.01% | -0.01% | 0.03% | 100% | 99% | -0.01% | 0.03% | 0.14% | 100% | 99%
Class C | 0.00% | -0.02% | 0.00% | 100% | 101% | -0.03% | 0.29% | 0.15% | 100% | 100%
Class E |  |  |  |  |  | -0.01% | 0.12% | -0.38% | 100% | 100%
Overall | 0.00% | -0.04% | 0.00% | 100% | 100% | -0.02% | 0.14% | 0.01% | 100% | 100%
Class D | 0.00% | -0.03% | -0.05% | 100% | 100% | -0.02% | 0.26% | -0.28% | 101% | 102%
Class F | -0.02% | -0.01% | -0.01% | 99% | 100% | -0.05% | -0.15% | -0.09% | 100% | 102%
Result of Proposed method 1 vs VTM4

## Slide 9: Result
Result of Proposed method 2 vs VTM4
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.08% | -0.01% | 100% | 100% |  |  |  |  | 
Class A2 | 0.00% | -0.07% | -0.02% | 100% | 99% |  |  |  |  | 
Class B | 0.01% | -0.01% | 0.03% | 100% | 100% | -0.01% | 0.03% | 0.14% | 100% | 100%
Class C | 0.00% | -0.02% | 0.00% | 101% | 102% | -0.03% | 0.29% | 0.15% | 100% | 100%
Class E |  |  |  |  |  | -0.01% | 0.12% | -0.38% | 100% | 100%
Overall | 0.00% | -0.04% | 0.00% | 100% | 101% | -0.02% | 0.14% | 0.01% | 100% | 100%
Class D | 0.00% | -0.03% | -0.05% | 101% | 102% | -0.02% | 0.26% | -0.28% | 101% | 102%
Class F | -0.02% | -0.01% | -0.01% | 101% | 102% | -0.05% | -0.15% | -0.09% | 100% | 102%
As expected, method 1 and method 2 result are almost the same ( many sequences are identical), while method 2 is simpler.

## Slide 10: Conclusion
Proposed 2 methods to simply the process to calculate Chroma residual scaling factor.
Method 1 still calculates the luma average in reshaped domain, but reduces the number of mapping operations by switching the order of averaging and mapping.
Method 2, obtain luma average in original domain, it replaces the for loop to find idxS with a simple shift.
Both method have near identical results, there are no loss.
Propose to adopt method 2 into VVC.
Thanks Tencent for Cross-checking