## Slide 1: CE10: CIIP with position-independent weights (CE10-1.1)
L. Pham Van, G. Van der Auwera,
A. K. Ramasubramonian, Vadim Seregin, M. Karczewicz
@qualcomm
03/2019
AV

## Slide 2: Proposed simplification of inter-intra prediction
Simplification:
Only intra planar
Blending weights are determined by number of intra coded neighboring
If top and left are intra-coded:
 (wIntra, wInter) = (3, 1)
If top or left is intra-coded:
 (wIntra, wInter) = (2, 2)
Else:  (wIntra, wInter) = (1, 3)

## Slide 3: Experimental results
Thank Huawei for cross-checking!
Luma BD-rate gain: 0.05% and 0.03% for RA and LDB, resp.
(EncT, DecT): (98%, 100%) for for RA and LDB.
 | RA |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | 0.06% | -0.08% | 100% | 101%
Class A2 | 0.00% | -0.04% | 0.06% | 99% | 100%
Class B | -0.06% | -0.05% | 0.06% | 98% | 100%
Class C | -0.02% | -0.05% | 0.00% | 99% | 100%
Class E |  |  |  |  | 
Overall | -0.05% | -0.02% | 0.02% | 98% | 100%
Class D | 0.02% | -0.07% | -0.08% | 98% | 100%
Class F (optional) | -0.11% | -0.09% | -0.06% | 99% | 100%
LDB |  |  |  | 
Over VTM-4.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.03% | -0.07% | 0.04% | 98% | 100%
0.03% | 0.67% | 0.24% | 98% | 100%
-0.11% | 0.00% | -0.10% | 98% | 100%
-0.03% | 0.20% | 0.07% | 98% | 100%
0.03% | 0.80% | 0.19% | 97% | 98%
-0.45% | -0.27% | -0.55% | 99% | 103%

## Slide 4: Conclusions
Simplification of inter-intra prediction.
Adaptive weights for intra and inter samples
Luma BD-rate gain: 0.05%, 0.03% for RA and LDB, resp.
Reduced encoding time without a decoding time increase: (98%, 100%)
It is recommended to adopt the proposed simplification to VVC.