## Slide 1: CE3-related: Simplified unified luma intra mode coding
Saverio Blasi, André Seixas Dias, Gosala Kulupana
14thJVET Meeting: Geneva, CH, 19–27 Mar. 2019
JVET-N0303

## Slide 2
Problem statement
JVET-M0528 proposes to signal non-angular modes separately
If non-angular, no need to compute MPM list
If angular:
  MPM list construction (only angular modes)
  intra_luma_mpm_flag to signal if mode is in MPM
  If mode is not in MPM, encode intra remainder idx
non-angular
non-angular
MPM list
default ang. mode 0
default ang. mode 1
default ang. mode 2
…
However, when no angular modes are available from neighbours (which can happen very frequently) the MPM list is populated using default values, which may not be ideal

## Slide 3
Proposed method 1
Check intra_luma_angular_mode_flag of neighbours (this comes for free)
If no angular mode is available, skip MPM computation and encode intra mode idx using truncated binary codes (as for intra luma remainder)
  intra_luma_mpm_flag is inferred to be 0
  No MPM list computation needed in these cases
  Total of 65 possible intra modes (all possible angular modes) encoded with truncated binary, which requires 6 bits (modes 2 – 65) or 7 bits (modes 66 – 67)
  For most modes, this is the same number of bits required in JVET-M0528, but no need to encode intra_luma_mpm_flag and no need to compute MPM list
  Number of bits needed to encode intra angular modes more uniform

## Slide 4
Proposed method 2
If angular mode is not in the MPM list, parsing still depends on the computation of the MPM list
It is proposed to avoid this. All angular modes are allowed to be coded with intra_luma_mpm_remainder
  Max value of intra_luma_mpm_remainder increases from 59 to 65
  Some small efficiency losses but no need to compute MPM list if mode is not in the MPM list (and no need for sorting)
  Higher flexibility at the encoder side: implementations could be done which completely avoid computing MPM lists

## Slide 5
Performance results
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.46% | -0.34% | -0.31% | 100% | 98%
Class A2 | -0.14% | 0.00% | -0.11% | 101% | 97%
Class B | -0.20% | -0.15% | -0.09% | 101% | 99%
Class C | -0.06% | -0.03% | -0.03% | 100% | 99%
Class E | -0.10% | -0.13% | -0.03% | 102% | 98%
Overall | -0.19% | -0.12% | -0.11% | 101% | 98%
Class D | -0.03% | -0.05% | -0.21% | 100% | 96%
Class F | 0.12% | 0.05% | 0.04% | 100% | 99%
 |  |  | Random access |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.10% | -0.12% | 100% | 99%
Class A2 | -0.06% | -0.03% | 0.03% | 100% | 99%
Class B | -0.09% | -0.08% | -0.04% | 100% | 99%
Class C | -0.02% | 0.12% | 0.02% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.08% | -0.02% | -0.03% | 100% | 99%
Class D | 0.00% | -0.32% | -0.29% | 101% | 97%
Class F | 0.07% | -0.01% | -0.05% | 102% | 102%
Proposed method 1

## Slide 6
Performance results
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.44% | -0.35% | -0.35% | 100% | 99%
Class A2 | -0.12% | 0.01% | -0.08% | 102% | 99%
Class B | -0.17% | -0.11% | -0.09% | 101% | 97%
Class C | 0.00% | -0.13% | -0.06% | 100% | 98%
Class E | -0.06% | 0.03% | -0.02% | 101% | 98%
Overall | -0.15% | -0.11% | -0.11% | 101% | 98%
Class D | 0.02% | -0.05% | -0.13% | 100% | 96%
Class F | 0.15% | 0.14% | 0.05% | 100% | 99%
 |  |  | Random access |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C |  |  |  |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D |  |  |  |  | 
Class F |  |  |  |  | 
Proposed method 1 + proposed method 2

## Slide 7
Performance results
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.03% | -0.05% | 103% | 98%
Class A2 | -0.06% | -0.02% | -0.03% | 102% | 97%
Class B | -0.09% | -0.04% | -0.07% | 103% | 100%
Class C | -0.06% | 0.05% | 0.01% | 102% | 100%
Class E | -0.06% | -0.23% | 0.08% | 103% | 100%
Overall | -0.08% | -0.05% | -0.02% | 103% | 100%
Class D | -0.06% | -0.01% | -0.06% | 100% | 100%
Class F | 0.04% | 0.07% | 0.04% | 112% | 95%
Proposed method 1 + proposed method 2
vs. baseline
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11% | -0.04% | -0.09% | 103% | 99%
Class A2 | -0.04% | -0.02% | 0.00% | 103% | 99%
Class B | -0.06% | 0.00% | -0.07% | 102% | 99%
Class C | 0.00% | -0.05% | -0.02% | 102% | 100%
Class E | -0.02% | -0.07% | 0.09% | 103% | 100%
Overall | -0.04% | -0.03% | -0.02% | 102% | 99%
Class D | 0.00% | -0.01% | 0.03% | 100% | 100%
Class F | 0.08% | 0.15% | 0.04% | 112% | 100%
Proposed method 1 vs. baseline

## Slide 8
Conclusion
When restricting MPMs to contain only angular modes, there are cases where default values need to be used
Proposed method 1: avoid usage of this list and only compute MPM list when at least one angular mode is available
Proposed method 2: remove dependency of parsing of modes not in the MPM list from the MPM computation
Decoder complexity is reduced + more encoder flexibility.
Proposed method 1 + 2: -0.15% luma BD-rate gains and -0.44% gains on Class A1

## Slide 9: Thank you
www.bbc.co.uk/rd
saverio.blasi@bbc.co.uk
Email: