## Slide 1: CE3-related: Luma intra mode coding with restricted MPM derivation
Saverio Blasi, André Seixas Dias, Gosala Kulupana
14th JVET Meeting: Geneva, CH, 19–27 Mar. 2019
JVET-N0305

## Slide 2
Proposed method
If angular mode is not in the MPM list, parsing still depends on the computation of the MPM list
It is proposed to avoid this. All angular modes are allowed to be coded with intra_luma_mpm_remainder
  Max value of intra_luma_mpm_remainder increases from 61to 67 (all modes)
  No need to compute MPM list if mode is not in the MPM list (and no need for sorting)
  Higher flexibility at the encoder side: implementations could be done which completely avoid computing MPM lists
We show that encoder side optimisations can “use” the reduced complexity to compensate for the produced efficiency losses

## Slide 3
Performance results
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | 0.07% | 0.03% | 96% | 93%
Class A2 | 0.04% | 0.11% | 0.04% | 98% | 92%
Class B | 0.05% | 0.02% | 0.05% | 98% | 95%
Class C | 0.09% | 0.04% | 0.02% | 99% | 97%
Class E | 0.08% | 0.08% | -0.03% | 99% | 96%
Overall | 0.06% | 0.06% | 0.02% | 98% | 95%
Class D | 0.10% | -0.03% | -0.20% | 99% | 94%
Class F | 0.09% | 0.04% | 0.12% | 98% | 97%
 |  |  | Random access |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.01% | 0.07% | 100% | 97%
Class A2 | 0.00% | -0.03% | 0.01% | 100% | 98%
Class B | 0.03% | 0.07% | 0.00% | 100% | 99%
Class C | 0.07% | -0.06% | -0.22% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.03% | 0.00% | -0.04% | 100% | 99%
Class D | 0.04% | -0.33% | -0.35% | 100% | 96%
Class F | 0.03% | 0.02% | -0.01% | 100% | 100%
No intra search modifications

## Slide 4
Performance results
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.04% | -0.03% | 97% | 91%
Class A2 | -0.05% | 0.08% | -0.01% | 97% | 90%
Class B | -0.05% | -0.03% | 0.03% | 100% | 93%
Class C | 0.01% | -0.05% | 0.02% | 102% | 97%
Class E | -0.05% | 0.05% | 0.02% | 102% | 96%
Overall | -0.04% | 0.00% | 0.01% | 100% | 94%
Class D | 0.07% | 0.05% | -0.15% | 102% | 95%
Class F | 0.10% | -0.09% | 0.03% | 102% | 98%
With intra search modifications

## Slide 5
Conclusion
It is proposed to remove dependency on parsing modes that are not in the MPM list from the computation of the MPM list
Decoder complexity is reduced + more encoder flexibility.
Marginal compression efficiency losses when no intra search modifications are employed: 0.06% luma BD-rate losses in AI, 0.03% BD-rate losses in RA, with encoder and decoder complexity savings
It is shown that the reduced complexity at the encoder can be used to perform additional RD searches which compensate the losses

## Slide 6: Thank you
www.bbc.co.uk/rd
saverio.blasi@bbc.co.uk
Email: