## Slide 1: JVET-N0314 CE9-related: Results for use of DMVR refined MVs from top and top-left CTUs for spatial MV prediction and CU boundary de-blocking
S. Sethuraman
Ittiam Systems

## Slide 2: Test-1: Using refined MVs of top and top-left CTUs
JVET-K0041 first proposed the use of refined MVs in neighbor CUs in top and top-left CTUs for spatial MV prediction and as refinement centers for CUs in a current CTU
  Studied in CE at the L and M meetings
  Not adopted at the M meeting due to existing designs performing MV reconstruction and de-blocking boundary strength computation in pipeline stages that do not depend on any pixel processing stages
    Using refined MVs would require MV reconstruction for reference sample pre-fetch and deblocking BS calculation to depend on the DMVR results of top-row CTUs
Purpose of Test-1 is to show the BD-RATE gain in VTM4.0 with use of refined MVs that do not affect any CTU-level pipeline design
Advantages of using refined MVs would be that delta MVs need not be maintained until MV reconstruction and de-blocking BS calculations have been computed using unrefined MVs
  Top CTU line buffer needs to only maintain one unrefined MV per CTU
  Refined MVs can be used at 4x4 granularity (replacing the need to maintain unrefined MVs and delta-MV at 4x4 granularity)

## Slide 3: Results for Test-1
Average luma BD-RATE gain of 0.11% with similar gains in chroma
Small increase in decoding time due to higher % of pixels using DMVR
Avoids need to store 6-bits of delta-MV for updating co-located MVs for use in temporal MV prediction

## Slide 4: Test-2: Using refined MVs to compute BS for CU edges
Current design uses unrefined MVs to compute de-blocking boundary strength across CU boundary edges
Using refined MV at a sub-block level at CU boundaries can improve visual quality without increasing the BS computation overheads
  Sub-block edges that do not align with CU (or SBT) boundary are not de-blocked

## Slide 5: Results for Test-2
Additional gain of 0.01% over Test-1
Potential subjective quality improvements
No additional increase in decoding time over Test-1

## Slide 6: Conclusions
Test-1 shows that 0.11% BDRATE gains are possible in VTM4.0 when using refined MVs from top and top-left CTUs for spatial MV prediction and as centers of refinement for CUs in current row
  Offers the benefit of not having to maintain delta-MVs from refinement till MV bank can be updated
  No dependency issues are present in a CTU-level pipeline and CTU-level pre-fetch is not impacted
Test-2 shows that an additional 0.01% BDRATE gain is possible when refined MVs are used for computing de-blocking boundary strength on CU boundaries
  Again, allows immediate update of refined MVs instead of waiting till BS computations are over
Further discussion on hardware design impact for accommodating these two aspects is requested

## Slide 7: Thanks to Panasonic for Cross-checking!