## Slide 1: CE8-related: Default Processing for IBC Mode
Yu Han, Wei-Jung Chien, Marta Karczewicz

## Slide 2: Abstract
There are 3 encoder constraints in the current design of IBC mode as below:
  The IBC merge list may not be fully filled. Therefore, encoder can only signal merge index which does not exceed the valid size of IBC merge list.
  The encoder can only signal valid block vector whether it is skip/merge mode or AMVP mode.
  The encoder can only signal chroma IBC mode when collocated luma blocks are all coded with IBC mode and the block vectors are all valid.
These encoder constraints are heavily relied on the quality of the encoder.
This contribution presents a default processing method for IBC mode in order to prevent un-defined decoder behavior.

## Slide 3: Technical description
In this method, if a block vector is not valid, a default processing method for IBC mode is designed which uses a default value of 1 << (internalBitDepth - 1) as the prediction samples.
For the constraint of invalid IBC merge index, in this method, the size of IBC merge list is set to be fixed to maximum merge candidate number, which is 6 for VTM4.0 CTC. If the available IBC merge candidates less than 6, fill the merge list with zero block vectors.
In VTM4.0, chroma IBC mode is sub-block based, each 2x2 chroma block inherits block vector from its collocated luma block. In test 3, the whole chroma CU uses one block vector which is inherited from the collocated luma block using the center position of the chroma CU.

## Slide 4: Simulation results
Thanks Sharp for crosschecking
Test 1: Apply default processing method to IBC merge/skip mode
  In this test, if the number of IBC merge candidates less than 6, add zero block vector candidates, and zero block vector candidates won’t be check in the encoder side.
  If a block vector is not valid, the default value, 1 << (internalBitDepth - 1), is used to fill the prediction values.
 | All Intra Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.02% | 0.01% | -0.07% | 99% | 95%
Class SCC 1080p | 0.00% | -0.04% | -0.04% | 81% | 94%
 | Random Access Main 10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.04% | -0.05% | -0.13% | 97% | 96%
Class SCC 1080p | -0.03% | 0.03% | 0.01% | 78% | 80%
 | Low delay B Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.20% | -0.60% | 0.13% | 96% | 94%
Class SCC 1080p | -0.04% | -0.10% | -0.11% | 78% | 78%

## Slide 5: Simulation results
Test 2: Test 1 + Apply default processing method to IBC chroma mode
  Based on test 1, in this test, for IBC chroma mode, if the inherited block vector of the chroma sub-block is invalid, use the default value 1 << (internalBitDepth - 1) as prediction.
 | All Intra Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.02% | -0.01% | -0.11% | 99% | 96%
Class SCC 1080p | -0.02% | -0.04% | -0.05% | 81% | 94%
 | Random Access Main 10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.04% | -0.08% | -0.14% | 96% | 95%
Class SCC 1080p | -0.04% | 0.00% | -0.01% | 78% | 79%
 | Low delay B Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.19% | -0.69% | 0.53% | 82% | 93%
Class SCC 1080p | 0.06% | 0.14% | 0.12% | 82% | 92%

## Slide 6: Simulation results
Test 3: Test 1 + Apply default processing method to CU based IBC chroma mode
  Based on test 1, in this test, for IBC chroma mode, the whole chroma CU use one block vector which is inherited from the collocated luma block using the center position of the chroma CU.
 | All Intra Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.05% | -0.11% | -0.21% | 82% | 91%
Class SCC 1080p | -0.18% | -0.21% | -0.31% | 85% | 91%
 | Random Access Main 10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.08% | -0.20% | -0.21% | 82% | 95%
Class SCC 1080p | 0.02% | -0.02% | -0.07% | 82% | 93%
 | Low delay B Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.18% | 0.03% | 0.46% | 81% | 92%
Class SCC 1080p | 0.04% | -0.02% | -0.07% | 82% | 90%