## Slide 1: CE8-related: Simplification on IBC Merge/Skip Mode
Yu Han, Wei-Jung Chien, Marta Karczewicz

## Slide 2: Abstract
In the VTM4.0:
  IBC merge/skip mode and inter merge/skip mode use two independent merge lists. In the worst case, two merge list may still be generated for 4x4 CUs in a shared listed region.
  Since these two merge lists can be generated parallelly, the cycle budget for a shared list region can still be meet. However, it is still desired to have a simplified merge list generation scheme to reduce the area size for hardware implementation and reduce cycles for software implementation.
In this contribution:
  A simplification method for IBC merge/skip mode by reducing the number of potential IBC merge candidates is presented.
  The simulation results show 0.02% loss in AI case, 0.00% loss in RA case and 0.00% loss in LB case in screen content coding materials.

## Slide 3: Technical description
IBC merge list in VTM4.0:
  Spatial candidates for blocks A1, B1, B0 and A0 (3 pruning required).
  If number of candidates less than 4, add B2 (2 pruning required).
  5 HMVP candidates (4 pruning required).
  Pairwise candidate.
Modification on merge list:
  Spatial candidates for blocks A1, B1 (1 pruning required)
  5 HMVP candidates (4 pruning required).
  Shared IBC merge list:
  32 and below pixels region shares the same IBC merge list. The IBC HMVP table is reset at the beginning of each CTU line.
  The tickets number of these two changes are ticket 193 and ticket 211.

## Slide 4: Simulation results
Thanks Technicolor for crosschecking.
Test 1: IBC merge list simplification
 | All Intra Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.03% | 0.09% | 0.03% | 99% | 99%
Class SCC 1080p | 0.02% | 0.01% | 0.00% | 99% | 100%
 | Random Access Main 10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.02% | -0.12% | -0.09% | 100% | 99%
Class SCC 1080p | 0.00% | 0.00% | -0.07% | 100% | 99%
 | Low delay B Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.11% | -0.46% | -0.14% | 100% | 97%
Class SCC 1080p | 0.00% | 0.01% | 0.01% | 100% | 100%

## Slide 5: Simulation results
Test 2: Use shared IBC merge list and reset IBC HMVP table at the beginning of each CTU line (Fix for ticket 193 and ticket 211)
 | All Intra Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.06% | -0.01% | -0.15% | 99% | 100%
Class SCC 1080p | 0.06% | 0.01% | 0.01% | 82% | 99%
 | Random Access Main 10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.01% | 0.02% | -0.17% | 100% | 100%
Class SCC 1080p | -0.03% | 0.04% | 0.00% | 81% | 84%
Test 3: Test 1 + Test 2
 | Low delay B Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.11% | -0.10% | -1.10% | 100% | 101%
Class SCC 1080p | 0.04% | 0.17% | 0.08% | 82% | 86%
 | All Intra Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.08% | 0.06% | -0.09% | 98% | 101%
Class SCC 1080p | 0.08% | 0.05% | 0.03% | 81% | 99%
 | Random Access Main 10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | -0.02% | 99% | 100%
Class SCC 1080p | 0.00% | 0.14% | 0.09% | 81% | 84%
 | Low delay B Main10 - VTM configuration |  |  |  | 
 | Over VTM-4 + IBC |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.20% | -0.30% | -0.46% | 100% | 102%
Class SCC 1080p | 0.23% | 0.17% | 0.16% | 82% | 87%