## Slide 1
JVET-N0326
Non-CE7: Simplification of cbf codin
Yi-Wen Chen, Xiaoyu Xiu, Tsung-Chuan Ma, Xianglin Wang

## Slide 2: Introduction
In current VVC, 4 contexts are used for luma cbf, 2 contexts for Cb and 2 contexts for Cr with the selection rules:
  Luma Cbf: select depending on ISP flag, cbf of previous sub-partition and transform depth
  Cb Cbf: select depending on transform depth
  Cr Cbf: select depending on cbf of Cb block
Proposed simplification
  Test 1:Use only transform depth to select the context for luma cbf coding
  Test 2:Remove the transform depth-dependent cbf coding for luma and Cb block
  Test 3:Combination of the two simplifications

## Slide 3: Test 1: Use Only Transform Depth for luma cbf Coding
*2 contexts are removed

## Slide 4
*2 contexts are removed
Test 2: Remove the TrDepth cbf coding

## Slide 5: Test 3: Combination of the Two Simplifications
*4 contexts are removed

## Slide 6: Results of Test 3
Anchor: VTM-4.0
Test : Anchor + Proposed Two Simplifications

## Slide 7: Summary
Simplifications on cbf coding are proposed to reduce the condition checking for context selection as well as the number of CABAC context models
The modifications provides {0.04%, 0.01%, 0.00} and {-0.01%, 0.63%, -0.10%} BD-rate increase for Y, Cb and Cr components under AI and RA, respectively
It is recommended to consider adoption of the proposed simplification into VVC for cbf coding.

## Slide 8: Thank you