## Slide 1
JVET-N0330
Non-CE3: Intra sub-partition coding without thin partitions
TC Ma, Xiaoyu Xiu, Yi-Wen Chen, Xianglin Wang

## Slide 2: Introduction
The implementation issue of ISP in VTM-4.0
  The dependency between sub-CU
  1xN and 2xN sub-CU
3 options for removing 1xN or 2xN sub-CU
  Option 1: removing 1xN sub-CU and skip ISP 4xN (N>8)
  Option 2: removing 1xN and 2xN sub-CU, skipping ISP 4xN and 8xN (N>=8)
  Option 3: removing 1xN and Nx1 sub-CU, skipping ISP 4xN and Nx4 (N>8)

## Slide 3: Results
 | AI | RA | LDB | EncT | DecT
Remove 1xN | 0.04%/0.05%/0.04% | 0.02%/0.05%/0.03% | 0.00%/0.19%/0.12% | 100% | 99%
Remove 1xN, 2xN | 0.14%/0.16%/0.13% | 0.07%/0.10%/-0.02% | 0.03%/0.31%/0.02% | 99% | 101%
Remove 1xN, Nx1 | 0.08%/0.11%/0.06% | 0.04%/0.06%/-0.10% | 0.01%/0.08%/0.08% | 99% | 99%

## Slide 4: Summary
Propose to skip multiple size of ISP CUs
  Reduce the latency of ISP mode for certain CUs
  Only simple logic for skipping specific size of CUs
  3 options are proposed
Thanks for MediaTek being our cross-checker

## Slide 5: Thank you