## Slide 1
JVET-N0332:Non-CE4: MVD scaling issue for LTRPs
Yi-Wen Chen, Xiaoyu Xiu, Tsung-Chuan Ma, Xianglin Wang

## Slide 2: Introduction
In current VVC, POC-based MV scaling is prohibited for long-term reference picture (LTRP) except for MMVD
In current MMVD design, the final MVDs may be derived by scaling the signaled MV offset according to the POC distances
POC-based scaling on the POC of a long term reference picture may result in extremely large or small values
Proposed to disable the motion vector difference (MVD) scaling process for MMVD when referring to a long-term reference picture

## Slide 3: Proposed Text Changes

## Slide 4: Summary
This contribution proposes to disable the motion vector difference scaling process for MMVD when a picture refers to a long-term reference
It is suggested that the JVET considers this proposal in refining the specification for MVD scaling process for MMVD.

## Slide 5: Thank you