## Slide 1
JVET-N0334
CE2/4/9-related: Overflow prevention for motion field storage
Xiaoyu Xiu, Yi-Wen Chen, Tsung-chuan Ma, Xianglin Wang

## Slide 2: Prevention of MV/CPMV overflow
At Marrakech meeting, JVET-M0145 was adopted
  Clipping the CPMVs of affine inherited merge candidates
Inter tools that can potentially go beyond 18-bit
  Affine constructed merge: deriving CPMVs based on the translational subblocks’ MVs
  MMVD: applying one signaled MV offset to one selected merge candidate
  DMVR: deriving motion refinement to L0 and L1 MVs of bi-pred merge candidate

## Slide 3: Prevention of MV/CPMV overflow
Proposal
  Clipping the derived MVs and CPMVs to the bit-depth of the motion field storage after the motion derivations of the MMVD, the DMVR and the constructed affine merge mode

## Slide 4: Mismatch on clipping the MVs/CPMVs of non-merge inter modes
In VCC working draft 4
  MVD is limited to 16-bit
  The MVs and CPMVs of non-merge modes are generated based on modulo of 18-bit
In the VTM-4.0
  Encoder constrain to ensure MVD within 16-bit
Proposal
  Align the software to the specification draft

## Slide 5: Mismatch on clipping the MVs/CPMVs of non-merge inter modes
In VCC working draft 4, for explicit regular inter
In VCC working draft 4, for explicit affine inter
4. When predFlagLX[ 0 ][ 0 ] is equal to 1, the luma motion vector mvLX[ 0 ][ 0 ] is derived as follows:
uLX[ 0 ] = ( mvpLX[ 0 ] + mvdLX[ 0 ] + 218 ) % 218 (8‑272)
mvLX[ 0 ][ 0 ][ 0 ] = ( uLX[ 0 ] >= 217 ) ? ( uLX[ 0 ] − 218 ) : uLX[ 0 ] (8‑273)
uLX[ 1 ] = ( mvpLX[ 1 ] + mvdLX[ 1 ] + 218 ) % 218 (8‑274)
mvLX[ 0 ][ 0 ][ 1 ] = ( uLX[ 1 ] >= 217 ) ? ( uLX[ 1 ] − 218 ) : uLX[ 1 ] (8‑275)
5. When predFlagLX[ 0 ][ 0 ] is equal to 1, the luma motion vectors cpMvLX[ cpIdx ] with cpIdx ranging from 0 to NumCpMv − 1, are derived as follows:
uLX[ cpIdx ][ 0 ] = ( mvpCpLX[ cpIdx ][ 0 ] + mvdCpLX[ cpIdx ][ 0 ] + 218 ) % 218 (8‑574)
cpMvLX[ cpIdx ][ 0 ] = (uLX[ cpIdx ][ 0 ] >= 217 ) ? (uLX[ cpIdx ][ 0 ] − 218 ) : uLX[ cpIdx ][ 0 ] (8‑575)
uLX[ cpIdx ][ 1 ] = ( mvpCpLX[ cpIdx ][ 1 ] + mvdCpLX[ cpIdx ][ 1 ] + 218 ) % 218 (8‑576)
cpMvLX[ cpIdx ][ 1 ] = (uLX[ cpIdx ][ 1 ] >= 217 ) ? (uLX[ cpIdx ][ 1 ] − 218 ) : uLX[ cpIdx ][ 1 ] (8‑577)

## Slide 6: Mismatch on clipping the MVs/CPMVs of non-merge inter modes

## Slide 7: Thank you