## Slide 1
JVET-N0336
CE2/4-related: On motion field storage reduction for spatial motion prediction
Xiaoyu Xiu, Yi-Wen Chen, Tsung-chuan Ma, Xianglin Wang

## Slide 2: Motivation
In the VCC, motion field is composed of MVs and CPMVs
The dynamic ranges of both MVs and CPMVs are 18-bit
Temporal MVs are stored based on 6-bit mantissa and 4-bit exponent
Storage | Local MV storage | Local CPMV storage | MV line-buffer | HMVP buffer | Total
Size | 864 bytes | 1296 bytes | 8640 bytes | 90 bytes | 10890 bytes

## Slide 3: Proposed Method #1
Proposed to store the spatial motion information using a 8-bit mantissa and 4-bit exponent
The converted motion contains 4×4 subblock MVs and the affine CPMVs stored in the local buffer and 4×4 subblock MVs in the line-buffer
33% storage reduction
Storage | Local MV storage* | Local CPMV storage* | MV line-buffer* | HMVP buffer | Total
Size | 576 bytes | 864 bytes | 5760 bytes | 90 bytes | 7290 bytes

## Slide 4: Proposed Method #1

## Slide 5: Proposed Method #2
Proposed to store 4×4 subblock MVs in line-buffer using a 7-bit mantissa and 4-bit exponent
31% storage reduction
Storage | Local MV storage | Local CPMV storage | MV line-buffer* | HMVP buffer | Total
Size | 864 bytes | 1296 bytes | 5280 bytes | 90 bytes | 7530 bytes

## Slide 6: Proposed Method #2

## Slide 7: Proposed Method #2
Proposed to store 4×4 subblock MVs in line-buffer using a 6-bit mantissa and 4-bit exponent
35% storage reduction
Storage | Local MV storage | Local CPMV storage | MV line-buffer* | HMVP buffer | Total
Size | 864 bytes | 1296 bytes | 4800 bytes | 90 bytes | 7050 bytes

## Slide 8: Proposed Method #2

## Slide 9: Thank you