## Slide 1: JVET-N0347 CE7-related: Joint coding of chroma residuals
Geert Van der Auwera, Adarsh K. Ramasubramonian, Muhammed Coban, Marta Karczewicz (Qualcomm)

## Slide 2: Joint coding of chroma residuals
Encoder:
    Cb residual: ( resCb(x,y) – resCr(x,y) ) / 2 → CRS → T → Q( sliceQp + jointCbCrQpOffset )
    Cr residual: 0
    Chroma residual scaling (CRS) after combined residual process
    Signalling of Qp offset for joint mode: pps_cb_cr_qp_offset, slice_cb_cr_qp_offset
      jointCbCrQpOffset = pps_cb_cr_qp_offset (-1) + slice_cb_cr_qp_offset (0)
    Lambda tuning:
      Inter: IF (jointCbCr) 0.6 x lambda
      Intra: IF (jointCbCr) THEN (0.6 x lambda) ELSE IF (sliceQP > 18) THEN (1.10 x lambda) ELSE (1.05 x lambda)
Decoder:
    Cb residual: invQ → invT → invCRS → resCb(x,y)’
    Cr residual: - resCb(x,y)’
Background: CE7-1

## Slide 3: Joint coding of chroma residuals
Proposal
Builds upon CE7-1
  Encoder:
    Cb residual: CRS → ( resCb(x,y) – resCr(x,y) ) / 2 → T → Q( sliceQp )
    Cr residual: CRS → ( resCb(x,y) + resCr(x,y) ) / 2 → T → Q( sliceQp )
    Similar to 1D 2-point transform
    Invertible (lossy due to rounding)
    CRS before combining residuals
    Special Qp offset tuning and signalling not required
  Decoder:
    Cb residual: invQ → invT → ( resCr(x,y)’ + resCb(x,y)’ ) → invCRS
    Cr residual: invQ → invT → ( resCr(x,y)’ - resCb(x,y)’ ) → invCRS

## Slide 4
Comparison between CE7-1 and proposed
 | Test CE7-1 | Current proposal
Cb residual encoder processing | resJointCb = (resCb – resCr) / 2 | resJointCb = (resCb – resCr) / 2
Cr residual encoder processing | 0 | resJointCr = (resCb + resCr) / 2
Cb reconstruction (recCb) | recCb = predCb + resJointCb | recCb = predCb + resJointCb + resJointCr
Cr reconstruction (recCr) | recCr = predCr – resJointCb | recCr = predCr – resJointCb + resJointCr
Processing invertible? | No | Yes (lossy due to rounding only)
Qp offsets for resJoint coding | -1 | 0
Lambda tuning | Inter: IF (jointCbCr) THEN (0.6 × lambda) Intra: IF (jointCbCr) THEN (0.6 × lambda) ELSE IF (sliceQP > 18) THEN (1.10 × lambda) ELSE (1.05 × lambda) | No (experimental results are provided with and without lambda tuning from CE7-1 for comparison)
Qp offset signalling for joint residual mode | Yes | No

## Slide 5
Comparison between CE7-1 and proposed
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
if( cIdx == 1 && tu_cbf_cb[ x0 ][ y0 ] ) {
tu_cb_cr_joint_residual[ x0 ][ y0 ]
}
…
CE7-1 joint residual flag signalling
Proposal
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
if( cIdx == 2 && tu_cbf_cb[ x0 ][ y0 ] ) {
tu_cb_cr_joint_residual[ x0 ][ y0 ]
if( tu_cb_cr_joint_residual [ x0 ][ y0 ] ) {
return
}
}
…
Both methods signal joint residual flag if tu_cbf_cb is true

## Slide 6
Comparison between CE7-1 and proposed
CE7-1
Proposed
CE7-1 method approximates chroma residuals and approximation error is not coded. Therefore, accidental use of the mode results in chroma artifacts.
Test: force use of joint residual mode (QP22; I frame)

## Slide 7
Comparison between CE7-1 and proposed
Test results
 |  | Y | U | V | EncT | DecT
Proposed method without CE7-1 lambda tuning | AI | -0.29% | 0.20% | -0.01% | 104% | 102%
 | RA | -0.21% | 0.15% | 0.39% | 102% | 100%
 | LDB | -0.14% | 1.10% | -0.14% | 102% | 102%
CE7-1 results without CE7-1 Qp/lambda tuning | AI | -0.30% | 0.16% | -1.02% |  | 
 | RA |  |  |  |  | 
 | LDB | -0.11% | -0.92% | -2.07% |  | 
Proposed method with CE7-1 lambda tuning | AI | -0.46% | 0.69% | 0.44% |  | 
 | RA | -0.33% | 0.48% | 0.67% |  | 
 | LDB | -0.16% | 0.44% | -1.18% |  | 
CE7-1 results with CE7-1 Qp/lambda tuning | AI | -0.38% | -0.49% | -1.52% | 103% | 100%
 | RA | -0.26% | -0.81% | -0.92% | 101% | 100%
 | LDB | -0.07% | -2.99% | -4.76% | 100% | 100%
 |  | Y | U | V | EncT | DecT
Proposed method without CE7-1 lambda tuning | AI | -0.11% | 0.14% | 0.07% |  | 
 | RA | -0.11% | 0.27% | 0.30% |  | 
 | LDB | -0.12% | 0.24% | 0.18% |  | 
CE7-1 results without CE7-1 Qp/lambda tuning | AI | -0.13% | 0.21% | -0.02% |  | 
 | RA |  |  |  |  | 
 | LDB | -0.13% | 0.17% | -0.06% |  | 
Proposed method with CE7-1 lambda tuning | AI | -0.28% | 0.56% | 0.48% |  | 
 | RA | -0.18% | 0.40% | 0.44% |  | 
 | LDB | -0.16% | 0.28% | 0.07% |  | 
CE7-1 results with CE7-1 Qp/lambda tuning | AI | -0.28% | 0.57% | 0.27% | 108% | 99%
 | RA | -0.19% | 0.24% | -0.10% | 102% | 100%
 | LDB | -0.18% | 0.09% | -0.58% | 103% | 100%
Default Qp {22, 27, 32, 27}
Low-Qp {2, 7, 12, 17}
Highest coding gains are observed for sequence classes A and F

## Slide 8
Conclusion
Main benefits of the proposed method:
Invertibility property avoids chroma artifacts due to accidental use of the method
Avoids determining and signalling a mode-specific Qp offset value, which may be an encoder burden
Interesting coding efficiency benefits with low runtime impact
It is suggested to adopt the proposed method for joint coding of chroma residuals into VVC.