## Slide 1: JVET-N0358 Harmonization of CBF coding for ISP coding mode
Zhi Zhang
Ericsson

## Slide 2: CBF for intra sub-partition in VTM4
Decoder assume at least one sub-partition has a non-zero CBF
  Block is divided into n (n = 2 or 4) sub-partitions
  CBF for first n  1 sub-partitions are decoded from bitstream
  CBF for the n-th sub-partition handled differently
    Inferred to be 1 if all first n  1 sub-partitions have a zero CBF
    Otherwise decoded from bitstream
Drawbacks
  Non-uniform handling of sub-partitions
  Restricted flexibility for encoder (all zero CBF not possible)

## Slide 3: Proposed method Explicit signal CBF for all sub-partitions
Same CBF decoding process for each sub-partition
Remove the restriction of encoder
  Encoder is able to select a block with each sub-partition has a zero CBF
Small impact on coding efficiency contributed by ISP
  Reference from AHG13 report: Tool reporting procedure
No impact on encoding / decoding time
 | AI (Y) | RA (Y) | LDB (Y)
Proposed method | 0.04% | 0.00% | 0.01%
ISP tool off | 0.61% | 0.26% | 0.13%

## Slide 4: Statistic of CBF useage for block is divided into 4 sub-partitions
16 possbile CBF usage in total
Usage for each sub-partition has a zero CBF is 6.7% (higher than many other CBF combinations)
CBF combination | Probability | CBF useage | Probability | CBF useage | Probability | CBF useage | Probability
0000 | 6.7% | 0100 | 3.2% | 1000 | 6.4% | 1100 | 4.8%
0001 | 15.0% | 0101 | 2.4% | 1001 | 3.3% | 1101 | 3.7%
0010 | 3.0% | 0110 | 3.2% | 1010 | 1.6% | 1110 | 5.0%
0011 | 8.2% | 0111 | 8.3% | 1011 | 3.7% | 1111 | 21.5%

## Slide 5: WD text change
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex ) { | Descriptor
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex < NumIntraSubPartitions − 1 ¦ ¦ !InferTuCbfLuma ) ) ) | 
tu_cbf_luma[ x0 ][ y0 ] | ae(v)
if (IntraSubPartitionsSplitType != ISP_NO_SPLIT ) | 
InferTuCbfLuma = InferTuCbfLuma && !tu_cbf_luma[ x0 ][ y0 ] | 
} | 

## Slide 6: Simulation results
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,03% | 0,04% | 0,07% | 94% | 100%
Class A2 | 0,03% | 0,15% | 0,02% | 92% | 100%
Class B | 0,04% | 0,06% | 0,10% | 91% | 101%
Class C | 0,05% | -0,03% | 0,00% | 81% | 101%
Class E | 0,07% | 0,09% | 0,10% | 88% | 101%
Overall | 0,04% | 0,06% | 0,06% | 89% | 100%
Class D | 0,02% | 0,13% | 0,01% | 78% | 101%
Class F | 0,08% | 0,05% | -0,09% | 87% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,06% | -0,06% | 88% | 100%
Class A2 | -0,02% | 0,10% | 0,00% | 90% | 101%
Class B | 0,01% | -0,04% | -0,10% | 83% | 100%
Class C | 0,03% | -0,26% | -0,06% | 82% | 100%
Class E |  |  |  |  | 
Overall | 0,00% | -0,05% | -0,06% | 85% | 100%
Class D | -0,03% | -0,12% | 0,39% | 83% | 99%
Class F | 0,02% | -0,02% | 0,06% | 89% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,01% | -0,11% | -0,37% | 97% | 99%
Class C | -0,02% | 0,32% | -0,06% | 86% | 99%
Class E | 0,10% | 0,22% | 0,15% | 80% | 98%
Overall | 0,01% | 0,11% | -0,14% | 89% | 99%
Class D | -0,05% | -0,21% | -0,64% | 74% | 99%
Class F | -0,03% | 0,32% | -0,07% | 87% | 99%
Encoding time on different machines
Decoding on same machine
Cross-checker results show
  Encoding time ~ 99%
  Decoding time ~ 99%

## Slide 7: Conclusion
Advantage to explicit signal the CBF for each sub-partition
  Harmonize CBF decoding process for each sub-partition
  Remove the encoder restriction
  Marginal impact on coding efficiency for AI
  Negligible impact on coding efficiency for RA / LDB