## Slide 1: JVET-N0359 On MV threshold for deblocking K. Andersson, J. Enhorn (Ericsson)
Kenneth Andersson
Ericsson
2019-03-18

## Slide 2: Summary
The MV threshold of 1 luma sample used for deblocking produce boundaries that not are deblocked in VTM-4.0
It is proposed to fix this for next version of VTM by reducing the threshold to a quarter sample
Gives a subjective benefit at a BDR loss of 0.1% for RA and LD with similar encoding and decoding time.

## Slide 3: Visual artifacts in VTM (LDP FourPeople QP=39)

## Slide 4: ¼ luma sample MV threshold (LDP FourPeople QP=39)

## Slide 5: Visual artifacts in VTM (LDP FourPeople QP=39)

## Slide 6: ¼ luma sample MV threshold(LDP FourPeople QP=39)

## Slide 7: Visual examples for sub sample differences in one MV component from block P and Q
Block P and Q in current picture
Reference picture

## Slide 8: Visual example for sub sample differences in horisontal MV components from block P and Q
2 quarter luma sample
(not discovered by VTM)
3 quarter luma sample
(not discovered by VTM)
4 quarter luma sample
(can be discovered by VTM)

## Slide 9: Proposed change to VVC
Modify MV component difference threshold in deblocking to one quarter luma sample

## Slide 10: WD text
  8.5.2.5 Derivation process of boundary filtering strength
  ..
      The coding subblock containing the sample p0 and the coding subblock containing the sample q0 are both coded in IBC prediction mode, and the absolute difference between the horizontal or vertical component of the motion vectors used in the prediction of the two coding subblocks is greater than or equal to 1 in units of quarter luma samples.
      For the prediction of the coding subblock containing the sample p0 different reference pictures or a different number of motion vectors are used than for the prediction of the coding subblock containing the sample q0.
NOTE 1 – The determination of whether the reference pictures used for the two coding sublocks are the same or different is based only on which pictures are referenced, without regard to whether a prediction is formed using an index into reference picture list 0 or an index into reference picture list 1, and also without regard to whether the index position within a reference picture list is different.
NOTE 2 – The number of motion vectors that are used for the prediction of a coding subblock with top-left sample covering ( xSb, ySb ), is equal to PredFlagL0[ xSb ][ ySb ] + PredFlagL1[ xSb ][ ySb ].
      One motion vector is used to predict the coding subblock containing the sample p0 and one motion vector is used to predict the coding subblock containing the sample q0, and the absolute difference between the horizontal or vertical component of the motion vectors used is greater than or equal to 1 in units of quarter luma samples.
      Two motion vectors and two different reference pictures are used to predict the coding subblock containing the sample p0, two motion vectors for the same two reference pictures are used to predict the coding subblock containing the sample q0 and the absolute difference between the horizontal or vertical component of the two motion vectors used in the prediction of the two coding subblocks for the same reference picture is greater than or equal to 1 in units of quarter luma samples.
      Two motion vectors for the same reference picture are used to predict the coding subblock containing the sample p0, two motion vectors for the same reference picture are used to predict the coding subblock containing the sample q0 and both of the following conditions are true:
        The absolute difference between the horizontal or vertical component of list 0 motion vectors used in the prediction of the two coding subblocks is greater than or equal to 1 in quarter luma samples, or the absolute difference between the horizontal or vertical component of the list 1 motion vectors used in the prediction of the two coding subblocks is greater than or equal to 1 in units of quarter luma samples.
The absolute difference between the horizontal or vertical component of list 0 motion vector used in the prediction of the coding subblock containing the sample p0 and the list 1 motion vector used in the prediction of the coding subblock containing the sample q0 is greater than or equal to 1 in units of quarter luma samples, or the absolute difference between the horizontal or vertical component of the list 1 motion vector used in the prediction of the coding subblock containing the sample p0 and list 0 motion vector used in the prediction of the coding subblock containing the sample q0 is greater than or equal to 1 in units of quarter luma samples.

## Slide 11: CTC results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,06% | 0,04% | -0,02% | 99% | 99%
Class A2 | 0,20% | -0,07% | -0,02% | 100% | 101%
Class B | 0,17% | -0,02% | 0,01% | 99% | 102%
Class C | 0,10% | 0,01% | -0,03% | 100% | 102%
Class E |  |  |  |  | 
Overall | 0,13% | -0,01% | -0,02% | 99% | 101%
Class D | 0,16% | -0,09% | -0,01% | 101% | 103%
Class F | 0,07% | 0,03% | -0,01% | 106% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,10% | -0,15% | -0,21% | 99% | 100%
Class C | -0,05% | 0,08% | -0,14% | 98% | 102%
Class E | 0,18% | -0,32% | -0,53% | 100% | 98%
Overall | 0,07% | -0,11% | -0,26% | 99% | 100%
Class D | 0,03% | 0,16% | -0,18% | 103% | 107%
Class F | -0,04% | -0,04% | -0,35% | 95% | 95%
 | All Intra Main10 |  |  |  | 
 | Over VTM-340 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 99% | 100%
Class A2 | 0,00% | 0,00% | 0,00% | 99% | 101%
Class B | 0,00% | 0,00% | 0,00% | 98% | 101%
Class C | 0,00% | 0,00% | 0,00% | 102% | 102%
Class E | 0,00% | 0,00% | 0,00% | 103% | 100%
Overall | 0,00% | 0,00% | 0,00% | 100% | 101%
Class D | 0,00% | 0,00% | 0,00% | 102% | 98%
Class F | 0,00% | 0,00% | 0,00% | 98% | 101%

## Slide 12: CTC only SBT fix
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,02% | 0,04% | 0,02% | 98% | 97%
Class A2 | 0,00% | -0,14% | -0,04% | 100% | 99%
Class B | 0,01% | -0,04% | 0,04% | 98% | 102%
Class C | 0,02% | -0,06% | 0,00% | 98% | 102%
Class E |  |  |  |  | 
Overall | 0,00% | -0,05% | 0,01% | 99% | 100%
Class D | 0,00% | -0,19% | -0,01% | 102% | 103%
Class F | 0,02% | 0,05% | 0,02% | 110% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,00% | -0,12% | 0,03% | 99% | 99%
Class C | -0,02% | 0,28% | -0,15% | 97% | 102%
Class E | -0,04% | -0,04% | -0,22% | 99% | 97%
Overall | -0,02% | 0,03% | -0,09% | 98% | 99%
Class D | 0,00% | 0,05% | -0,23% | 101% | 101%
Class F | -0,16% | -0,01% | 0,13% | 95% | 95%
 | All Intra Main10 |  |  |  | 
 | Over VTM-340 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 99% | 100%
Class A2 | 0,00% | 0,00% | 0,00% | 99% | 101%
Class B | 0,00% | 0,00% | 0,00% | 98% | 101%
Class C | 0,00% | 0,00% | 0,00% | 102% | 102%
Class E | 0,00% | 0,00% | 0,00% | 103% | 100%
Overall | 0,00% | 0,00% | 0,00% | 100% | 101%
Class D | 0,00% | 0,00% | 0,00% | 102% | 98%
Class F | 0,00% | 0,00% | 0,00% | 98% | 101%

## Slide 13: Conclusion
It has been shown that sub sample luma differences in a motion vector component can result in blocking artifacts.
It is therefore proposed to set the MV component difference threshold in deblocking more conservatively to a quarter of a luma sample to avoid by passing deblocking when its needed.
Benefits in subjective quality at BDR loss of 0.1% for RA and LDB.
It is proposed to include the new threshold for next version of VVC