## Slide 1: JVET-N0364: Non-CE6: Further cost reduction for primary transform
X. Zhao, X. Li , S. Liu ( Tencent )
2019/03

## Slide 2: Introduction
In Marrakesh meeting, a zero-out scheme for 32-point DST-7 and DCT-8 was adopted which reduces the worst-case multiplications per coefficient on primary transform
According to the analysis in JVET-M0046

## Slide 3: Proposed methods
Method 1
For 32x64 DCT-2, switch the horizontal and vertical transform, such that 64-length vertical DCT-2 transform using zero-out is performed first, followed by the 32-length full size DCT-2.
For the 32x32 DCT-2, it is proposed to keep the non-zero coefficients for the top half 32x16 region, i.e., a zero-out transform (keeps the first 16 coefficients) is applied only for the vertical transform, while the horizontal transform is still a full-size transform

## Slide 4: Proposed methods
Method 2
For bot the 32x32 and 32x64 DCT-2, it is proposed to keep the non-zero coefficients for the top half 32x16 region

## Slide 5: Simulation Results
Anchor: VTM-4.0
Test 1: Method 1
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.00% | 0.01% | 100% | 98% | 0.01% | -0.01% | 0.03% | 101% | 102% |  |  |  |  | 
Class A2 | 0.03% | 0.16% | 0.08% | 101% | 101% | 0.02% | 0.10% | -0.04% | 102% | 102% |  |  |  |  | 
Class B | 0.02% | 0.08% | 0.06% | 100% | 100% | 0.04% | -0.01% | -0.15% | 101% | 101% | 0.01% | -0.20% | -0.32% | 101% | 104%
Class C | 0.01% | 0.03% | 0.02% | 100% | 101% | 0.05% | -0.02% | -0.05% | 101% | 102% | 0.08% | -0.07% | -0.23% | 100% | 102%
Class E | 0.01% | 0.04% | -0.05% | 100% | 100% |  |  |  |  |  | -0.08% | -0.25% | 0.28% | 101% | 103%
Overall | 0.02% | 0.06% | 0.03% | 100% | 100% | 0.03% | 0.01% | -0.06% | 101% | 102% | 0.01% | -0.17% | -0.14% | 100% | 103%
Class D | 0.03% | 0.03% | 0.01% | 103% | 104% | 0.06% | -0.24% | -0.12% | 101% | 103% | 0.07% | 0.10% | -0.71% | 101% | 100%
Class F | 0.00% | -0.03% | -0.05% | 101% | 101% | 0.02% | 0.11% | -0.04% | 102% | 102% | -0.03% | 0.06% | 0.19% | 100% | 103%

## Slide 6: Simulation Results
Anchor: VTM-4.0
Test 1: Method 2
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.00% | 0.01% | 102% | 99% | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class A2 | 0.03% | 0.16% | 0.08% | 101% | 101% | 0.03% | 0.06% | -0.05% | 101% | 100% |  |  |  |  | 
Class B | 0.02% | 0.08% | 0.05% | 101% | 101% | 0.05% | -0.04% | -0.10% | 100% | 100% | 0.04% | -0.45% | -0.06% | 100% | 100%
Class C | 0.01% | 0.03% | 0.02% | 104% | 103% | 0.03% | 0.10% | -0.07% | 101% | 103% | 0.10% | -0.03% | -0.03% | 98% | 99%
Class E | 0.01% | 0.04% | -0.05% | 99% | 99% |  |  |  |  |  | 0.00% | -0.08% | 0.76% | 104% | 104%
Overall | 0.02% | 0.06% | 0.03% | 101% | 101% | 0.03% | 0.02% | -0.06% | 101% | 101% | 0.05% | -0.22% | 0.16% | 101% | 101%
Class D | 0.03% | 0.03% | 0.01% | 102% | 104% | 0.06% | -0.18% | -0.10% | 101% | 103% | 0.06% | -0.15% | -1.17% | 104% | 104%
Class F | 0.00% | -0.03% | -0.05% | 102% | 102% | 0.02% | 0.15% | -0.03% | 101% | 102% | -0.10% | -0.32% | -0.04% | 98% | 101%

## Slide 7: Conclusion
It is reportedly shown that the worst-case multiplication per sample is reduced by 25% with proposed method
It is recommended to further study in CE together with coefficient coding changes applied for transform zero-out
Thanks to Samsung for crosscheck!