## Slide 1: Non-CE6: Shape Adaptive Transform Selection for ISP, SBT and MTS
JVET-N0388
Mar. 2019
Karam NASER, Tangi POIRIER, Fabrice Le LEANNEC

## Slide 2: Introduction
Current spec is too complicated for transform selection

## Slide 3: Introduction
VTM4.0:
SPS flag to enable implicitMTS:
  sps_mts_enabled_flag is true and both sps_explicit_mts_intra_enabled_flag are false
sps_mts_enabled_flag | u(1)
if( sps_mts_enabled_flag ) { | 
sps_explicit_mts_intra_enabled_flag | u(1)
sps_explicit_mts_inter_enabled_flag | u(1)
} | 

## Slide 4: Proposal
Clean up the transform selection process

## Slide 5: Proposal
- Embedding shape adaptive transform selection in MTS:
- ISP and SBT uses shape adaptive transform selection
tu_mts_idx | transform type |  | binarization |  | 
 | horizontal | vertical | MTS & TS enabled | MTS enabled | TS enabled
0 | SKIP | SKIP | 0 | - | 0
1 | DCT-II | DCT-II | 10 | 0 | 1
2 | DST-VII | DST-VII | 110 | 10 | -
3 | DCT-VIII | DST-VII | 1110 | 110 | -
4 | DST-VII | DCT-VIII | 11110 | 1110 | -
5 | ImplicitMTS | ImplicitMTS | 11111 | 1111 | -

## Slide 6: Proposal
No ImplicitMTS flag coding
The encoder can optionally select to always use shape adaptive transform selection (last pair in MTS) to emulate ImplicitMTS
sps_mts_enabled_flag | u(1)
if( sps_mts_enabled_flag ) { | 
sps_explicit_mts_intra_enabled_flag | u(1)
sps_explicit_mts_inter_enabled_flag | u(1)
} | 
If (sps_explicit_mts_intra_enabled_flag ¦¦ sps_explicit_mts_inter_enabled_flag) | 
sps_mts_enabled_flag =1 | 

## Slide 7: Experimental Results
Test 1: Implicit MTS for ISP and SBT and inside MTS
Thanks to LGE for cross-check

## Slide 8: Experimental Results
Test 2: Implicit MTS for ISP and SBT and inside MTS
Thanks to LGE for cross-check

## Slide 9: Conclusion
-Simplification and cleanup regarding transform selection is presented
-SPS flag is removed
-Results show zero loss (Test2) or reasonable loss (Test1)