## Slide 1: CE3-related: Unified MPM list based on CE3-3.3 and CE3-3.5.1 (JVET-N0394)
L. Zhao, X. Zhao, X. Li , S. Liu ( Tencent )
2019/03

## Slide 2: Introduction
Harmonization of MPM list has been studied in CE3-3
For CE3-3.3.2 and CE3-3.3.3
  Planar and DC modes are always the first two MPMs
  4 angular MPMs are derived using the zero-reference line MPM list generation
For CE3-3.5.1
  Planar and DC modes are coded separately
  5/6 angular MPMs are derived by using the non-zero reference lines MPM list generation process

## Slide 3: Proposed method
Combination between CE3-3.3 and CE3-3.5.1
  Planar and DC modes are always the first two MPMs (CE3-3.3)
  5/6 angular MPMs are derived by using the non-zero reference lines MPM list generation process (CE3-3.5.1)

## Slide 4: Proposed method
Further combination with JVET-N0450
  Lossless encoder speedup for the intra mode search (Feature #1)
  Encoder search in section 2.1 of JVET-N0450 is applied (Feature #2)
  Lambda value for the initial mode search is doubled (Feature #3)
  Only the first entry in the MPM list may be VDIA_IDX (Feature #4)

## Slide 5: Simulation Results
Anchor: VTM-4.0
Test 1: 5 angular MPMs + 2 contexts for MPM index
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.36% | -0.25% | -0.30% | 98% | 100% | -0.11% | -0.08% | -0.20% | 100% | 100%
Class A2 | -0.10% | 0.00% | -0.10% | 98% | 97% | -0.03% | 0.06% | -0.04% | 100% | 100%
Class B | -0.13% | -0.06% | -0.03% | 101% | 102% | -0.05% | -0.09% | 0.07% | 100% | 100%
Class C | -0.01% | -0.03% | 0.01% | 101% | 98% | 0.00% | 0.08% | -0.15% | 100% | 101%
Class E | -0.09% | 0.11% | -0.10% | 99% | 98% |  |  |  |  | 
Overall | -0.13% | -0.05% | -0.09% | 100% | 99% | -0.04% | -0.01% | -0.06% | 100% | 100%
Class D | -0.09% | -0.03% | -0.16% | 100% | 101% | 0.04% | -0.23% | -0.30% | 100% | 101%
Class F | 0.11% | 0.05% | 0.13% | 101% | 101% | 0.03% | -0.06% | -0.03% | 101% | 101%

## Slide 6: Simulation Results
Anchor: VTM-4.0
Test 2: 5 angular MPMs + 4 contexts for MPM index
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.42% | -0.31% | -0.34% | 100% | 103% | -0.12% | -0.04% | -0.15% | 100% | 100%
Class A2 | -0.14% | 0.01% | -0.18% | 98% | 98% | -0.03% | 0.24% | 0.09% | 100% | 99%
Class B | -0.17% | -0.14% | -0.11% | 102% | 102% | -0.05% | 0.03% | -0.24% | 101% | 100%
Class C | -0.05% | -0.11% | -0.04% | 99% | 100% | 0.03% | -0.01% | -0.06% | 101% | 101%
Class E | -0.16% | -0.08% | -0.08% | 99% | 98% |  |  |  |  | 
Overall | -0.18% | -0.13% | -0.14% | 100% | 101% | -0.04% | 0.05% | -0.11% | 100% | 100%
Class D | -0.09% | -0.03% | -0.19% | 100% | 100% | 0.00% | -0.22% | -0.12% | 100% | 101%
Class F | 0.10% | -0.06% | 0.01% | 100% | 100% | -0.01% | -0.02% | -0.14% | 100% | 101%

## Slide 7: Simulation Results
Anchor: VTM-4.0
Test 3: 6 angular MPMs + 2 contexts for MPM index
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.37% | -0.33% | -0.33% | 99% | 101% | -0.13% | -0.22% | -0.16% | 100% | 100%
Class A2 | -0.10% | -0.02% | -0.09% | 101% | 99% | -0.03% | 0.16% | 0.12% | 102% | 100%
Class B | -0.14% | -0.07% | -0.05% | 103% | 102% | -0.06% | 0.00% | -0.24% | 100% | 100%
Class C | -0.04% | -0.07% | -0.01% | 100% | 98% | 0.02% | 0.11% | -0.02% | 101% | 102%
Class E | -0.12% | 0.06% | 0.05% | 100% | 101% |  |  |  |  | 
Overall | -0.15% | -0.08% | -0.08% | 101% | 100% | -0.04% | 0.02% | -0.09% | 101% | 101%
Class D | -0.10% | 0.01% | -0.09% | 102% | 100% | 0.02% | -0.28% | -0.25% | 101% | 102%
Class F | 0.07% | 0.17% | 0.07% | 104% | 104% | 0.02% | 0.02% | 0.00% | 101% | 101%

## Slide 8: Simulation Results
Anchor: VTM-4.0
Test 4: 6 angular MPMs + 4 contexts for MPM index
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.42% | -0.41% | -0.35% | 99% | 102% | -0.14% | -0.38% | -0.10% | 99% | 100%
Class A2 | -0.15% | -0.03% | -0.11% | 99% | 98% | -0.06% | 0.02% | -0.01% | 100% | 99%
Class B | -0.18% | -0.08% | -0.11% | 101% | 100% | -0.06% | -0.10% | -0.22% | 100% | 99%
Class C | -0.06% | -0.09% | -0.02% | 100% | 95% | -0.03% | -0.03% | -0.18% | 101% | 100%
Class E | -0.18% | -0.08% | -0.07% | 100% | 98% |  |  |  |  | 
Overall | -0.19% | -0.13% | -0.12% | 100% | 99% | -0.07% | -0.11% | -0.15% | 100% | 100%
Class D | -0.09% | -0.09% | -0.18% | 103% | 100% | -0.01% | -0.12% | 0.11% | 100% | 100%
Class F | 0.07% | -0.07% | -0.06% | 101% | 99% | -0.01% | -0.02% | 0.00% | 100% | 99%

## Slide 9: Simulation Results
Anchor: VTM-4.0
Test 5: Test 4 + feature #1 (lossless encoder speedup) + feature #2 (modified intra search)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.42% | -0.47% | -0.35% | 95% | 101% | -0.15% | -0.22% | -0.25% | 99% | 99%
Class A2 | -0.14% | -0.01% | -0.14% | 95% | 97% | -0.07% | 0.07% | 0.04% | 99% | 99%
Class B | -0.18% | -0.17% | -0.05% | 97% | 101% | -0.04% | -0.05% | -0.06% | 100% | 99%
Class C | -0.06% | -0.08% | -0.04% | 97% | 101% | -0.01% | -0.08% | -0.14% | 101% | 103%
Class E | -0.15% | 0.00% | -0.02% | 98% | 102% |  |  |  |  | 
Overall | -0.18% | -0.15% | -0.11% | 97% | 100% | -0.06% | -0.07% | -0.10% | 100% | 100%
Class D | -0.07% | -0.04% | -0.13% | 99% | 103% | 0.02% | -0.35% | -0.08% | 101% | 103%
Class F | 0.04% | 0.05% | -0.10% | 98% | 100% | -0.03% | 0.03% | -0.09% | 101% | 101%

## Slide 10: Simulation Results
Anchor: VTM-4.0
Test 6: Test 5 + feature #3 (double lambda for intra search)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.48% | -0.42% | -0.33% | 94% | 102% | -0.12% | -0.26% | -0.24% | 99% | 98%
Class A2 | -0.19% | 0.00% | -0.16% | 95% | 96% | -0.04% | 0.21% | 0.01% | 99% | 99%
Class B | -0.23% | -0.16% | -0.13% | 96% | 102% | -0.09% | -0.02% | -0.24% | 100% | 99%
Class C | -0.12% | -0.10% | -0.04% | 96% | 100% | -0.03% | 0.05% | -0.31% | 100% | 101%
Class E | -0.23% | -0.04% | -0.06% | 96% | 100% |  |  |  |  | 
Overall | -0.24% | -0.14% | -0.14% | 96% | 100% | -0.07% | 0.00% | -0.21% | 99% | 100%
Class D | -0.14% | -0.03% | -0.20% | 97% | 104% | -0.04% | -0.39% | -0.12% | 100% | 103%
Class F | -0.02% | -0.05% | 0.11% | 98% | 100% | -0.03% | -0.13% | 0.04% | 101% | 102%

## Slide 11: Simulation Results
Anchor: VTM-4.0
Test 7: Test 6 + feature #4 (MPM list derivation modification)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.49% | -0.42% | -0.35% | 96% | 102% | -0.12% | -0.17% | -0.14% | 99% | 99%
Class A2 | -0.21% | -0.07% | -0.15% | 96% | 99% | -0.09% | -0.08% | 0.06% | 100% | 98%
Class B | -0.24% | -0.13% | -0.15% | 96% | 101% | -0.08% | 0.14% | -0.29% | 100% | 100%
Class C | -0.15% | -0.07% | -0.07% | 95% | 99% | 0.00% | -0.06% | -0.16% | 100% | 103%
Class E | -0.23% | -0.10% | -0.20% | 96% | 99% |  |  |  |  | 
Overall | -0.25% | -0.15% | -0.17% | 96% | 100% | -0.07% | -0.02% | -0.16% | 100% | 100%
Class D | -0.14% | -0.17% | -0.09% | 97% | 99% | -0.03% | -0.16% | 0.01% | 100% | 103%
Class F | -0.03% | -0.05% | -0.10% | 99% | 101% | -0.03% | -0.11% | -0.02% | 101% | 102%

## Slide 12: Conclusion
This contribution reports the combined CE tests between CE3-3.3 and CE3-3.5.1. Methods in CE3-related proposal JVE-N0450 are also combined
Combined test 7 achieves 0.25% coding gain in AI configuration with 96% encoding time
It is proposed to adopt this proposal