## Slide 1: CE10-related: Simplification and improvement of combined intra-inter prediction mode (JVET-N0395)
L. Zhao, X. Li , X. Zhao, S. Liu ( Tencent )
2019/03

## Slide 2: Proposed method
Firstly, Bi-directional optical flow (BDOF) is disabled for CIIP mode to save complexity
Secondly, a new mode Inter-PDPC is added
  When CIIP is on, another flag, called InterPdpc flag, is signaled to indicate whether to use the newly added mode or not
    When InterPdpc flag is true, PDPC filtering process is directly applied to the inter prediction indicated by merge index

## Slide 3: Decoder pipeline structure
One example of the decoder pipeline structure for the proposed method

## Slide 4: Simulation Results
Anchor: VTM-4.0
Test 1: Method 1 (Disable BDOF for CIIP mode)
 | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.03% | 100% | 100%
Class B | 0.00% | 0.01% | 0.01% | 100% | 100%
Class C | 0.01% | -0.09% | -0.06% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.02% | -0.01% | 101% | 100%
Class D | 0.01% | -0.16% | -0.18% | 101% | 103%
Class F | -0.01% | 0.01% | -0.02% | 101% | 101%

## Slide 5: Simulation Results
Anchor: VTM-4.0
Test 2: Method 1 + Method 2
 | Random Access Main10 |  |  |  |  | Low Delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.12% | -0.14% | -0.04% | 102% | 101% |  |  |  |  | 
Class A2 | -0.11% | -0.08% | 0.03% | 101% | 100% |  |  |  |  | 
Class B | -0.10% | -0.08% | -0.07% | 102% | 100% | -0.30% | -0.70% | -0.63% | 101% | 101%
Class C | -0.12% | -0.11% | -0.21% | 103% | 103% | -0.26% | -0.12% | -0.19% | 102% | 103%
Class E |  |  |  |  |  | -0.25% | -0.55% | -0.61% | 100% | 97%
Overall | -0.11% | -0.10% | -0.08% | 102% | 101% | -0.28% | -0.47% | -0.48% | 101% | 101%
Class D | -0.11% | 0.04% | -0.03% | 102% | 104% | -0.18% | -0.43% | -1.45% | 101% | 103%
Class F | -0.10% | 0.00% | -0.01% | 103% | 102% | -0.21% | 0.05% | 0.32% | 101% | 100%

## Slide 6: Conclusion
This contribution presents simplification and improvement for CIIP mode.
  Firstly, BDOF is disabled for CIIP mode to save complexity
  Secondly, Inter-PDPC is added as an additional mode of CIIP
The proposed method achieve 0.11% and 0.28% coding gain in RA and LDB configurations 102% and 101% encoding time
It is proposed to further study this proposal in CE