## Slide 1: JVET-N0396 – CE3-related: Enabling parallel reconstruction of small intra-coded blocks
L. Pham Van, G. Van der Auwera, A. K. Ramasubramonian, Vadim Seregin, H. Huang, M. Karczewicz
@qualcomm
03/2019
AV

## Slide 2: Introduction
In VTM4.0, chroma blocks may be small, e.g., 2x2, 2x4/4x2
Processing throughput is dropped when there are many small intra-coded blocks
VTM4.0 worst-case processing throughput: 2x2 chroma block (1/4 that of HEVC)
Data dependency for intra pred (IP).
Reconstruction order

## Slide 3: Increase worst-case processing throughput by: Enabling parallel processing for chroma blocks
Parallel processable region (PPR)
- All blocks in a PPR can be processed in parallel
PPR examples with minimum number of samples of 16:
4 | 4
4 | 4
8 | 
4 | 4
4 | 8 | 4
4 | 4 | 8
16

## Slide 4: Increase worst-case processing throughput by: Enabling parallel processing for chroma blocks
Parallel processing ability is achieved by removing intra-prediction dependency
All blocks in a PPR are treated as unavailable for IP of other blocks in this PPR
VTM4.0 ref. samples substitution is automatically invoked to fill unavailable samples
c | 
 | c
c
Unavailable for IP of current block
Current block

## Slide 5: Experimental results
Thanks LGE for cross-checking!
Experimental setting for chroma:
Dual tree: Disable 2x2, 2x4/4x2
Single tree: Enable parallel processing (Min size of PPR: 16)
 | AI |  | 
 | Over VTM-4.0 |  | 
 | Y | U | V
Class A1 | 0.01% | 0.16% | 0.11%
Class A2 | 0.04% | 0.39% | 0.23%
Class B | 0.00% | 0.18% | 0.29%
Class C | 0.05% | 1.06% | 1.56%
Class E | -0.02% | -0.05% | 0.05%
Overall | 0.02% | 0.37% | 0.49%
Class D | 0.12% | 1.80% | 2.48%
Class F | 0.19% | 1.56% | 1.96%
RA |  | 
Over VTM-4.0 |  | 
Y | U | V
0.02% | 0.12% | 0.14%
0.03% | 0.31% | 0.19%
0.04% | 0.24% | 0.29%
0.16% | 0.90% | 1.23%
0.07% | 0.40% | 0.49%
0.20% | 1.43% | 1.83%
0.21% | 1.10% | 1.42%
LDB |  | 
Over VTM-4.0 |  | 
Y | U | V
0.00% | -0.24% | -0.17%
0.02% | 0.36% | 0.42%
0.03% | 0.93% | 0.46%
0.01% | 0.25% | 0.18%
0.05% | 0.88% | -0.06%
-0.11% | 0.73% | 0.39%

## Slide 6: Conclusions
Worst-case processing throughput is increased by 4X.
- Prohibited 2x2, 2x4/4x2 chroma in DT
- Remove intra-prediction dependency in a PPR of size 16 samples
Minor (Y, U, V) BD-rate loss.
Consistent design with VTM4, no notable code change, clean spec text.
It is recommended to adopt the proposed technique to VVC.