## Slide 1: JVET-N0400 CE4-related Signaling of maximum number of triangle candidates
X. Li, G. Li, X. Xu, S. Liu
2019/03

## Slide 2: Introduction
In current WD,
  a fixed number of candidates in triangle merge is used
  Signaled number of candidates for other merge lists: regular/IBC merge, affine merge
  More flexibility is desirable
Reusing regular merge list for triangle merge process in JVET-N0340 has been adopted. When a small number of candidates is allowed for regular merge
  No enough candidates for triangle mode

## Slide 3: Proposed Method (1)
Triangle candidate number is signaled in tile group header based on candidate number of regular merge list
  Two candidate indices are signaled for triangle merge, two or more candidates are needed for triangle merge list
six_minus_max_num_merge_cand | ue(v)
if( sps_affine_enabled_flag ) | 
five_minus_max_num_subblock_merge_cand | ue(v)
if( sps_fpel_mmvd_enabled_flag ) | 
tile_group_fpel_mmvd_enabled_flag | u(1)
if( sps_triangle_enabled_flag && MaxNumMergeCand >= 2 ) | 
max_num_merge_cand_minus_max_num_triangle_cand | ue(v)

## Slide 4: Proposed Method (2)
Syntax change for merge data
  Max values used in truncated unary coding of merge_triangle_idx0 and merge_triangle_idx1 are set to MaxNumTriangleMergeCand – 1 and MaxNumTriangleMergeCand – 2, respectively
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
…… | 
if( sps_triangle_enabled_flag && tile_group_type = = B && ciip_flag[ x0 ][ y0 ] = = 0 && cbWidth * cbHeight >= 64 && MaxNumTriangleMergeCand >= 2) | 
merge_triangle_flag[ x0 ][ y0 ] | ae(v)
if( merge_triangle_flag[ x0 ][ y0 ] ) { | 
merge_triangle_split_dir[ x0 ][ y0 ] | ae(v)
merge_triangle_idx0[ x0 ][ y0 ] | ae(v)
merge_triangle_idx1[ x0 ][ y0 ] | ae(v)
} else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} | 
…… | 

## Slide 5: Simulation results
More tradeoff points between complexity and coding efficiency
  Anchor VTM-4.0
  Test, on top of CE-4-4-9-A
 | MaxTriangleCand=2 |  | MaxTriangleCand=4 |  | MaxTriangleCand=5 |  | MaxTriangleCand=6 | 
 | RA | LDB | RA | LDB | RA | LDB | RA | LDB
BD-rate Y | 0.25% | 0.67% | 0.02% | 0.13% | -0.03% | 0.02% | -0.07% | -0.01%
EncT | 91% | 88% | 96% | 95% | 100% | 102% | 103% | 106%
DecT | 99% | 99% | 99% | 99% | 100% | 101% | 99% | 100%

## Slide 6: Supplementary results on top of JVET-N0340
On top of newly adopted JVET-N0340
 |  | cand=6 |  | 
Over combN0400-cand5 |  |  |  | 
Y | U | V | EncT | DecT
0.00% | 0.11% | -0.02% | 104% | 100%
-0.01% | -0.12% | -0.06% | 105% | 99%
-0.03% | -0.02% | 0.10% | 104% | 99%
-0.05% | -0.17% | -0.11% | 104% | 99%
-0.02% | -0.05% | -0.01% | 104% | 99%
-0.08% | -0.17% | -0.33% | 104% | 99%
-0.05% | -0.07% | -0.08% | 104% | 101%
Over combN0400-cand5 |  |  |  | 
Y | U | V | EncT | DecT
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
0.00% | 0.17% | 0.36% | 106% | 104%
-0.03% | 0.59% | -0.75% | 108% | 97%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
-0.13% | -0.65% | -0.41% | 105% | 99%
-0.03% | 0.87% | -0.11% | 106% | 97%
 |  | Cand=2 |  | 
Over combN0400-cand5 |  |  |  | 
Y | U | V | EncT | DecT
#VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
0.19% | 0.28% | 0.26% | 90% | 99%
0.17% | 0.20% | 0.46% | 92% | 100%
0.34% | 0.40% | 0.53% | 92% | 100%
#VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
0.24% | 0.35% | -0.05% | 90% | 100%
0.23% | 0.22% | 0.18% | 93% | 100%
Over combN0400-cand5 |  |  |  | 
Y | U | V | EncT | DecT
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
0.43% | 0.94% | 1.01% | 90% | 100%
0.48% | 1.22% | 0.26% | 84% | 99%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
0.29% | 0.91% | 0.08% | 89% | 100%
0.24% | 1.06% | 0.09% | 88% | 96%
 | Cand5 | 
Over JVET-N0340 |  | 
Y | U | V
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.01% | 0.01% | 0.01%
0.02% | 0.02% | 0.02%
0.01% | 0.01% | 0.01%
0.06% | 0.06% | 0.06%
0.03% | 0.03% | 0.03%
Over JVET-N0340 |  | 
Y | U | V
#VALUE! | #VALUE! | #VALUE!
0.02% | 0.01% | 0.01%
0.13% | 0.11% | 0.11%
#VALUE! | #VALUE! | #VALUE!
0.06% | 0.04% | 0.04%
0.05% | 0.04% | 0.04%
 |  | cand=4 |  | 
Over combN0400-cand5 |  |  |  | 
Y | U | V | EncT | DecT
0.02% | 0.20% | 0.15% | 97% | 100%
0.04% | -0.02% | 0.03% | 96% | 100%
0.03% | 0.12% | 0.26% | 97% | 101%
0.06% | -0.04% | 0.06% | 96% | 100%
0.04% | 0.06% | 0.14% | 97% | 100%
0.06% | -0.03% | -0.11% | 96% | 100%
0.00% | 0.02% | 0.01% | 97% | 100%
Over combN0400-cand5 |  |  |  | 
Y | U | V | EncT | DecT
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
0.04% | 0.09% | 0.34% | 96% | 103%
0.13% | 0.82% | 0.26% | 94% | 100%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
-0.07% | -0.38% | -0.04% | 96% | 101%
-0.06% | -0.14% | 0.46% | 95% | 99%
 |  | MaxTriangleCand=2 |  | MaxTriangleCand=4 |  | MaxTriangleCand=5 |  | MaxTriangleCand=6 | 
on top of CE4-4-9-A |  | RA | LDB | RA | LDB | RA | LDB | RA | LDB
 | BD-rate Y | 0.25% | 0.67% | 0.02% | 0.13% | -0.03% | 0.02% | -0.07% | -0.01%
 | EncT | 91% | 88% | 96% | 95% | 100% | 102% | 103% | 106%
 | DecT | 99% | 99% | 99% | 99% | 100% | 101% | 99% | 100%
on top of JVET-N0340 |  | RA | LDB | RA | LDB | RA | LDB | RA | LDB
 | BD-rate Y |  |  | 0.04% |  | 0.01% |  | -0.02% | 
 | EncT |  |  | 97% |  | - |  | 104% | 
 | DecT |  |  | 100% |  | - |  | 99% | 

## Slide 7: Conclusion
Max number of triangle merge candidates is signaled instead of a fixed number
  More flexibility is obtained
Recommend to consider adoption of this proposal
Thanks to Qualcomm and Kwai for crosschecking!

## Slide 8
Thank you!