## Slide 1: JVET-N0426 History-based intra MPM default angular modes derivation
Zhi Zhang
Ericsson
2019-01-08

## Slide 2: Intra MPM default angular modes
Pre-defined angular mode ordering is applied in MPM list when:
  left neighbor block is not intra predicted or have a non-angular intra prediction mode
  above neighbor block is not intra predicted or have a non-angular intra prediction mode
Pre-defined angular mode ordering can not capture the spatially correlation in a local area
 | Pre-defined angular mode ordering |  |  |  |  | 
Reference line index > 0 | VER | HOR | 2 | DIA | VDIA | 26
ISP horizontal split | HOR | 25 | 10 | 65 | VER | 
ISP vertical split | VER | 43 | 60 | 3 | HOR | 
Reference line index == 0 && ISP no split | VER | HOR | 46 | 54 |  | 

## Slide 3: Intra modes buffer table Definition
The table is composed by
  3 unique vertical likely angular intra prediction modes (mode index >= 34)
  3 unique horizontal likely angular intra prediction modes (1 < mode index < 34)
  1 latest coded mode
The table is reset to pre-defined intra modes ordering [VER_IDX, HOR_IDX, VER_IDX - 4, VER_IDX + 4, 2, DIA_IDX] when a new slice is encountered
The table is updated following first in first out (FIFO) rule

## Slide 4: Intra modes buffer table Update process – CU level
A CU is coded with intra mode X
  X is angular mode
  Update the lastest coded mode to X
X is vertical likely mode (X >= 34)
  If X already in the table, remove the duplicate entry
  If X not in the table, remove the first entry
  Insert X to last entry of vertical likely mode table
X is horizontal likely mode (1 < X < 34)
  If X already in the table, remove the duplicate entry
  If X not in the table, remove the first entry
  Insert X to last entry of horizontal likely mode table

## Slide 5: Intra modes buffer table Update process – CTU level
First CTU
  Reset to pre-defined table
CTU at picture left boundary
  Inherit table from the last CU in CTU at above of current CTU
Other CTUs
  Inherit table from the last CU in CTU at left of current CTU

## Slide 6: MPM list derivation Both Left and Above are non-angular modes
extended reference line index > 0
ISP split type is horizontal split or vertical split
extended reference line index == 0 && ISP split type is no split
 | latest coded mode ≥ 34 | 1 < latest coded mode < 34
MPM list | V3, H3, V2, H2, V1, H1 | H3, V3, H2, V2, H1, V1
 | Vertical split | Horizontal split
MPM list | Planar, V3, V2, V1, H3, H2 | Planar, H3, H2, H1, V3, V2
 | latest coded mode ≥ 34 | 1 < latest coded mode < 34
MPM list (L == planar) | Planar, dc, V3, H3, V2, H2 | Planar, dc, H3, V3, H2, V2
MPM list (L == dc) | Dc, planar, V3, H3, V2, H2 | Dc, planar, H3, V3, H2, V2

## Slide 7: (Test 1) History-based MPM default angular modes derivation
VTM4.0 MPM list derivation when at least one angular mode from left and above neighbor block
History-based MPM list derivation when both left and above are non-angular modes
 | All Intra Main10 |  | 
 | Over VTM-4.0 |  | 
 | Y | U | V
Class A1 | -0,07% | -0,06% | -0,08%
Class A2 | -0,06% | 0,02% | -0,13%
Class B | -0,07% | -0,07% | 0,00%
Class C | -0,02% | -0,07% | -0,04%
Class E | 0,01% | 0,15% | 0,07%
Overall | -0,05% | -0,02% | -0,03%
Class D | 0,02% | -0,09% | -0,17%
Class F | 0,04% | 0,02% | -0,07%
 | Random Access Main 10 |  | 
 | Over VTM-4.0 |  | 
 | Y | U | V
Class A1 | -0,06% | -0,14% | -0,03%
Class A2 | -0,07% | 0,11% | -0,03%
Class B | -0,05% | 0,06% | -0,19%
Class C | -0,04% | -0,15% | -0,29%
Class E |  |  | 
Overall | -0,06% | -0,02% | -0,16%
Class D | 0,01% | -0,17% | -0,10%
Class F | 0,01% | -0,15% | -0,24%

## Slide 8: (Test 2) New initiate value for Left and Above intra prediction modes
In VTM4.0, Left (L) and Above (A) intra prediction modes are initiated to planar
In Test 2, L and A are initiated to -1
Insert to encoder full RD candidate list (numCand) increasing from 1 to 2 in following cases
  Left neighbor block does not exist or not intra predicted && A == planar
  L == planar && above neighbor block does not exist or not intra predicted
MPM list derivation is same as Test 1
 | All Intra Main10 |  | 
 | Over VTM-4.0 |  | 
 | Y | U | V
Class A1 | -0,09% | -0,01% | -0,10%
Class A2 | -0,08% | 0,03% | -0,09%
Class B | -0,10% | -0,07% | -0,02%
Class C | -0,05% | -0,14% | -0,05%
Class E | -0,01% | -0,01% | -0,01%
Overall | -0,07% | -0,05% | -0,05%
Class D | -0,04% | 0,04% | -0,06%
Class F | 0,03% | -0,03% | 0,00%
 | Random Access Main 10 |  | 
 | Over VTM-4.0 |  | 
 | Y | U | V
Class A1 | -0,07% | -0,15% | -0,14%
Class A2 | -0,10% | -0,06% | -0,03%
Class B | -0,03% | 0,02% | -0,18%
Class C | -0,03% | -0,19% | -0,11%
Class E |  |  | 
Overall | -0,05% | -0,09% | -0,12%
Class D | -0,05% | -0,25% | -0,10%
Class F | 0,03% | 0,02% | -0,14%

## Slide 9: Complexity analysis
No impact on MPM list derivation process
  The worst case for MPM list derivation process is when both L and A > dc && L != A
Complexity analysis compared to VTM4.0:
  A buffer table with 7 unsigned integers to store the coded angular intra prediction modes
  Maximum of 4 comparison to update the buffer table
  No complexity increases for MPM list derivation process
Avoid the complexity increase on 4x4 luma block
  Buffer table update process has been skipped when the coded block size is 4 × 4

## Slide 10: (Test B) Encoder full RD search for all mdoes in MPM list
Test B is defined in CE3.3
No decoder change
Encoder change is tested on top of test 1 and test 2
 | All Intra Main10 |  | 
Test 1 Test B | Over VTM-4.0 (encoder full RD search for modes in MPM list) |  | 
 | Y | U | V
Class A1 | -0,10% | -0,11% | -0,08%
Class A2 | -0,08% | -0,14% | -0,09%
Class B | -0,10% | -0,16% | -0,08%
Class C | -0,07% | -0,07% | -0,01%
Class E | 0,03% | 0,03% | 0,06%
Overall | -0,07% | -0,10% | -0,04%
Class D | -0,01% | -0,04% | -0,01%
Class F | 0,04% | -0,11% | 0,06%
 | All Intra Main10 |  | 
Test 2 Test B | Over VTM-4.0 (encoder full RD search for modes in MPM list) |  | 
 | Y | U | V
Class A1 | -0,11% | -0,12% | -0,06%
Class A2 | -0,09% | -0,15% | -0,12%
Class B | -0,10% | -0,13% | -0,11%
Class C | -0,07% | -0,10% | -0,05%
Class E | 0,02% | -0,03% | 0,04%
Overall | -0,07% | -0,11% | -0,07%
Class D | -0,01% | 0,09% | 0,09%
Class F | 0,05% | -0,03% | 0,01%

## Slide 11: Conclusion
Provide a solution for MPM list derivation when L and A are non-angular modes
Achieve similar BDR gain from AI configuration and RA configuration
Consistent results from Test B (encoder full RD search all modes in MPM list)