## Slide 1: JVET-N0433: CE3-related: Unification of MPM derivation for luma intra modes
A. K. Ramasubramonian, G. Van der Auwera, L. Pham Van, M. Karczewicz
Qualcomm

## Slide 2: Overview
For luma intra mode coding (excluding CIIP), MPM lists are generated differently for
  MRL blocks - reference line index greater than 0; PL, DC not included
  ISP blocks - coded with intra sub-partitions; DC not included
  Regular blocks – other blocks (not coded with ISP and reference line index 0)
Complicated design with several branches
Proposal – a simpler MPM list derivation which brings gain

## Slide 3: Proposal
Unified MPM list generation
  Six MPMs always in the list
  Simplified MPM design – starting with MPM list for regular blocks
  One or two replacement modes - to replace PL, DC as applicable
  No change in signalling
  No additional contexts defined
BD-rate: -0.11% (AI), -0.03% (RA)

## Slide 4: Proposal

## Slide 5: Simulation results
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.20% | -0.07% | -0.08% | 100% | 99%
Class A2 | -0.09% | 0.09% | -0.07% | 101% | 102%
Class B | -0.10% | -0.07% | 0.02% | 101% | 102%
Class C | -0.03% | -0.12% | -0.02% | 101% | 100%
Class E | -0.16% | 0.07% | -0.07% | 101% | 102%
Overall | -0.11% | -0.03% | -0.03% | 101% | 101%
Class D | -0.09% | -0.14% | -0.19% | 100% | 101%
Class F | 0.12% | 0.16% | 0.15% | 100% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | 0.04% | -0.20% | 100% | 99%
Class A2 | -0.03% | 0.21% | 0.04% | 97% | 96%
Class B | -0.03% | 0.04% | -0.21% | 100% | 100%
Class C | -0.02% | -0.14% | -0.22% | 99% | 100%
Class E |  |  |  |  | 
Overall | -0.03% | 0.02% | -0.16% | 99% | 99%
Class D | -0.01% | 0.04% | -0.17% | 99% | 99%
Class F | 0.05% | 0.05% | 0.09% | 100% | 100%

## Slide 6: Simulation results – modified encoder
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0-All |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.23% | -0.05% | 100% | 100%
Class A2 | -0.03% | -0.08% | -0.05% | 103% | 103%
Class B | -0.04% | 0.01% | 0.03% | 100% | 97%
Class C | 0.01% | -0.06% | 0.09% | 101% | 101%
Class E | -0.06% | -0.04% | 0.00% | 101% | 100%
Overall | -0.04% | -0.07% | 0.01% | 101% | 100%
Class D | -0.05% | 0.04% | -0.13% | 100% | 96%
Class F | 0.15% | 0.12% | 0.11% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0-All |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.07% | -0.17% | 100% | 99%
Class A2 | 0.00% | 0.03% | -0.01% | 104% | 103%
Class B | -0.01% | 0.02% | 0.00% | 100% | 100%
Class C | 0.00% | -0.12% | 0.03% | 99% | 99%
Class E |  |  |  |  | 
Overall | -0.01% | -0.03% | -0.03% | 101% | 100%
Class D | 0.02% | -0.36% | -0.04% | 100% | 100%
Class F | 0.04% | 0.00% | 0.08% | 100% | 100%

## Slide 7: Conclusions
Unified MPM list generation proposed
Results in simpler MPM design
  Only modification in list construction
  No changes to signalling
  No additional contexts defined
BD rate of -0.11% (AI), -0.03% (RA)
Proposed to include it in the VVC specification