## Slide 1: Non-CE3: On allowing non-MPM modes for ISP and non-zero reference line (JVET-N0437)
F. Bossen, K. Misra

## Slide 2: Overview
Motivation
Proposed Solution
Experimental Results
Recommendations

## Slide 3: Motivation
Current VVC WD limits Intra Sub Partitions (ISP) and Non-zero reference ling (NZRL) to Most Probable Modes (MPM)
MPMs are derived based on spatial intra modes. If a prediction mode suitable for current block of samples is not in MPM list, it cannot be used.
It is proposed to remove this constraint. It provides the following benefits:
Makes the intra mode signaling design more consistent,
Reduces the number of checks required for parsing, and
Allows flexibility in the design of future encoders

## Slide 4: Proposal
Allow non-MPM intra modes to be signaled for ISP and NZRL (same as for zero reference index): PLANAR, DC, 65 angular modes
Reference sample selection for INTRA_PLANAR and INTRA_DC prediction modes when using different reference lines
Removing the constraint and extending the search to be similar to zero reference index can give gains of up to 0.3% in certain classes albeit at higher encoder runtime
NOTE: The set of reference lines allowed is same as in VVC WD

## Slide 5: Experimental Results
Thank You Ericsson for crosscheck
Changes to WD provided with contribution
 | Y | U | V | EncT | DecT
All-Intra | 0.04% | 0.02% | 0.06% | 100% | 98%
Random Access | 0.02% | -0.06% | -0.08% | 100% | 100%
Low Delay B | -0.02% | 0.18% | 0.03% | 99% | 100%
PROPOSAL: Remove constraint but use VTM4 search

## Slide 6: Recommendation
It is proposed to allow non-MPM intra modes to be signaled for ISP and NZRL (same as for zero reference index)
It is recommended that the approach be adopted in the next version of the VVC WD and VTM.

## Slide 8: Backup Slides
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | 0.02% | -0.02% | 108% | 98%
Class A2 | -0.03% | 0.07% | -0.05% | 109% | 98%
Class B | -0.07% | 0.00% | 0.00% | 110% | 99%
Class C | -0.17% | -0.15% | -0.17% | 111% | 99%
Class E | -0.16% | -0.08% | -0.11% | 109% | 99%
Overall | -0.09% | -0.03% | -0.07% | 110% | 99%
Class D | -0.21% | -0.17% | -0.24% | 110% | 95%
Class F | -0.21% | -0.11% | -0.15% | 105% | 98%
  Allow non-MPM for ISP with encoder changes

## Slide 9: Backup Slides
Allow non-MPM for NZRL with encoder changes
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.06% | 0.05% | 156% | 97%
Class A2 | -0.03% | 0.17% | 0.03% | 156% | 98%
Class B | -0.03% | 0.03% | 0.05% | 157% | 98%
Class C | -0.06% | -0.07% | -0.03% | 159% | 99%
Class E | -0.02% | 0.12% | 0.07% | 159% | 98%
Overall | -0.03% | 0.05% | 0.03% | 157% | 98%
Class D | -0.05% | 0.09% | 0.00% | 160% | 98%
Class F | -0.15% | -0.02% | -0.14% | 131% | 96%

## Slide 10: Backup Slides
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.06% | 0.05% | 167% | 98%
Class A2 | -0.07% | 0.13% | 0.02% | 162% | 98%
Class B | -0.09% | 0.04% | -0.04% | 164% | 97%
Class C | -0.23% | -0.22% | -0.19% | 161% | 97%
Class E | -0.17% | 0.04% | -0.07% | 167% | 100%
Overall | -0.12% | 0.00% | -0.05% | 164% | 98%
Class D | -0.27% | -0.24% | -0.31% | 157% | 88%
Class F | -0.34% | -0.18% | -0.36% | 134% | 97%
  Allow non-MPM for ISP and NZRL with encoder changes