## Slide 1: JVET-N0438 AHG 12: Loop filter disabled across virtual boundaries
Sheng-Yen Lin, Lin Liu, Jian-Liang Lin, Yung-Chang Chang, Chi-Cheng Ju
Philippe Hanhart, Yuwen He

## Slide 2: Introduction
In some use cases, the in-loop could be selectively disabled in a picture to achieve better performance.
  For example of a 360° video, applying the in-loop filters on discontinuous edges directly may result in poor visual quality and decreased coding efficiency.
To address this problem, it is proposed to disable the in-loop filters across virtual boundaries in the picture.
Fig. 1. An image of HEC in 3×2 layout

## Slide 3: Introduction (cont.)
In JVET-M0892, a syntax is proposed to signal vertical/horizontal virtual boundaries across which the in-loop filtering operations are disabled.
The signaling is designed to be general purpose, and applicable to other non-360° video use cases.
The BoG on CE13 recommended to adopt JVET-M0892 for disabling of in-loop filters at vertical and horizontal boundaries signalled in the SPS.
However, during the plenary, some concerns were raised regarding the 4 luma samples granularity and the maximum number of vertical/horizontal virtual boundaries that could be signaled.

## Slide 4: Proposed
In this contribution, the following changes are proposed compared to JVET-M0892 to address these concerns:
  The virtual boundary granularity is 8 luma samples to align with the deblocking grid.
  The maximum number of vertical virtual boundaries is 3.
  The maximum number of horizontal virtual boundaries is 3.
Compared to tiles, the proposed solution is more flexible as it does not require the virtual boundaries to be a multiple of the CTU size.

## Slide 5: Proposed Syntax
seq_parameter_set_rbsp( ) { | Descriptor
… | 
sps_loop_filter_across_virtual_boundaries_disabled_flag | u(1)
if( sps_loop_filter_across_virtual_boundaries_disabled_flag ) { | 
sps_num_ver_virtual_boundaries | u(2)
for( i = 0; i < sps_num_ver_virtual_boundaries; i++ ) { | 
sps_virtual_boundaries_pos_x[ i ] | u(v)
} | 
sps_num_hor_virtual_boundaries | u(2)
for( i = 0; i < sps_num_hor_virtual_boundaries; i++ ) { | 
sps_virtual_boundaries_pos_y[ i ] | u(v)
} | 
} | 
… | 
} | 
The location of vertical and horizontal virtual boundaries (in units of luma samples) are derived as follows :
  SpsVirtualBoundariesPosX[ i ] = sps_virtual_boundaries_pos_x[ i ] * 8
  SpsVirtualBoundariesPosY[ i ] = sps_virtual_boundaries_pos_y[ i ] * 8

## Slide 6: Experimental Results
Code base: VTM-4.0 and 360Lib-9.0-dev
Face size : 1280x1280
The simulations are conducted on PHEC and HEC.
 | End-to-end WS-PSNR |  |  | Codec WS-PSNR |  |  | Codec PSNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
PHEC with proposed method vs PHEC | -0.02% | -0.29% | -0.16% | -0.03% | -0.49% | -0.32% | -0.36% | -1.62% | -1.44%
EncT | 100 % |  |  |  |  |  |  |  | 
DecT | 99 % |  |  |  |  |  |  |  | 
 | End-to-end WS-PSNR |  |  | Codec WS-PSNR |  |  | Codec PSNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
HEC with proposed method vs HEC | -0.28% | -1.07% | -0.92% | -0.30% | -1.42% | -1.22% | -0.35% | -1.60% | -1.41%

## Slide 7: Subjective Quality Evaluation
Reconstructed YUV encoded under VTM-4.0 with QP = 37
Viewport centered at (yaw=135°, pitch=35°) and (yaw=135°, pitch=35°) are tested
viewport centered at (yaw=135°, pitch=35°)
viewport centered at (yaw=45°, pitch=-35°)

## Slide 8: HEC without in-loop filters disabled across face discontinuities
The subjective quality of SkateboardInLot (frame 19)
The image is cropped from the viewport centered at (yaw=135°, pitch=35°)

## Slide 9: HEC with in-loop filters disabled across face discontinuities
The subjective quality of SkateboardInLot (frame 19)
The image is cropped from the viewport centered at (yaw=135°, pitch=35°)

## Slide 10: HEC without in-loop filters disabled across face discontinuities
The subjective quality of Balboa (frame 288)
The image is cropped from the viewport centered at (yaw=45°, pitch=-35°)

## Slide 11: HEC with in-loop filters disabled across face discontinuities
The subjective quality of Balboa (frame 288)
The image is cropped from the viewport centered at (yaw=45°, pitch=-35°)

## Slide 12: HEC without in-loop filters disabled across face discontinuities
The subjective quality of Broadway (frame 192)
The image is cropped from the viewport centered at (yaw=45°, pitch=-35°)

## Slide 13: HEC with in-loop filters disabled across face discontinuities
The subjective quality of Broadway (frame 192)
The image is cropped from the viewport centered at (yaw=45°, pitch=-35°)