## Slide 1: JVET-N0447 Non-CE4: On triangle merge mode
​Yao-Jen Chang, Chun-Chi Chen, Wei-Jung Chien, Marta Karczewicz
​
​Geneva, CH
​Mar. 2019

## Slide 2: Summary
Two syntax changes proposed for triangle merge mode
  Proposed 1: Signal a new tile group index to indicate the maximum number of triangle merge candidates, i.e., MaxNumTriangleMergeCand
  Proposed 2: Skip the paring of the merge candidate index for the second triangle block, i.e., merge_triangle_idx1, as MaxNumTriangleMergeCand = 2
    Coding performance:
CTC | YUV-Bitrate | EncT / DecT
RA | -0.06%, -0.17%, -0.12% | 100% / 100%
LB | To be updated | To be updated
Notes: Proposal 1: It benefits to the video codec especially for video encoder to trade-off the complexity and bitrate

## Slide 3: Current VVC
VVC introduces a triangle merge mode for inter prediction to evenly split a CU into two triangle-shaped partitions
  Each triangle-shaped partition block always signals a merge index to specify the selected merge candidate, i.e., merge_triangle_idx0 and merge_triangle_idx1
There is no higher-level syntax to specify the number of triangle merge candidates
  In current VTM, the number is fixed to be 5, which is less flexible compared with normal merge mode and subblock merge mode

## Slide 4: Proposed 1
A new tile group element five_minus_max_num_triangle_merge_cand to indicate the maximum number of triangle merge candidates, i.e., MaxNumTriangleMergeCand
tile_group_header ( ) { | Descriptor
… | 
if( ( weighted_pred_flag && tile_group_type = = P ) ¦ ¦ ( weighted_bipred_flag && tile_group = = B ) ) | 
pred_weight_table( ) | 
six_minus_max_num_merge_cand | ue(v)
if( sps_affine_enabled_flag ) | 
five_minus_max_num_subblock_merge_cand | ue(v)
if( sps_triangle_enabled_flag ) | 
five_minus_max_num_triangle_merge_cand | ue(v)
if( sps_fpel_mmvd_enabled_flag ) | 
tile_group_fpel_mmvd_enabled_flag | u(1)
… | 
} | 
MaxNumTriangleMergeCand = T − five_minus_max_num_triangle_merge_cand
The value of MaxNumTriangleMergeCand shall be in the range of 2 to T, inclusive
If five_minus_max_num_triangle_merge_cand is not present, five_minus_max_num_triangle_merge_cand is inferred to be (T-2)
This proposal supports T could be either 5 or 6

## Slide 5: Proposed 2
Skip the parsing of merge_triangle_idx1 as MaxNumTriangleMergeCand = 2
  merge_triangle_idx1 inferred to be 0 as merge_triangle_idx0 = 1
  merge_triangle_idx1 inferred to be 1 as merge_triangle_idx0 = 0
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
… | 
if( sps_triangle_enabled_flag && tile_group_type = = B && ciip_flag[ x0 ][ y0 ] = = 0 && cbWidth * cbHeight >= 64 ) | 
merge_triangle_flag[ x0 ][ y0 ] | ae(v)
if( merge_triangle_flag[ x0 ][ y0 ] ) { | 
merge_triangle_split_dir[ x0 ][ y0 ] | ae(v)
merge_triangle_idx0[ x0 ][ y0 ] | ae(v)
if(MaxNumTriangleMergeCand > 2) | 
merge_triangle_idx1[ x0 ][ y0 ] | ae(v)
… | 
} | 

## Slide 6: Simulation results in VTM-4.0
Anchor: VTM-4.0 with MaxNumTriangleMergeCand = 2
Tested: Proposed 2 (Skip the parsing of merge_triangle_idx1 as MaxNumTriangleMergeCand = 2)
Thank Tencent for crosscheck!
Notes: Low delay
V4.0: Disable Triangle merge mode
  1.12, 1.20, 0.99
V4.2: QCM_MAX_NUM_TRI_CAND = 2
  0.53, 0.54, 0.55
v4.3: QCM_MAX_NUM_TRI_CAND = 3
  0.27, 0.25, 0.27
V4.4: QCM_MAX_NUM_TRI_CAND = 4
  0.08, 0.05, 0.08

## Slide 7: Conclusion
The proposed tile group syntax element five_minus_max_num_triangle_merge_cand could flexibly adjust the maximum number of triangle merge candidates
As MaxNumTriangleMergeCand = 2, no signaling of merge_triangle_idx1 by inferring merge_triangle_idx1 to be the opposite number of merge_triangle_idx0
  RA: -0.06% coding gain without runtime change
  LB: To be updated
Recommend to adopt the proposed syntax changes into the next VVC