## Slide 1: CE4-related: Simplification on MMVD distance table
Yan Zhang, Yao-Jen Chang, Chun-Chi Chen, Wei-Jung Chien, Marta Karczewicz

## Slide 2: Abstract
This contribution presents modifications on distance table of Merge with Motion Vector Difference (MMVD) by two methods:
    Method 1: Encoder only change.
    Method 2: Normative change.
Sub tests:
    Method 1 achieves 0.00% in RA case and -0.02% in LDB case with 3% and 3% encoding time saving respectively.
    Method 2 achieves 0.00% in RA case and -0.03% in LDB case with 3% and 2% encoding time saving respectively.

## Slide 3: Technical description
Method 1: Encoder only change
  MMVD candidates with distance offsets of 16 and 32 are skipped for testing in the encoder side
Method 2: Encoder only change
  MMVD distance table is modified from [1/4, 1/2, 1, 2, 4, 8, 16, 32] to [1/4, 1/2, 1, 2, 4, 8]
  Binarization of the last entry in modified distance table is also changed accordingly from 111110 to 11111

## Slide 4: Simulation results
Method 1, skipping MMVD candidates with distance offsets of 16 and 32 in encoder side
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.07% | 0.19% | 96% | 102%
Class A2 | -0.02% | -0.04% | 0.07% | 96% | 102%
Class B | 0.02% | 0.08% | 0.07% | 97% | 104%
Class C | -0.01% | 0.02% | -0.10% | 98% | 102%
Class E |  |  |  |  | 
Overall | 0.00% | 0.04% | 0.05% | 97% | 102%
Class D | -0.02% | -0.11% | -0.10% | 98% | 100%
Class F | 0.01% | 0.06% | 0.05% | 100% | 104%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | -0.03% | 0.19% | 97% | 105%
Class C | -0.03% | 0.00% | 0.17% | 96% | 106%
Class E | -0.07% | -0.01% | -0.35% | 97% | 114%
Overall | -0.02% | -0.02% | 0.05% | 97% | 107%
Class D | 0.00% | 0.54% | 0.13% | 97% | 103%
Class F | -0.04% | 0.24% | 1.08% | 98% | 113%

## Slide 5: Simulation results
Method 2, Remove the two largest distance table entries and modify binarization of the last distance index
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | 0.14% | 96% | 102%
Class A2 | -0.01% | -0.01% | 0.02% | 96% | 103%
Class B | -0.01% | 0.01% | 0.05% | 97% | 103%
Class C | 0.01% | 0.04% | -0.08% | 97% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | 0.01% | 0.03% | 97% | 102%
Class D | -0.04% | 0.03% | -0.01% | 97% | 99%
Class F | -0.02% | 0.02% | -0.02% | 100% | 104%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | -0.31% | 0.08% | 98% | 106%
Class C | -0.03% | 0.20% | 0.10% | 99% | 107%
Class E | -0.05% | -0.01% | -0.06% | 97% | 115%
Overall | -0.03% | -0.06% | 0.05% | 98% | 108%
Class D | -0.06% | 0.03% | 0.06% | 100% | 104%
Class F | -0.05% | 0.22% | 0.01% | 99% | 115%