## Slide 1: Non-CE8: On IBC reference buffer design
Jizheng Xu, Li Zhang, Kai Zhang, Hongbin Liu, Yue Wang

## Slide 2: Current design
Current 64x64
Reference area
Unavailable
Current IBC needs 3 additional 64x64 memory
  IBC reference buffer is highly bundled with VPDU decoding memory
  Irregular valid area and motion vectors
  Burden either encoder or decoder to check validity
  Memory reduction is desired
Propose an separate IBC reference buffer
  Remove most bitstream conformance constrains for IBC
  With 6.7% memory reduction, BD-rate is -0.99% classF, -2.57% TGM for AI
  With 6.7% memory increase, BD-rate is -1.31% classF, -3.23 % TGM for AI
  With 20% memory reduction, BD-rate is -0.43% classF, -0.93% TGM for AI

## Slide 3: A separate IBC reference buffer
Buffer size
  128x128 samples
    8-bit, 128x128x1.5x8/(64x64x3x1.5x10) = 1.067
    7-bit, 128x128x1.5x7/(64x64x3x1.5x10) = 0.933
  96x128 samples
    8-bit, 96x128x1.5x8/(64x64x3x1.5x10) = 0.8

## Slide 4: Writing to the buffer
For 128x128 CTU
  After decoding a CU, its reconstructed pixels before loop-filtering will be written to the buffer
IBC reference buffer
CTUi,j
CTUi,j-1
CTUi-1,j
CTUi-1,j-1
CTUi+1,j-1
CTUi+1,j1
Current CU
(x,y)
Convert to 7-bit
(x%128,y%128)

## Slide 5: An example
CTUi,j
CTUi-1,j
IBC reference buffer status
Current CU
Reconstructed samples in previous CTU
Before decoding current CU
After decoding current CU
Reconstructed samples in current CTU

## Slide 6: Reference from the buffer
For any sample (x, y) relative to the picture with block vector (BVx, Bvy)
  Its prediction is IBC_buffer[(x+BVx)%128][(y+BVy)%128], converted to 10-bit.
    (-n)%128 128 – (n%128)
  “Wraparound” within IBC reference buffer
One CU’s IBC takes 1 or 2 parts’ copying from IBC reference buffer
IBC reference buffer
(xCb+BVx)%128 = 124
(yCb+BVy)%128 = 0

## Slide 7: Smaller CTU
For 64x64 CTU
  After decoding a CU, its reconstructed pixels before loop-filtering will be written to the buffer
  Prediction is from IBC_buffer[(x+BVx)%256][(y+BVy)%64]
CTUi,j
CTUi,j-1
CTUi-1,j
CTUi-1,j-1
CTUi+1,j-1
CTUi+1,j1
Current CU
(x,y)
Convert to 7-bit
(x%256,y%64)

## Slide 8: Benefit & cost
Benefits
  More reference area (up to 64x64), corresponding to previous CE8.1.2d
  7-bit’s setting reduces IBC memory requirement by 6.7%
  Easy validity check
    As long as reference block is within the reconstructed area in the current CTU-row, decoder’s results are well defined
    Simplify text, with much less bitstream conformance constrains
    With buffer initialization for each CTU row, all bitstream conformance constrains can be removed.
Costs
  One memory writing w/ bit-depth reduction after decoding each CU
  One additional step for bit-depth increase for each IBC block’s prediction

## Slide 9: Coding efficiency vs buffer size change
Thanks LGE for cross-checking JVET-N0251 and JVET-N0472
 | class | AI |  |  | RA |  | 
Anchor w/ local search range fix | F | -0.09% | -0.01% | -0.21% | -0.12% | -0.07% | -0.13%
 | TGM | -0.24% | -0.25% | -0.27% | -0.76% | -0.62% | -0.65%
7-bit 128x128 buffer (-1.5KBytes IBC reference memory) | F | -0.81% | -0.78% | -1.15% | -0.71% | -0.77% | -0.77%
 | TGM | -2.68% | -2.83% | -2.78% | -1.81% | -1.65% | -1.64%
8-bit 128x128 buffer (+1.5KBytes IBC reference memory) | F | -1.31% | -1.27% | -1.29% | -1.01% | -0.99% | -1.01%
 | TGM | -3.23% | -3.27% | -3.24% | -2.33% | -2.14% | -2.19%
8-bit 96x128 buffer (-4.5KBytes IBC reference memory) | F | -0.43% | -0.32% | -0.38% | -0.35% | -0.38% | -0.42%
 | TGM | -0.93% | -0.94% | -0.94% | -1.19% | -0.96% | -1.02%
JVET-N0251 bitstreams are decoded by a decoder implemented w/ a low bit-depth is applied.