## Slide 1
JVET-N0476:Non-CE4: Shared Merge List on the Constraints of Picture Sizes
Yi-Wen Chen, Xiaoyu Xiu, Tsung-Chuan Ma, Xianglin Wang

## Slide 2: Introduction
In current VVC, the picture width and height have to be multiple of 4 (the smallest CU size)
Two issues are observed for input sequences with resolution (8M+4) x (8N+4)
  SIMD Implementation issue of ALF in VTM4.0
  Sharing merge node have region located outside the picture boundary

## Slide 3: Proposed Solutions for the Issue of SML
1st solution: The picture width and height are constrained to be multiples of 8 (same as HEVC SPEC)
2nd solution: The picture width and height are constrained to be multiples of 4 (same as VVC SPEC)
  Fix the issue of share merge list (SML) by applying a truncation to the boundary to move the boundary of the merge sharing node to be aligned with a picture boundary when a boundary of a merge sharing node is located outside a picture
Both solutions introduces no impact on CTC

## Slide 4: Summary
When the input picture resolution is of (8M+4) x (8N+4), VTM encoder may crash
It is recommended to
  Fix the SIMD implementation issue of ALF
  Fix the SML issue by truncating the boundary of the sharing merge node to align with the picture boundary when its outside the picture boundary

## Slide 5: Thank you