## Slide 1: CE1 Related: Additional test results for CE1-7 tests
Dmytro Rusanovskyy, Kevin Reuze, Marta Karczewicz
JVET-K0482

## Slide 2: CE1-1.7 Test
Bilateral filter tested in CE1-1.x
  Constrains on neighboring access: a,b,c
  CE1-1.1 used as base design
  CE1-1.7 tested different parametrization
CE1-1.7 essence:
  More accurate PWL approximation of Weight Functions
    2 ranges instead of 1 range in CE1-1.1
    5 params to block level:
      [2],
  Complexity increase compare C1-1.1:
    +1 shift, 1 add, 1 comp
  Memory requirements:
    285 bytes ROM
    48 bits per block
Simulation results:
  Constrains A: -0.38% BD-Rate for RA, -0.41% BD-Rate for LDB
  Constrains C: -0.32% BD-Rate for RA, -0.39% BD-Rate for LDB
Chart: PWL model of Weights function

## Slide 3: CE1-1.7 test results
Simulation results vs. VTM4.0
CE1-1.7a |  |  | Random Access |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.19% | -0.28% | -0.04% | 107% | 116%
Class A2 | -0.42% | -0.24% | -0.08% | 100% | 102%
Class B | -0.49% | -0.08% | -0.04% | 88% | 99%
Class C | -0.35% | -0.03% | -0.08% | 90% | 102%
Class E |  |  |  |  | 
Overall | -0.38% | -0.14% | -0.06% | 95% | 104%
Class D | -0.37% | 0.07% | 0.04% | 90% | 98%
Class F | -0.16% | 0.08% | 0.01% | 100% | 86%
CE1-1.7a |  |  | Low Delay B |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.41% | 0.43% | 0.37% | 116% | 105%
Class C | -0.45% | 0.71% | 0.39% | 104% | 97%
Class E | -0.38% | 0.58% | 0.71% | 85% | 97%
Overall | -0.41% | 0.56% | 0.46% | 104% | 100%
Class D | -0.60% | 1.33% | -0.05% | 102% | 94%
Class F | -0.31% | 0.14% | 0.77% | 101% | 84%
CE1-1.7c | Random Access Main 10 |  |  |  | 
 | Over CE1-1.7c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.06% | -0.03% | 112% | 119%
Class A2 | -0.39% | -0.23% | -0.12% | 103% | 106%
Class B | -0.43% | -0.08% | -0.11% | 85% | 101%
Class C | -0.26% | 0.00% | 0.02% | 84% | 102%
Class E |  |  |  |  | 
Overall | -0.32% | -0.09% | -0.06% | 93% | 105%
Class D | -0.34% | 0.22% | 0.13% | 83% | 99%
Class F (optional) | -0.13% | 0.03% | -0.04% | 101% | 102%
CE1-1.7c | Low delay B Main10 |  |  |  | 
 | Over CE1-1.7c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.35% | 0.49% | 0.56% | 104% | 119%
Class C | -0.39% | 0.89% | 0.65% | 98% | 109%
Class E | -0.45% | 0.50% | -0.05% | 84% | 105%
Overall | -0.39% | 0.63% | 0.44% | 97% | 112%
Class D | -0.60% | 0.80% | 0.29% | 82% | 96%
Class F (optional) | -0.26% | 0.06% | 0.09% | 102% | 103%

## Slide 4: CE1-1.7 test results
Simulation results vs. CE1-1.1
CE1-1.7a vs. CE1-1.1a |  |  | Random Access |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.16% | 0.02% |  | 
Class A2 | -0.02% | 0.02% | 0.04% |  | 
Class B | -0.02% | 0.09% | 0.07% |  | 
Class C | -0.07% | -0.04% | -0.11% |  | 
Class E |  |  |  |  | 
Overall | -0.02% | -0.01% | 0.00% |  | 
Class D | -0.05% | 0.02% | -0.11% |  | 
Class F | -0.04% | 0.04% | 0.04% |  | 
CE1-1.7a vs. CE1-1.1a |  |  | Low Delay |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.05% | -0.25% | -0.58% |  | 
Class C | -0.15% | 0.09% | -0.28% |  | 
Class E | 0.03% | -0.07% | -0.01% |  | 
Overall | -0.06% | -0.09% | -0.34% |  | 
Class D | -0.08% | 0.27% | -0.58% |  | 
Class F | -0.15% | -0.18% | 0.46% |  | 
CE1-1.7c vs. CE1-1.1c | Random Access Main 10 |  |  |  | 
 | Over CE1-1.7c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.09% | 0.08% |  | 
Class A2 | -0.02% | -0.02% | 0.01% |  | 
Class B | 0.01% | -0.04% | -0.09% |  | 
Class C | -0.03% | -0.03% | 0.00% |  | 
Class E |  |  |  |  | 
Overall | -0.01% | -0.01% | -0.01% |  | 
Class D | -0.03% | 0.21% | 0.07% |  | 
Class F (optional) | -0.02% | -0.02% | -0.04% |  | 
CE1-1.7c vs. CE1-1.1c | Low delay B Main10 |  |  |  | 
 | Over CE1-1.7c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.07% | -0.14% | -0.35% |  | 
Class C | -0.11% | 0.37% | 0.07% |  | 
Class E | -0.08% | -0.30% | -0.72% |  | 
Overall | -0.08% | -0.01% | -0.30% |  | 
Class D | -0.05% | -0.11% | -0.66% |  | 
Class F (optional) | -0.17% | -0.04% | -0.57% |  | 

## Slide 5: CE1-1.7 summary:
More accurate PWL approximation of weight function:
  Complexity increase vs. CE1-1.1:
    1 add, 1 shift, 1 comp
  Memory increase vs. CE1-1.1:
    2 additional parameters to block (5 instead of 3)
    48 bits per block
Simulation results vs. VTM4.0:
  Constrains A:
    -0.38% BD-Rate for RA, -0.41% BD-Rate for LDB
  Constrains C:
    -0.32% BD-Rate for RA, -0.39% BD-Rate for LDB
Improvement over CE1-1.1:
  Constrains A:
    -0.02% BD-Rate for RA, -0.06% BD-Rate for LDB
    0.15% gain for class C and F
  Constrains C:
    -0.01% BD-Rate for RA, -0.0% BD-Rate for LDB
    0.11% gain for class C, 0.17% gain for class F
 | RA |  |  |  |  | LDB |  |  |  |  | 
Test# | Y | U | V |  |  | Y | U | V |  |  | 
CE1-1.1a | -0.35% | -0.13% | -0.06% |  |  | -0.35% | 0.65% | 0.81% |  |  | 
CE1-1.1c | -0.31% | -0.08% | -0.05% |  |  | -0.31% | 0.64% | 0.74% |  |  | 
CE1-1.2a | -0.33% | -0.13% | -0.10% |  |  | -0.23% | 0.74% | 0.52% |  |  | 
CE1-1.2c | -0.27% | -0.12% | -0.11% |  |  | -0.19% | 0.70% | 0.56% |  |  | 
CE1-1.3a | -0.25% | -0.09% | -0.07% |  |  | -0.09% | 0.88% | 0.41% |  |  | 
CE1-1.3b | -0.24% | -0.09% | -0.07% |  |  | -0.09% | 0.74% | 0.57% |  |  | 
CE1-1.3c | -0.21% | -0.08% | -0.09% |  |  | -0.04% | 0.93% | 0.60% |  |  | 
CE1-1.5 | -0.44% | -0.09% | -0.11% |  |  | -0.26% | 0.99% | 0.64% |  |  | 
CE1-1.7a2 | -0.38% | -0.14% | -0.06% |  |  | -0.41% | 0.56% | 0.46% |  |  | 
CE1-1.7c2 | -0.32% | -0.09% | -0.06% |  |  | -0.39% | 0.63% | 0.44% |  |  | 
CE1-2.1a | -0.32% | -0.13% | -0.06% |  |  | -0.34% | 0.64% | 0.59% |  |  | 
CE1-2.1b | -0.31% | -0.11% | -0.09% |  |  | -0.35% | 0.66% | 0.59% |  |  | 
CE1-2.1c | -0.30% | -0.09% | -0.06% |  |  | -0.36% | 0.75% | 0.72% |  |  | 
CE1-2.3 | -0.45% | -0.05% | -0.19% |  |  | -0.34% | 0.99% | 0.54% |  |  |