## Slide 1: JVET-N0492 CBF flags signalling in VVC
R. Chernyak, Y. Zhao, S. Ikonin, J. Chen

## Slide 2: Background
There is a mismatch between VVC 4 specification draft and VTM4.0 SW (ticket #203)
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex ) {
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) {
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex < NumIntraSubPartitions − 1 ¦ ¦ !InferTuCbfLuma ) ) )
tu_cbf_luma[ x0 ][ y0 ]
if (IntraSubPartitionsSplitType != ISP_NO_SPLIT )
InferTuCbfLuma = InferTuCbfLuma && !tu_cbf_luma[ x0 ][ y0 ]
}
if( ( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) {
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex = = NumIntraSubPartitions − 1 ) ) ) {
tu_cbf_cb[ x0 ][ y0 ]
tu_cbf_cr[ x0 ][ y0 ]
}
}
…
}
Specification
SW
void CABACReader::transform_tree(…)
{
...
if (chromaCbfs.Cb)
{
...
chromaCbfs.Cb &= cbf_comp(..., cbfDepth);
}
...
if (chromaCbfs.Cb)
{
...
chromaCbfs.Cb &= cbf_comp(..., cbfDepth);
}
...
if(... !chromaCbfs.sigChroma( area.chromaFormat ) )
{
TU::setCbfAtDepth( tu, COMPONENT_Y, trDepth, 1 );
}
else
{
cbfY = cbf_comp( cs, tu.Y(), trDepth );
...
}
...

## Slide 3: Spec - SW differences
The SW has hierarchical Chroma CBFs signaling
The SW has Luma Cbf deriving method
Both of abovementioned methods missed in the spec
 | Random Access Main 10 |  |  |  | 
 | Over VTM4.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.32% | 0.21% | 100% | 100%
Class A2 | 0.01% | 0.11% | 0.00% | 100% | 100%
Class B | 0.02% | 0.13% | 0.04% | 100% | 100%
Class C | 0.03% | 0.06% | -0.03% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.15% | 0.05% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 101% | 104%
Class F | 0.01% | 0.03% | 0.01% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM4.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | -0.11% | 0.00% | 100% | 100%
Class A2 | 0.06% | 0.04% | 0.16% | 100% | 100%
Class B | 0.10% | 0.08% | 0.02% | 100% | 100%
Class C | 0.12% | 0.10% | 0.16% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.10% | 0.04% | 0.08% | 100% | 100%
Class D | 0.11% | 0.10% | -0.08% | 101% | 104%
Class F | 0.23% | 0.39% | 0.11% | 101% | 100%
Hierarchical Cbf Off Test
Luma Cbf deriving Off Test

## Slide 4: Performance impact CTC
Hierarchical Cbf
Luma Cbf deriving

## Slide 5: Proposed solution. Aspect 1
Keep Luma Cbf deriving method only
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex ) { | Descriptor
if( ( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex = = NumIntraSubPartitions − 1 ) ) ) { | 
tu_cbf_cb[ x0 ][ y0 ] | ae(v)
tu_cbf_cr[ x0 ][ y0 ] | ae(v)
} | 
} | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) && (CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) ) ¦ ¦( (IntraSubPartitionsSplitType != ISP_NO_SPLIT) && ( subTuIndex < NumIntraSubPartitions − 1 ¦ ¦ !InferTuCbfLuma ) ) ) | 
tu_cbf_luma[ x0 ][ y0 ] | ae(v)
… | 
} | 

## Slide 6: Proposed solution. Aspect 2
Apply same to ISP Luma Cbf derivation method for TU64 partitioning
transform_tree( x0, y0, tbWidth, tbHeight , treeType) {
InferTuCbfLuma = 1
if( IntraSubPartSplitType = = NO_ISP_SPLIT ) {
if( tbWidth > MaxTbSizeY ¦ ¦ tbHeight > MaxTbSizeY ) {
trafoWidth = ( tbWidth > MaxTbSizeY ) ? (tbWidth / 2) : tbWidth
trafoHeight = ( tbHeight > MaxTbSizeY ) ? (tbHeight / 2) : tbHeight
transform_tree( x0, y0, trafoWidth, trafoHeight )
if( tbWidth > MaxTbSizeY )
transform_tree( x0 + trafoWidth, y0, trafoWidth, trafoHeight, treeType )
if( tbHeight > MaxTbSizeY )
transform_tree( x0, y0 + trafoHeight, trafoWidth, trafoHeight, treeType )
if( tbWidth > MaxTbSizeY && tbHeight > MaxTbSizeY )
transform_tree( x0 + trafoWidth, y0 + trafoHeight, trafoWidth, trafoHeight, treeType )
} else {
transform_unit( x0, y0, tbWidth, tbHeight, treeType, 0 )
}
} else if( cu_sbt_flag ) {
…

## Slide 7: Proposed solution. Aspect 2. Cont’d
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex ) { | Descriptor
if( ( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex = = NumIntraSubPartitions − 1 ) ) ) { | 
tu_cbf_cb[ x0 ][ y0 ] | ae(v)
tu_cbf_cr[ x0 ][ y0 ] | ae(v)
} | 
} | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) && (CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) ) ¦ ¦( (IntraSubPartitionsSplitType != ISP_NO_SPLIT ¦ ¦ (CbWidth[ x0 ][ y0 ] > MaxTbSizeY ¦ ¦ CbHeight[ x0 ][ y0 ] > MaxTbSizeY )) && ( subTuIndex < NumIntraSubPartitions − 1 ¦ ¦ !InferTuCbfLuma ) ) ) | 
… | 

## Slide 8: Acknowledgement
Many thanks to InterDigital and Philippe Hanhart for cross-check