## Slide 1: JN0493 – Multiplication-free bilateral loop filter
J. Ström, P. Wennersten, J. Enhorn, R. Sjöberg
VISTA
ER DRI
2019-01-31

## Slide 2: Overview
New loop filter stage right before deblocking
Center sample is filtered using neighboring samples
  Only right sample and belows samples needed
Difference is formed
Difference used to look-up modifier value
Sum together modifier values
Apply strength:
Filtered output:

## Slide 3: Arithmetic operations and memory requirements
Arithmetic operations per sample:
  13 additions plus 5 rounding additions per pixel, 8 shifts and 8 checks
  Largest addition width is 11 bits
Memory requirements
  Five tables of 16 items each, 6 bits
  5*16*6/8=60 bytes

## Slide 4: AI
 | Over VTM-4.0 |  |  |  |  | SIMD
 | Y | U | V | EncT | DecT | DecT
Class A1 | -0.28% | 0.31% | 0.18% | 111% | 120% | 104%
Class A2 | -0.43% | 0.36%! | 0.19% | 109% | 114% | 107%
Class B | -0.35% | 0.32% | 0.38% | 111% | 114% | 105%
Class C | -0.69% | 0.12% | 0.27% | 112% | 110% | 107%
Class E | -0.52% | 0.30% | 0.09% | 110% | 113% | 106%
Overall | -0.46% | 0.28% | 0.24% | 111% | 114% | 106%
Class D | -0.57% | 0.24% | 0.27% | 111% | 105% | 105%
Class F | -0.95% | 0.05% | 0.10% | 108% | 114% | 109%

## Slide 5: RA
 | Over VTM-4.0 |  |  |  |  | SIMD
 | Y | U | V | EncT | DecT | DecT
Class A1 | -0.40% | 0.13% | 0.18% | 103% | 100% | 103%
Class A2 | -0.56% | 0.09% | 0.05% | 103% | 99% | 99%
Class B | -0.61% | 0.34% | 0.15% | 105% | 103% | 102%
Class C | -0.79% | 0.47% | 0.25% | 106% | 101% | 100%
Class E |  |  |  |  |  | 
Overall | -0.61% | 0.28% | 0.16% | 104% | 101% | 101%
Class D | -0.75% | 0.10% | 0.12% | 104% | 105% | 101%
Class F | -1.15% | 0.04% | 0.05% | 115% | 104% | 102%

## Slide 6: LD
 | Over VTM-4.0 |  |  |  |  | SIMD
 | Y | U | V | EncT | DecT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | 
Class C | -0.73% | 1.37% | 0.99% | 101% | 98% | 100%
Class E | -0.34% | 1.10% | 0.70% | 102% | 96% | 98%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | 
Class D | -1.00% | 1.19% | 1.04% | 107% | 103% | 101%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | 99%

## Slide 7: LD version 1 (without CTU check)
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.46% | 1.31% | 0.90% |  | 
Class C | -0.78% | 1.19% | 0.89% |  | 
Class E | -0.50% | 0.65% | 1.82% |  | 
Overall | -0.58% | 1.11% | 1.13% |  | 
Class D | -1.01% | 1.32% | 1.23% |  | 
Class F | -1.29% | 0.69% | 0.51% |  | 

## Slide 8: RA version 3 (filters 1xN and 2xN blocks)
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.66% | 0.20% | -0.07% | 107% | 104%
Class C | -0.84% | 0.04% | -0.04% | 106% | 101%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.82% | -0.02% | -0.24% | 107% | 106%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Estimated end result is -0.65%

## Slide 10: Arithmetic operations
Operations per modification value | add +(round add) | add width | shift | check
 | 1 (1) | 10, 11 | 1 | 
 |  |  |  | 2
sum | 1 (1) |  | 1 | 2
Operations per modification value | add +(round add) | add width | shift | check
 | 1 (1) | 10, 11 | 1 | 
 |  |  |  | 2
sum | 1 (1) |  | 1 | 2

## Slide 11: Arithmetic operations per sample
Step | add (+round add) | add width | shift | check
and | 2 (2) | 10, 11 | 2 | 4
and | 2 (2) | 10, 11 | 4 | 4
 | 7 | 6,7,8 |  | 
 | 1 | 10 | 1 | 
 | 1 (1) | 10 | 1 | 
total per pixel | 13 + (5) |  | 8 | 8
Step | add (+round add) | add width | shift | check
 | 2 (2) | 10, 11 | 2 | 4
 | 2 (2) | 10, 11 | 4 | 4
 | 7 | 6,7,8 |  | 
 | 1 | 10 | 1 | 
 | 1 (1) | 10 | 1 | 
total per pixel | 13 + (5) |  | 8 | 8
13 additions plus 5 rounding additions per pixel, 8 shifts and 8 checks
Largest addition width is 11 bits