## Slide 1: Non-CE9: Simplification of parametric motion vector refinement in DMVR
JVET-N0505
Eiichi Sasaki
Tianyang Zhou
Tomohiro Ikai
Shap Corpolation

## Slide 2: Introduction
In Decoder-side Motion Vector Refinement (DMVR), sub-pel level refined motion vector is calculated by using SADs of integer-pel search.
This parametric motion vector refinement process requires division operation and we propose a simplification to remove division.
Copyright © All rights reserved, SHARP CORPORATION

## Slide 3: Original draft text on parametric motion vector refinement process
Copyright © All rights reserved, SHARP CORPORATION
The variable dX is derived as follows:
If sadList[ 3 ] + sadList[ 5 ] is equal to sadList[ 4 ] << 1,dX is set equal to 0.
Otherwise, (sadList[ 3 ] + sadList[ 5 ] is greater than sadList[ 4 ] << 1 ), the following applies:
dX = ( ( sadList[ 3 ] − sadList[ 5 ] ) << 3 ) / ( sadList[ 3 ] + sadList[ 5 ] − ( sadList[ 4 ] << 1 ) ) The variable dY is derived as follows:
If sadList[ 1 ] + sadList[ 7 ] is equal to sadList[ 4 ] << 1,dY is set equal to 0.
Otherwise (sadList[ 1 ] + sadList[ 7 ] is greater than sadList[ 4 ] << 1), the following applies:
dY = ( ( sadList[ 1 ] − sadList[ 7 ] ) << 3 ) / ( sadList[ 1 ] + sadList[ 7 ] − ( sadList[ 4 ] << 1 ) )
NOTE – dX is constrained to be between −8 and 8 since all values of sadList[ i ] with i = 0..8 are greater than 0 and the smallest value is sadList[ 4 ]. This allows the division to be performed with up to 4 quotient bits and can be implemented using compares, shifts, and subtractions.

## Slide 4: Proposed draft text on parametric motion vector refinement process
Copyright © All rights reserved, SHARP CORPORATION
The variable dX is derived as follows:
If Abs( sadList[ 3 ] – sadList[ 5 ] ) is less than or equal to Min( sadList[ 3 ], sadList[ 5 ] ) – sadList[ 4 ],dX is set equal to 0.
Otherwise, dX is set equal to Sign( sadList[ 3 ] – sadList[ 5 ] ) * 3.
The variable dY is derived as follows:
If Abs( sadList[ 1 ] – sadList[ 7 ] ) is less than or equal to Min( sadList[ 1 ], sadList[ 7 ] ) – sadList[ 4 ],dY is set equal to 0.
Otherwise, dY is set equal to Sign( sadList[ 1 ] – sadList[ 7 ] ) * 3.
Chart: 
original | 0 | 0 | 0 | 1 | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 3 | 4 | 4 | 4 | 5 | 5 | 5 | 6 | 6 | 6 | 7 | 7 | 7 | 8 | 8 | 8
proposal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3

## Slide 5: Simulation results
Proposed simplification has been implemented on VTM-4.0 and simulated under CTC
Thank NHK for cross-checking
Copyright © All rights reserved, SHARP CORPORATION
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.06% | -0.02% | 100% | 100%
Class A2 | 0.05% | 0.10% | 0.05% | 100% | 100%
Class B | 0.03% | 0.03% | 0.02% | 100% | 100%
Class C | 0.01% | -0.02% | -0.06% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.04% | 0.00% | 100% | 100%
Class D | 0.05% | 0.04% | -0.03% | 100% | 100%
Class F | -0.04% | 0.03% | 0.00% | 94% | 100%

## Slide 6: Conclusion
A division-free parametric motion vector refinement in DMVR is proposed.
We suggest to adopt this simplification to next WD.
Copyright © All rights reserved, SHARP CORPORATION