## Slide 1: JVET-N0507: Early termination of BDOF with DMVR cost
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: Summary
Introduce the proposal
  Reduce complexity of SAD calculation in BDOF
  Reuse SAD value that is calculated in DMVR
Report experiment results
Conclusion

## Slide 3: Proposed frame-work
SAD calc.
DMVR process
Motion estimation
BDOF process
Prediction with optical flow / usual bi-prediction
SAD cost
SAD calc.
DMVR process
Motion estimation
BDOF process
Prediction with optical flow / usual bi-prediction
MV
MV
VTM-4.0
Proposal
Normalize SAD cost, gap between DMVR and BDOF for bit depth and even lines usage in DMVR.
<<4

## Slide 4: In BDOF process
SAD calc.
Gradient filter
Find optical flow pram.
Prediction
4x4
If the 1st early termination was not used using SAD value from DMVR, also 2nd early termination is not used.
SAD from DMVR
Check the 1st early termination using SAD value from DMVR.
Threshold: same as 2nd early termination
Maybe the threshold differs to JVET-N0097.

## Slide 5: Experiment results
 | Random Access |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | -0.02% | 100% | 98%
Class A2 | 0.04% | 0.01% | 0.01% | 100% | 98%
Class B | 0.02% | 0.01% | -0.02% | 100% | 99%
Class C | 0.02% | 0.00% | -0.04% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.02% | 0.00% | -0.02% | 100% | 99%
Class D | 0.02% | 0.06% | -0.03% | 100% | 99%
Class F | 0.02% | 0.02% | 0.01% | 99% | 98%
Thank Sharp for the crosscheck!

## Slide 6: Conclusions
Introduced the proposal
  Reuse SAD value of DMVR in BDOF process.
Reported experiment results
  BD-rate impact is negligible.
  Decoding run time slightly decreases to 99%.
Recommendation
  This technique is studied in CE.