## Slide 1: JVET-N0507: Early termination of BDOF with DMVR cost
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: Summary
Introduce the proposal
  Reduce complexity of SAD calculation in BDOF
  Reuse SAD value that is calculated in DMVR
Report experiment results
Conclusion

## Slide 3: Proposed frame-work
SAD calc.
DMVR process
Motion estimation
BDOF process
Prediction with optical flow / usual bi-prediction
SAD cost
SAD calc.
DMVR process
Motion estimation
BDOF process
Prediction with optical flow / usual bi-prediction
MV
MV
VTM-4.0
Proposal
Normalize SAD cost, gap between DMVR and BDOF for bit depth and even lines usage in DMVR.
<<4

## Slide 4: In BDOF process
SAD calc.
Gradient filter
Find optical flow pram.
Prediction
4x4
If the 1st early termination was not used using SAD value from DMVR, also 2nd early termination is not used.
SAD from DMVR
Check the 1st early termination using SAD value from DMVR.
Threshold: same as 2nd early termination
Maybe the threshold differs to JVET-N0097.

## Slide 5: Experiment
Test-1
  Reuse SAD cost of DMVR
    If DMVR was disabled, the original early termination of BDOF is used.
Test-2 (Additional test on test-1)
  Remove SAD calculation in BDOF.
    If DMVR was enabled, the early termination is checked using SAD cost of DMVR.
    If DMVR was disabled, BDOF is always processed without early termination.

## Slide 6: Experiment results
 | Random Access |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | -0.02% | 100% | 98%
Class A2 | 0.04% | 0.01% | 0.01% | 100% | 98%
Class B | 0.02% | 0.01% | -0.02% | 100% | 99%
Class C | 0.02% | 0.00% | -0.04% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.02% | 0.00% | -0.02% | 100% | 99%
Class D | 0.02% | 0.06% | -0.03% | 100% | 99%
Class F | 0.02% | 0.02% | 0.01% | 99% | 98%
Thank Sharp for the crosscheck!
 |  |  | Random Access |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.08% | 0.01% | 100% | 98%
Class A2 | 0.02% | 0.03% | 0.05% | 101% | 98%
Class B | 0.01% | 0.04% | -0.02% | 101% | 99%
Class C | 0.00% | 0.02% | -0.03% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.01% | 0.04% | 0.00% | 101% | 99%
Class D | 0.02% | -0.03% | -0.08% | 100% | 99%
Class F | 0.01% | 0.02% | 0.00% | 101% | 98%
Test - 1
Test – 2 (Removed SAD in BDOF)

## Slide 7: DMVR and BDOF combination
Reuse SAD cost of DMVR
  Good to reduce a latency for SAD calculation.
    Although, it depends on the pipeline design.
Removal of the SAD calculation in BDOF
  Good to reduce hardware complexity
  Decoding run time doesn’t increase if DMVR cost is re-used.
    But, if DMVR was disabled, an early termination in BDOF can’t be used.
      But, the early termination may not be needed because decoder run time is already decreased since DMVR is disabled.
A threshold value to decide the early termination
  In VTM-4.0, there are two thresholds for 1st and 2nd early termination.
    This proposal used the threshold of 2nd early termination.

## Slide 8: Conclusions
Introduced the proposal
  Reuse SAD value of DMVR in BDOF process.
Reported experiment results
  BD-rate impact is negligible.
  Decoding run time slightly decreases to 99%.
Recommendation
  This technique is studied in CE.