## Slide 1: JVET-N0512 AhG2 : Editorial Suggestion on the text specification for Inter and IBC mode
H. Jang, J. Nam, N. Park, J. Lim, S. Kim

## Slide 2: Introduction
In this contribution, Only editorial change is suggested for inter prediction and intra block copy.
In VTM-4.0,
  IBC is enabled in dual tree I tile group.
  A variable CuPredMode[][] specifying prediction mode is not described for dual tree luma and dual tree chroma. In dual tree structure, CuPredMode[][] is overwritten
  The chroma block refer corresponding luma block for derivation process of INTRA_DM and derivation process for IBC chroma motion vector.
  If Current chroma block is coded intra prediction mode and the coding mode is INTRA_DM then intraPredModeY[][] should be defined. However in dual tree structure, intraPredModeY[][] could not be defined, if current luma block is IBC coded.

## Slide 3
pred_mode_flag equal to 0 specifies that the current coding unit is coded in inter prediction mode. pred_mode_flag equal to 1 specifies that the current coding unit is coded in intra prediction mode. The variable CuPredMode[ x ][ y ][ treeType ] is derived as follows for x = x0..x0 + cbWidth − 1 and y = y0..y0 + cbHeight − 1:
If pred_mode_flag is equal to 0, CuPredMode[ x ][ y ][ treeType ] is set equal to MODE_INTER.
Otherwise (pred_mode_flag is equal to 1), CuPredMode[ x ][ y ][ treeType ] is set equal to MODE_INTRA.
When pred_mode_flag is not present, it is inferred to be equal to 1 when decoding an I tile group, and equal to 0 when decoding a P or B tile group, respectively.

## Slide 4: Problem statement
IBC
INTRA_DM
INTRA
INTRA
CuPredMode[xCuY][yCuY] ????
CuPredMode[xCb][yCb]
Intra prediction
mode
intraPredModeY[][] ????

## Slide 5
8.4.3 Derivation process for chroma intra prediction mode Input to this process are: a luma location ( xCb, yCb ) specifying the top-left sample of the current chroma coding block relative to the top‑left luma sample of the current picture, a variable cbWidth specifying the width of the current coding block in luma samples, a variable cbHeight specifying the height of the current coding block in luma samples. a variable treeType specifying whether a single or a dual tree is used and if a dual tree is used, it specifies whether the current tree corresponds to the luma or chroma components. In this process, the chroma intra prediction mode IntraPredModeC[ xCb ][ yCb ] is derived as following:. If treeType is equal to DUAL_TREE_CHROMA_and CuPredMode[ xCb + (cbWidth /2) ][ yCb + (cbHeight /2) ][DUAL_TREE_LUMA] is equal to MODE_INTRA, the chroma intra prediction mode IntraPredModeC[ xCb ][ yCb ] is derived using intra_chroma_pred_mode[ xCb ][ yCb ] and IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] as specified in Table 8‑2 and Table 8‑3. Otherwise, if treeType is equal to SINGLE_TREE and CuPredMode[ xCb + (cbWidth /2)) ][ yCb + (cbHeight /2) ][SINGLE_TREE] is equal to MODE_INTRA, the chroma intra prediction mode IntraPredModeC[ xCb ][ yCb ] is derived using intra_chroma_pred_mode[ xCb ][ yCb ] and IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] as specified in Table 8‑2 and Table 8‑3. Otherwise, IntraPredModeC[ xCb ][ yCb ] is set equal to INTRA_DC.
intra_chroma_pred_mode[ xCb ][ yCb ] | IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] |  |  |  | 
 | 0 | 50 | 18 | 1 | X ( 0 <= X <= 66 )
0 | 66 | 0 | 0 | 0 | 0
1 | 50 | 66 | 50 | 50 | 50
2 | 18 | 18 | 66 | 18 | 18
3 | 1 | 1 | 1 | 66 | 1
4 | 0 | 50 | 18 | 1 | X

## Slide 6: Problem statement
Intra
IBC
IBC
IBC
CuPredMode[xCuY][yCuY] ????
CuPredMode[xCb][yCb]
Block Vector

## Slide 7
8.6 Decoding process for coding units coded in IBC prediction mode 8.6.1 General decoding process for coding units coded in IBC prediction mode The motion vector components of the current coding unit are derived as follows: If treeType is equal to SINGLE_TREE or DUAL_TREE_LUMA, the following applies: ……… ……… Otherwise, if treeType is equal to DUAL_TREE_CHROMA, the following applies: The number of luma coding subblocks in horizontal direction numSbX and in vertical direction numSbY are derived as follows: numSbX = ( cbWidth >> 2 ) (8‑955) numSbY = ( cbHeight >> 2 ) (8‑956) The chroma motion vectors mvC[ xSbIdx ][ ySbIdx ] are derived as follows for xSbIdx = 0..numSbX − 1, ySbIdx = 0..numSbY − 1: The luma motion vector mvL[ xSbIdx ][ ySbIdx ] is derived as follows: The location ( xCuY, yCuY ) of the collocated luma coding unit is dervied as follows: xCuY = xCb + xSbIdx*4 (8‑957) yCuY = yCb + ySbIdx*4 (8‑958) If CuPredMode[ xCuY ][ yCuY ][DUAL_TREE_LUMA] is equal to MODE_INTRA, the following applies. mvL[ xSbIdx ][ ySbIdx ][ 0 ] = 0 (8‑959) mvL[ xSbIdx ][ ySbIdx ][ 1 ] = 0 (8‑960) Otherwise ( CuPredMode[ xCuY ][ yCuY ][DUAL_TREE_LUMA] is equal to MODE_IBC ), the following applies: mvL[ xSbIdx ][ ySbIdx ][ 0 ]=MvL0[ xCuY ][ yCuY ][ 0 ] (8‑963) mvL[ xSbIdx ][ ySbIdx ][ 1 ]=MvL0[ xCuY ][ yCuY ][ 1 ] (8‑964)