## Slide 1: CE6-related: Simplification of the Reduced Secondary Transform
M. Siekmann M. Winken H. Schwarz D. Marpe T. Wiegand
JVET-N0555

## Slide 2: Introduction: Reduced Secondary Transform
Orange: secondary transform coefficients
Blue: enforced non-significant coefficients
Green: coefficients unaltered by the RST (‚primary-only‘ coefficients )
RST index is signalled if none of the the coefficients in the restricted (blue) area is significant.
64x16 RST Matrix
48x16 RST Matrix

## Slide 3: Proposal: Zeroing of ‘primary-only’ coefficients
64x16 RST Matrix
48x16 RST Matrix
16 x16 RST Matrix
Only the first coefficient sub-group (4x4) can have significant coefficients when RST is applied. The signalling constraint for the RST index can be derived from the last-significant position.

## Slide 4: Results
Test 3 (on top of CE6-3.1d):
48x16 RST
2 transforms per set
8kB table size
worst case: 22 multipl. p. coeff. (sec. + prim. transform)
(For comparison DCT-II x DCT-II: 32x32: 40, 16x16: 32 multipl. p. coefficient [JVET-M0046])

## Slide 5: Conclusion
compared to JVET-N0193:
Encoder runtime overhead is halved (AI: 113% vs. 126%)
negligible effect on the performance (AI: -1.28% vs. -1.34%)
Number of multiplications per coefficient (primary+secondary) is the same for 8x8 and 4x4, reduced for all other block sizes
Condition for RST index signalling is simplified.
We would like to thank LGE for the cross-checking.

## Slide 6: Results – Test3 ( JVET-N0555 on top of CE6-3.1d )
Test 3: (on top of CE6-3.1d): 48x16 RST, 2 transforms per set, 8kB

## Slide 7: Results
Test 1:
64x16 RST
1 transform per set
5kB table size
no RST for 4x4
worst case: 24 multipl. p. coeff. (sec. + prim. transform)
(For comparison DCT-II x DCT-II: 32x32: 40, 16x16: 32 multipl. p. coefficient [JVET-M0046])

## Slide 8: Results: JVET-N0555 Test 1

## Slide 9: Results
Test 4 (on top of CE6-3.1e):
64x16 RST
1 transform per set
5kB table size
worst case: 32 multipl. p. coeff. (sec. + prim. transform)
(For comparison DCT-II x DCT-II: 32x32: 40, 16x16: 32 multipl. p. coefficient [JVET-M0046])

## Slide 10: Results – Test 4 ( JVET-N0555 on top of CE6-3.1e )
Test 4: (on top of CE6-3.1e): 64x16 RST, 1 transform per set, 5kB