## Slide 1: Context reduction for inter and split syntax elements
JVET-N0600
Mars 2019
Y. Chen, F. Le Léannec, T. Poirier

## Slide 2: JVET-N0600
  VTM-4.0 for affine_flag, amvr_flag, triangle_flag and split_qt_flag coding:
    Context ID derivation uses left (L) and above (A) neighboring syntax elements
      ctxId = (L is available && condition L) (A is available && condition A)
    Context ID for some inter syntax elements
      affine_flag ctxId = (L is available && L is affine) (A is available && A is affine)
      amvr_flag ctxId = (L is available && L is AMVR) (A is available && A is AMVR)
      triangle_flag ctxId = (L is available && L is triangular prediction) (A is available && A is triangular prediction)
    Context ID for split syntax element:
      split_qt_flag ctxId = (L is available && cqDepth_L > cqDepth) (A is available && cqDepth_A > cqDepth) (cqDepth < 2 ? 0: 2)

## Slide 3: JVET-N0600
  Proposed Method 1:
    Derive context ID for affine_flag and split_qt_flag with the OR information
      affine_flag ctxId = (L is available && L is affine) (A is available && A is affine)
      split_qt_flag ctxId = (L is available && cqDepth_L > cqDepth) (A is available && cqDepth_A > cqDepth) (cqDepth < 2 ? 0: 2)
    Saves 1 context for affine_flag and 2 contexts for split_qt_flag

## Slide 4: JVET-N0600: Method 1 (-3 ctx)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | 0.04% | 104% | 103%
Class A2 | 0.04% | -0.08% | 0.01% | 103% | 102%
Class B | 0.02% | 0.00% | -0.12% | 102% | 101%
Class C | 0.02% | -0.12% | -0.04% | 101% | 102%
Class E |  |  |  |  | 
Overall | 0.02% | -0.04% | -0.04% | 102% | 101%
Class D | 0.01% | 0.02% | -0.21% | 101% | 103%
Class F (optional) | 0.04% | -0.10% | -0.07% | 102% | 103%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | 0.04% | 102% | 99%
Class A2 | 0.00% | 0.09% | -0.02% | 100% | 98%
Class B | 0.00% | -0.01% | 0.07% | 99% | 99%
Class C | 0.03% | -0.04% | 0.03% | 101% | 99%
Class E | -0.01% | -0.01% | 0.01% | 102% | 100%
Overall | 0.00% | 0.01% | 0.03% | 101% | 99%
Class D | 0.03% | 0.06% | -0.11% | 102% | 98%
Class F (optional) | 0.06% | 0.02% | -0.03% | 102% | 103%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 0.00% | 0.28% | -0.02% | 102% | 99%
Class E | 0.10% | 0.50% | 0.26% | 101% | 100%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.04% | 0.33% | -0.23% | 101% | 101%
Class F (optional) | -0.04% | 0.15% | 0.35% | 99% | 100%

## Slide 5: JVET-N0600
  Proposed Method 2:
    Only uses one context ID for amvr_flag and triangle_flag
      amvr_flag ctxId = affine ? 3 : (L && L is AMVR) (A && A is AMVR) 0
      triangle_flag ctxId = (L && L is triangle) (A && A is triangle)0
    No more information needed from neighboring blocks
    Reduces the line buffer size and parsing complexity
    Saves 2 contexts for amvr_flag and 2 contexts for triangle_flag
    Harmonize amvr_flag context with and without affine

## Slide 6: JVET-N0600: Method 2 (-4 ctx)
Thanks to Qualcomm for cross-check!
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | 0.03% | 104% | 98%
Class A2 | -0.02% | 0.00% | 0.03% | 102% | 98%
Class B | -0.01% | -0.02% | -0.13% | 102% | 98%
Class C | 0.00% | -0.12% | -0.03% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | -0.04% | -0.04% | 102% | 98%
Class D | -0.02% | -0.03% | -0.09% | 100% | 99%
Class F (optional) | -0.01% | 0.04% | -0.02% | 102% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.12% | -0.23% | 101% | 98%
Class C | -0.02% | 0.08% | 0.07% | 101% | 98%
Class E | -0.03% | 0.14% | -0.32% | 101% | 101%
Overall | -0.01% | 0.01% | -0.15% | 101% | 99%
Class D | -0.01% | -0.04% | -0.40% | 99% | 99%
Class F (optional) | -0.07% | -0.34% | -0.15% | 99% | 100%

## Slide 7: JVET-N0600: Method 1 + Method 2 (-7 ctx)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | 0.03% | 104% | 102%
Class A2 | -0.02% | 0.00% | 0.03% | 102% | 102%
Class B | 0.01% | 0.00% | -0.08% | 101% | 100%
Class C | 0.03% | -0.02% | -0.08% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.01% | 0.00% | -0.04% | 102% | 101%
Class D | 0.03% | 0.00% | -0.01% | 100% | 104%
Class F (optional) | 0.04% | -0.09% | -0.13% | 103% | 103%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | 0.04% | 102% | 100%
Class A2 | 0.00% | 0.09% | -0.02% | 100% | 98%
Class B | 0.00% | -0.01% | 0.07% | 100% | 100%
Class C | 0.03% | -0.04% | 0.03% | 102% | 102%
Class E | -0.01% | -0.01% | 0.01% | 101% | 100%
Overall | 0.00% | 0.01% | 0.03% | 101% | 100%
Class D | 0.03% | 0.06% | -0.11% | 101% | 100%
Class F (optional) | 0.06% | 0.02% | -0.03% | 102% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.01% | 0.21% | -0.11% | 103% | 100%
Class E | 0.15% | 0.90% | 0.81% | 101% | 101%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.01% | -0.16% | -0.60% | 99% | 99%
Class F (optional) | -0.01% | 0.03% | -0.39% | 99% | 99%

## Slide 8: JVET-N0600 + JVET-N0311 (-83 ctx)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.08% | 0.24% | 0.21% | 104% | 103%
Class A2 | 0.11% | 0.13% | 0.02% | 103% | 103%
Class B | 0.05% | 0.21% | 0.06% | 102% | 101%
Class C | 0.09% | 0.09% | -0.15% | 102% | 101%
Class E |  |  |  |  | 
Overall | 0.08% | 0.17% | 0.03% | 103% | 102%
Class D | 0.07% | -0.08% | -0.10% | 102% | 102%
Class F (optional) | 0.04% | 0.02% | 0.26% | 104% | 103%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.08% | 0.26% | 0.33% | 106% | 101%
Class A2 | 0.12% | 0.51% | 0.35% | 103% | 99%
Class B | 0.08% | 0.15% | 0.13% | 105% | 101%
Class C | 0.10% | -0.02% | 0.16% | 105% | 101%
Class E | 0.06% | 0.19% | 0.05% | 105% | 99%
Overall | 0.09% | 0.20% | 0.19% | 105% | 100%
Class D | 0.10% | 0.14% | -0.15% | 105% | 99%
Class F (optional) | 0.04% | 0.12% | 0.15% | 108% | 105%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.27% | -0.13% | 106% | 106%
Class C | -0.04% | 0.12% | -0.09% | 103% | 100%
Class E | 0.09% | 0.65% | 0.63% | 103% | 102%
Overall | 0.00% | 0.09% | 0.07% | 104% | 103%
Class D | -0.10% | 0.21% | -0.04% | 103% | 102%
Class F (optional) | -0.05% | 0.02% | -0.57% | 101% | 101%

## Slide 9: JVET-N0600: Context reduction for inter and split syntax elements
  Conclusion
    Reduced complexity for context ID computation and number of context ID
    Method 2: No more neighboring blocks information
Proposed method | Nb contexts vs. VTM-4.0 | RA (Y/Cb/Cr)
1 | -3 | 0.02% -0.04% -0.04%
2 | -4 | -0.01% -0.04% -0.04%
1+2 | -7 | 0.01% 0.00% -0.04%
N0311 + N0600 | -83 | 0.08% 0.17% 0.03%
Thanks to Qualcomm for cross-check!