## Slide 1: JVET-N0671 Support of 4:4:4 and 4:2:2 chroma formats in VVC
A. Filippov, V. Rufitskiy, T. Solovyev, R. Chernyak, J. Chen (Huawei), X. Zhao, X. Li, X. Xu, S. Liu (Tencent), H. Wang, Y.-H. Chao, W.-J. Chien, V. Seregin, M. Karczewicz (Qualcomm)

## Slide 2
Support of chroma 4:4:4 format

## Slide 3: Modifications to the VTM decoding process
4:4:4 format:
  CCLM:
    no downsampling

## Slide 4: Modifications to the VTM decoding process (cont’d)
4:4:4 format:
  Affine chroma subblock motion vector derivation:
    Use MV of co-located luma subblock in case of 4:4:4 format
Luma subblocks
Chroma subblocks
(4:4:4 case)

## Slide 5: ISP changes (editorial)

## Slide 6: Experimental setup
Anchor software: HM-16.18-SCM8.7-rext
Test material is defined in JCT-VC RExt CTC:
C. Rosewarne, K. Sharman, D. Flynn, “Common test conditions and software reference configurations for HEVC range extensions” , JCTVC-P1006, 16th JCT-VC Meeting, San Jose, CA, January 2014.
Test conditions are defined in JVET CTC:
F. Bossen, J. Boyce, X. Li, V. Seregin, K. Sühring, “JVET common test conditions and software reference configurations for SDR video”, JVET-L1010, 12th JVET Meeting, Macao, China, October 2018.

## Slide 7: Results for RGB content
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
Traffic_2560x1600_30_12bit_444.rgb | -27.8% | -13.1% | -18.1% | -34.8% | -17.3% | -23.5% | -33.7% | -16.5% | -20.4%
Kimono1_1920x1080_24_10bit_444.rgb | -28.9% | -10.6% | -11.2% | -35.5% | -17.5% | -23.3% | -28.1% | -11.0% | -16.0%
EBULupoCandlelight_1920x1080_50_10bit_444.rgb | -25.7% | -21.3% | -23.5% | -31.3% | -28.6% | -26.9% | -22.3% | -16.5% | -16.5%
EBURainFruits_1920x1080_50_10bit_444.rgb | -24.5% | -19.1% | -24.2% | -19.7% | -19.0% | -19.3% | -4.3% | 1.3% | 0.8%
VenueVu_1920x1080_30_8bit_444.rgb | -25.7% | -21.0% | -19.7% | -38.1% | -33.5% | -33.3% | -28.0% | -23.0% | -23.5%
DucksAndLegs_1920x1080_30_10bit_444.rgb | -6.3% | -6.8% | -3.4% | -26.9% | -8.9% | -12.5% | -23.7% | -8.1% | -7.2%
OldTownCross_1920x1080_50_10bit_444.rgb | -13.6% | -14.2% | -12.3% | -35.5% | -13.9% | -15.4% | -24.9% | -14.4% | -13.4%
ParkScene_1920x1080_24_10bit_444.rgb | -21.5% | -10.1% | -10.3% | -31.4% | -15.5% | -19.1% | -30.3% | -13.5% | -12.9%
Overall | -21.7% | -14.5% | -15.3% | -31.7% | -19.3% | -21.7% | -24.4% | -12.8% | -13.4%
Enc Time[%] | 2000% |  |  | 723% |  |  | 604% |  | 
Dec Time[%] | 143% |  |  | 134% |  |  | 121% |  | 

## Slide 8: Results for YUV4:4:4 content
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
Traffic_2560x1600_30_10bit_444_crop.yuv | -24.8% | -10.9% | -11.6% | -31.8% | -17.4% | -15.7% | -29.4% | -16.1% | -9.7%
Kimono1_1920x1080_24_10bit_444.yuv | -24.3% | -8.9% | -7.6% | -30.0% | -18.1% | -14.8% | -24.5% | -8.1% | -4.0%
EBULupoCandlelight_1920x1080_50_10bit_444.yuv | -18.2% | -18.9% | -22.8% | -24.2% | -25.2% | -25.2% | -21.2% | -17.3% | -21.2%
EBURainFruits_1920x1080_50_10bit_444.yuv | -17.5% | -15.6% | -16.2% | -24.3% | -14.8% | -14.2% | -16.6% | -4.2% | 7.7%
VenueVu_1920x1080_30_10bit_444.yuv | -24.8% | -20.8% | -18.4% | -39.8% | -33.0% | -32.1% | -31.9% | -22.5% | -23.3%
BirdsInCage_1920x1080_60_10bit_444.yuv | -27.9% | -8.8% | -9.7% | -48.4% | -33.1% | -12.8% | -47.4% | -21.1% | -2.3%
CrowdRun_1920x1080_50_10bit_444.yuv | -15.3% | -12.3% | -12.9% | -24.7% | -20.5% | -21.9% | -20.8% | -13.4% | -13.0%
Overall | -21.8% | -13.7% | -14.2% | -31.9% | -23.2% | -19.5% | -27.4% | -14.7% | -9.4%
Enc Time[%] | 1475% |  |  | 573% |  |  | 527% |  | 
Dec Time[%] | 141% |  |  | 128% |  |  | 116% |  | 

## Slide 9: Results for Screen content (summary)
 | All Intra |  |  | Rancomaccess |  |  | LowDelay |  | 
 | Over HM-16.18+SCM8.7 |  |  | Over HM-16.18+SCM8.7 |  |  | Over HM-16.18+SCM8.7 |  | 
 | Y | U | V | Y | U | V | Y | U | V
TGM444 1080p | 30.23% | 56.81% | 58.46% | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Mixed & Camera Captured 1080p | -16.36% | -0.57% | 1.23% | -22.23% | -5.24% | -4.08% | #VALUE! | #VALUE! | #VALUE!
TGM444 720p | 0.96% | 28.52% | 37.62% | -5.10% | 19.20% | 28.56% | #VALUE! | #VALUE! | #VALUE!
Animation 720p | -20.98% | -0.83% | -2.76% | -29.02% | -3.47% | -9.01% | #VALUE! | #VALUE! | #VALUE!
Mixed 2560x1440 | -7.50% | 25.26% | 25.99% | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall All | 2.84% | 27.81% | 31.23% | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time [%] | 707.74% |  |  | #DIV/0! |  |  | #DIV/0! |  | 
Dec Time[%] | 157.54% |  |  | #DIV/0! |  |  | #DIV/0! |  | 

## Slide 10: Results for TGM 4:4:4 sequences
 |  | All Intra |  |  | Rancomaccess |  |  | LowDelay |  | 
 |  | Over HM-16.18+SCM8.7 |  |  | Over HM-16.18+SCM8.7 |  |  | Over HM-16.18+SCM8.7 |  | 
 |  | Y | U | V | Y | U | V | Y | U | V
1080p | FlyingGraphics_444 | 4.59% | 32.64% | 34.96% | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Desktop_444 | 48.20% | 71.84% | 76.81% | 31.18% | 42.88% | 45.99% | #VALUE! | #VALUE! | #VALUE!
 | Console_444 | 31.70% | 58.86% | 52.12% | 11.57% | 18.91% | 13.45% | #VALUE! | #VALUE! | #VALUE!
 | ChineseEditing_444 | 36.43% | 63.92% | 69.93% | 25.63% | 59.07% | 63.13% | #VALUE! | #VALUE! | #VALUE!
720p | Web_Brousing_444 | 24.40% | 74.90% | 85.62% | 31.94% | 69.30% | 72.43% | #VALUE! | #VALUE! | #VALUE!
 | Map_444 | -5.35% | 31.23% | 52.16% | -20.38% | 13.40% | 35.54% | #VALUE! | #VALUE! | #VALUE!
 | Programming_444 | -4.63% | 8.85% | 13.55% | -6.53% | 6.38% | 17.74% | #VALUE! | #VALUE! | #VALUE!
 | SlideShow_444 | -10.56% | -0.91% | -0.84% | -25.41% | -12.28% | -11.49% | #VALUE! | #VALUE! | #VALUE!
 |  | 694% |  |  | #DIV/0! |  |  | #DIV/0! |  | 
 |  | 169% |  |  | #DIV/0! |  |  | #DIV/0! |  | 

## Slide 11
Support of chroma 4:2:2 format

## Slide 12: Modifications to the VTM decoding process
4:2:2 format:
  CCLM:
    [1 2 1] / 4 filtering prior to downsampling in horizontal direction

## Slide 13: Modifications to the VTM decoding process (cont’d)
4:2:2 format:
  Affine chroma subblock motion vector derivation:
    Use averaging for MV of two horizontally-adjacent luma sub-blocks
Luma subblocks
Chroma subblocks
(4:2:2 case)

## Slide 14: Results for YUV4:2:2 content
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
Traffic_2560x1600_30_10bit_422_crop.yuv | -23.5% | -16.6% | -21.2% | -28.2% | -20.5% | -22.4% | -24.0% | -16.8% | -15.2%
Kimono1_1920x1080_24_10bit_422.yuv | -22.4% | -16.4% | -13.8% | -26.1% | -23.9% | -15.8% | -19.8% | -12.9% | -5.7%
EBUHorse_1920x1080_50_10bit_422.yuv | -13.2% | -17.2% | -25.3% | -19.3% | -27.4% | -27.0% | -20.3% | -26.8% | -30.2%
EBUGraphics_1920x1080_50_10bit_422.yuv | -20.2% | -19.0% | -20.8% | -28.0% | -25.3% | -25.9% | -27.3% | -26.1% | -26.5%
EBUWaterRocksClose_1920x1080_50_10bit_422.yuv | -14.8% | -10.1% | -10.4% | -14.6% | -12.6% | -10.5% | -13.6% | -10.7% | -8.6%
EBUKidsSoccer_1920x1080_50_10bit_422.yuv | -10.0% | -26.2% | -26.2% | -11.9% | -32.5% | -34.6% | -13.7% | -35.8% | -32.3%
Seeking_1920x1080_50_10bit_422.yuv | -20.4% | -30.7% | -21.9% | -26.8% | -38.9% | -25.8% | -21.9% | -19.5% | -13.6%
Overall | -17.8% | -19.5% | -20.0% | -22.1% | -25.9% | -23.2% | -20.1% | -21.2% | -18.9%
Enc Time[%] | 2435% |  |  | 665% |  |  | 564% |  | 
Dec Time[%] | 157% |  |  | 138% |  |  | 119% |  | 

## Slide 15
Chroma alignment

## Slide 16: Modifications to the VTM decoding process
Unification of chroma operations for YUV4:4:4
  Triangle edge pixel blending: avoid using longWeight for YUV 4:4:4 chroma.
  Intra reference sample smoothing: disable for YUV 4:4:4 chroma.

## Slide 17: Results of proposed chroma alignment
Compared with HM RExt
 | All Intra |  |  |  | 
 | Over HM-16.18+SCM8.7 |  |  |  | 
 | Y | U | V | EncT | DecT
RGB 4:4:4 | -21.7% | -14.5% | -15.3% | 2037% | 138%
YCbCr 4:4:4 | -21.8% | -13.7% | -14.1% | 1512% | 141%
Overall All | -21.8% | -14.1% | -14.8% | 1772% | 139%
 | Rancomaccess |  |  |  | 
 | Over HM-16.18+SCM8.7 |  |  |  | 
 | Y | U | V | EncT | DecT
RGB 4:4:4 | -31.5% | -19.2% | -21.5% | 703% | 142%
YCbCr 4:4:4 | -31.9% | -23.1% | -19.6% | 559% | 143%
Overall All | -31.7% | -21.0% | -20.6% | 631% | 143%
 | All Intra |  |  |  | 
 | Over VTM+444 |  |  |  | 
 | Y | U | V | EncT | DecT
RGB 4:4:4 | 0.01% | 0.02% | 0.07% | 100% | 98%
YCbCr 4:4:4 | 0.00% | 0.03% | 0.03% | 99% | 98%
Overall All | 0.01% | 0.02% | 0.05% | 100% | 98%
 | Random Access |  |  |  | 
 | Over VTM+444 |  |  |  | 
 | Y | U | V | EncT | DecT
RGB 4:4:4 | 0.21% | 0.14% | 0.23% | 100% | 99%
YCbCr 4:4:4 | 0.00% | 0.05% | -0.13% | 100% | 100%
Overall All | 0.11% | 0.10% | 0.06% | 100% | 100%
Compared with VTM+4:4:4 support

## Slide 18: Recommended action items
Necessary changes for VTM to enable 4:4:4
Changes for 4:2:2
Changes for Chroma alignment