## Slide 1: JVET-N0808: Joint proposal on configurable max transform size of JVET-N0362 and JVET-N0227
X. Zhao, X. Li, S. Liu (Tencent), L. Li, M. Koo, J. Heo, J. Lim, S. Kim (LGE)

## Slide 2: Problem statement
In VVC spec draft 4, the maximum transform size is fixed as 64x64
The VTM-4.0 SW has a configuration parameter for max transform size, but not working properly (SW crashes if set to be 32 or 16)
It can be a desirable feature to support configurable maximum transform size in HLS, such that for encoder have the flexibility to support large CU without an effort to do large transform size

## Slide 3: Proposal
Several spec and sw fixes are proposed to support max transform size
HLS: a high-level syntax is added to SPS to configure max TU size
SBT: max CU allowing SBT is set to be no larger than max TU size
ISP: max CU allowing ISP is set to be no larger than max TU size
CIIP: max CU allowing CIIP is set to be no larger than max TU size
The CU is first split into multiples of min(W, 64) x min (H, 64), then each sub-block is further split into max TU size

## Slide 4
Max TU 32x32 by limiting Max CU size (Encoder)
Max TU 32x32 by Proposal (HLS syntax and SBT and ISP fixes)
Max TU 32x32 by Proposal (HLS syntax and SBT and ISP fixes), --MaxBTDepth=1

## Slide 5
Max TU 16x16 by limiting Max CU size (Encoder)
Max TU 16x16 by SW and Spec text fix (Proposal, including HLS syntax and SBT and ISP fixes)