## Slide 1: Study on Immersive Media Decoding Interface for VVC (m47925)
Youngkwon Lim (Samsung)
& Emmanuel Thomas (TNO)

## Slide 2: Legacy decoding interface
Access Unit from a single Elementary Stream (same Profile/Level and parameters)
Presentation Unit or Composition Unit as a decoded media data for synchronized presentation according to PTS or CTS
Figure 4 — Flow diagram for the systems (elementary) decoder model
Figure 2-1 – Transport Stream system target decoder notation
13818-1
14496-1

## Slide 3: Application example: 360 tiled streaming
Viewport determines the video stream selection
1 | 2 | 3 | 4 | 5 | 6
7 | 8 | 9 | 10 | 11 | 12
13 | 14 | 15 | 16 | 17 | 18
19 | 20 | 21 | 22 | 23 | 24
Only video streams 1, 4, 7, 10, 11, 12, 13, 14, 15, 16, 21 and 22 are dynamically selected, streamed and decoded at this point in time to render the viewport.
(in practice, some 16 out of 96)
24 video streams
are encoded and made available
The dynamically changing small fractions from multiple elementary stream are extracted and combined as a single elementary stream whose profile/level could be different than that of original elementary streams

## Slide 4: Application example: Point Cloud Objects with 360 video
A content is composed of one 360 degree 2D video with VVC PTL X1 and two point cloud objects encoded with VVC PTL X2 and X3 respectively.
At a given time, each user needs up to one point cloud object and a portion of 2D video depends on the location, viewport, FoV and so on.
The dynamically changing combination of a fraction of 2D video and a point cloud data encoded as video
are extracted from each elementary streams and combined as a single elementary stream
whose profile/level could be different than that of original elementary streams

## Slide 5: Simulcasting not suitable for Immersive Media
Decoder
CB
DB
PTL A
…
AU
NALU
picture
Decoder
CB
DB
…
Decoder
CB
DB
…
PTL B
PTL C
GPU
Simulcasting with independent decoder instances brings the following challenges:
  No interoperability point between content and application (number of parallel decoding instances u not predictable)
  Variability in time to decode frames across decoder instances while the output pictures are intended to be composed into one picture for rendering
Time-locking is difficult

## Slide 6: New System Decoder Model for Immersive Media
Can we design a NALUs and decoder to allow following operation?
  Each source is encoded in different bitstreams conforming to different PTLs
  Each source may be in different format (e.g. resolution, framerate, bit depth, etc.)
  Bitstream extractor & merger operations are limited to copy/paste and simple modification operations
  Each AU may have NALUs of different random access type (e.g. IRAP and non IRAP)
Ongoing JVET activities related with contributions at this meeting
  NALU Header design
  Independent coded picture regions
Systems is interested in studying following topics to answer this question
  How to specify normative bitstream extraction & merging operation?
  What are the information need to be exposed in NALU header?
PTL A
…
NALU
…
…
Decoder
CB
DB
…
picture
Bitstream Extractor
& Merger
PTL B
PTL C
PTL X
GPU
Time-locking is natural
AU