## Slide 1: CE8-related: Combination test of JVET-N0176/JVET-N0317/JVET-N0382 on simplification of IBC vector prediction (JVET-N0843)
X. Xu, X. Li, S. Liu (Tencent)
Y. Han, W.-J. Chien, M. Karczewicz (Qualcomm)
H. Gao, S. Esenlik, B. Wang, A. M. Kotra, J. Chen (Huawei)
2019/03

## Slide 2: Summary
Currently in VVC WD-4.0/VTM-4.0,
  IBC is considered in VVC as a separate mode from inter/intra mode
  IBC BV prediction is (in merge and AMVP) largely aligned with inter, but not necessary
In this contribution, two aspects are proposed
  Apply a simplified IBC predictor list to both merge and AMVP mode
  Reduce pruning operation of HMVP from 4 to 2
It is reported that the proposed methods bring:
  No significant performance change to the VTM-4 anchor
  Simplification to the BV derivation process

## Slide 3: Current BV prediction in VVC
Merge mode
  5 spatial neighboring positions
  5 HMVP entries
  1 pairwise average
Note: list may not be full
AMVP mode
  First available candidate from left two neighbors
  First available candidate from top three neighbors
  4 HMVP entries
  Zero vector candidates

## Slide 4: Proposed BV predictor list
Apply the following list to both merge and AMVP mode
  2 spatial neighboring positions (A1, B1 as in Fig. )
  5 HMVP entries
  Zero vectors
HMVP pruning up to 2
  Opt1: pruning with 1st HMVP cand.
  Opt2: pruning with 1st Spatial cand.

## Slide 5: Simulation results
BVP with 2 HMVP pruning, Opt. 1
BVP with 2 HMVP pruning, Opt. 2
BVP with 4 HMVP pruning (VTM)
 | All Intra Main10 |  |  |  | 
 | Over VTM401 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.05% | -0.03% | 0.07% | 95% | 93%
Class TGM | 0.15% | 0.13% | 0.12% | 95% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM401 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.04% | 0.06% | -0.09% | 97% | 95%
Class TGM | 0.09% | 0.09% | 0.06% | 96% | 93%
 | All Intra Main10 |  |  |  | 
 | Over VTM401 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.05% | -0.01% | 0.06% | 98% | 97%
Class TGM | 0.17% | 0.14% | 0.13% | 96% | 94%
 | Random Access Main 10 |  |  |  | 
 | Over VTM401 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.09% | 0.05% | 0.13% | 99% | 97%
Class TGM | 0.16% | 0.14% | 0.17% | 97% | 96%
 | All Intra Main10 |  |  |  | 
 | Over VTM401 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.04% | 0.00% | 0.13% | 96% | 95%
Class TGM | 0.07% | 0.09% | 0.05% | 97% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM401 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.08% | 0.02% | 0.22% | 98% | 96%
Class TGM | 0.07% | 0.05% | 0.08% | 97% | 95%

## Slide 6: Conclusion
In this contribution, simplification of BV prediction for IBC mode is proposed
It is reported that the BD rate changes are minor compared with the VTM-4.0.1 anchor
It is recommended to adopt one of the two methods in this proposal into VVC
Thanks Alibaba for performing crosschecking!