## Slide 1: JVET-O0366 Non-CE4 : Simplifications on BCW index derivation process
N. Park, H. Jang, J. Nam, J. Lim, S. Kim

## Slide 2: Introduction
For affine merge constructed mode, BCW index is derived by
  Check whether two or more CPs has the same BCW index
  Check whether BCW index of all CPs are in the same group
  In working draft.
if (bcwIdxCorner0 == bcwIdxCorner1 && bcwIdxGroup0 == bcwIdxGroup2) bcwIdxConst = bcwIdxCorner0 else if (bcwIdxCorner0 == bcwIdxCorner2 && bcwIdxGroup0 == bcwIdxGroup1) bcwIdxConst = bcwIdxCorner0 else if (bcwIdxCorner1 == bcwIdxCorner2 && bcwIdxGroup1 == bcwIdxGroup0) bcwIdxConst = bcwIdxCorner2 else bcwIdxConst = Default value
Candidates of the constructed mode :
[CP0, CP1, CP2]
[CP0, CP1, CP3]
[CP0, CP2, CP3]
[CP1, CP2, CP3]
[CP0, CP1]
[CP0, CP2]
For affine merge candidate : Max 4 candidates (with 3 CPs) x 6 comparison + 1 candidate (with 2 CPs) x 1 = 25

## Slide 3: Introduction
Point 1. BCW index of the CP3 (TMVP) is set to default value (i.e., equal weight)
Point 2. BCW indices in non-low-delay condition is in one group (Group 1)
Candidates of the constructed mode with 3 CPs :
[CP0, CP1, CP2]
[CP0, CP1, CP3]
[CP0, CP2, CP3]
[CP1, CP2, CP3]
BCW index and Group index :
0 : (-1/4, 5/4) -------- Group 0
1 : (1/4, 3/4) -------- Group 1
2 : (2/4, 2/4) -------- Group 1
3 : (3/4, 1/4) -------- Group 1
4 : (5/4, -1/4) -------- Group 2
if (bcwIdxCorner0 == bcwIdxCorner1 && bcwIdxGroup0 == bcwIdxGroup2) bcwIdxConst = bcwIdxCorner0 else if (bcwIdxCorner0 == bcwIdxCorner2 && bcwIdxGroup0 == bcwIdxGroup1) bcwIdxConst = bcwIdxCorner0 else if (bcwIdxCorner1 == bcwIdxCorner2 && bcwIdxGroup1 == bcwIdxGroup0) bcwIdxConst = bcwIdxCorner2 else bcwIdxConst = Default value

## Slide 4: Proposed methods
Proposed simplified BCW index derivation methods
if (bcwIdxCorner0 == bcwIdxCorner1 && bcwIdxGroup0 == bcwIdxGroup2) bcwIdxConst = bcwIdxCorner0 else if (bcwIdxCorner0 == bcwIdxCorner2 && bcwIdxGroup0 == bcwIdxGroup1) bcwIdxConst = bcwIdxCorner0 else if (bcwIdxCorner1 == bcwIdxCorner2 && bcwIdxGroup1 == bcwIdxGroup0) bcwIdxConst = bcwIdxCorner2 else bcwIdxConst = Default value
if (bcwIdxCorner0 == bcwIdxCorner1) bcwIdxConst = bcwIdxCorner0 else bcwIdxConst = Default value
bcwIdxConst = bcwIdxCorner0
Proposed Method I : The number of comparison is reduced to 1 (in worst case, 25  5)
Proposed Method II : The number of comparison is reduced to 0 (in worst case, 25  0)

## Slide 5: Experimental results
Simulation results
  Anchor : VTM5.0 + bug-fix(Ticket #312 : BCW index initialization bug-fix)
  Proposed Method I : The number of comparison is reduced to 1
  Proposed Method II : The number of comparison is reduced to 0
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 with bug-fix (Ticket#312) |  |  |  |  | Over VTM-5.0 with bug-fix (Ticket#312) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.08% | 0.05% | 100% | 100% |  |  |  |  | 
Class A2 | 0.00% | 0.01% | -0.02% | 100% | 100% |  |  |  |  | 
Class B | 0.01% | 0.08% | -0.01% | 100% | 100% | -0.04% | -0.15% | -0.19% | 100% | 100%
Class C | 0.00% | -0.13% | -0.12% | 100% | 100% | -0.03% | 0.18% | -0.36% | 100% | 100%
Class E |  |  |  |  |  | -0.04% | 0.22% | 0.06% | 100% | 101%
Overall | 0.01% | 0.01% | -0.03% | 100% | 100% | -0.03% | 0.05% | -0.18% | 100% | 101%
Class D | 0.01% | 0.04% | 0.03% | 100% | 100% | -0.03% | 0.14% | 0.08% | 100% | 101%
Class F | 0.02% | -0.01% | 0.02% | 100% | 100% | 0.01% | -0.30% | -0.56% | 100% | 100%
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 with bug-fix (Ticket#312) |  |  |  |  | Over VTM-5.0 with bug-fix (Ticket#312) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.14% | 0.01% | 100% | 100% |  |  |  |  | 
Class A2 | 0.01% | -0.09% | -0.08% | 100% | 100% |  |  |  |  | 
Class B | 0.01% | 0.03% | 0.05% | 100% | 100% | -0.03% | -0.20% | -0.01% | 99% | 97%
Class C | -0.01% | -0.07% | 0.01% | 100% | 100% | 0.01% | 0.25% | -0.32% | 100% | 99%
Class E |  |  |  |  |  | 0.02% | 0.20% | 0.43% | 100% | 99%
Overall | 0.00% | 0.00% | 0.01% | 100% | 100% | 0.00% | 0.05% | 0.00% | 100% | 98%
Class D | 0.01% | 0.02% | 0.05% | 100% | 100% | -0.03% | 0.14% | 0.14% | 101% | 99%
Class F | 0.01% | 0.01% | 0.05% | 100% | 100% | -0.02% | -0.36% | -0.65% | 100% | 100%

## Slide 6: Conclusion
Simplified BCW index derivation methods for affine constructed candidate are proposed.
In worst case, the number of the comparison is reduced from 25 to 5 or 0.
The experimental results reportedly show negligible changes in BD-rate and run-time
It is recommended to consider Method I in the next VTM.
Thanks to Sharp (JVET-O0685) for crosscheck