## Slide 1: CE3-related: Chroma intra prediction mode mapping for 4:2:2 format
Biao Wang, Anand Meher Kotra, Semih Esenlik, Han Gao, Elena Alshina

## Slide 2
Chroma intra mode mapping for 4:2:2
For chroma 4:2:2 format, samples are sub-sampled by half at horizontal direction
  For mode 2 to 34, their corresponding width is increased by 2x
  For mode 34 to 66, their corresponding width is decrease by 1/2
Tan(α) =1/2
α

## Slide 3
Find theoretically accurate mapping
50
66
34
18
2
8
width
width/2
Tan(α) =1/2
α
(width)
A similar approach can be used for other modes.
  Note: for input mode 2 to 34, the column “intraPredAng/2” in 4:2:2 format is replaced with intraPredAng*2
42
43
44
44
45
46
46
48
In VVC6 draft 6

## Slide 4
Proposed Changes
Highlighted are the corrected new modes.

## Slide 5: Results
Simulation conducted with the 4:2:2 video sequences
Consistent coding gain are observed
 | Y | U | V | EncTime | DecTime
Traffic | -0.04% | -0.06% | -0.02% | 101% | 100%
Kimono | -0.05% | 0.04% | -0.17% | 101% | 101%
Seeking | -0.01% | -0.01% | 0.02% | 100% | 100%
EBUHorse | -0.02% | -0.04% | 0.03% | 100% | 100%
EBUGraphics | -0.06% | 0.02% | 0.00% | 99% | 100%
EBUWaterRocksClose | -0.01% | 0.00% | 0.01% | 99% | 99%
EBUKidSoccer | 0.00% | -0.04% | 0.03% | 100% | 100%
All | -0.03% | -0.01% | -0.01% | 100% | 100%
All intra
Random Access
 | Y | U | V | EncTime | DecTime
Traffic | 0.00% | -0.05% | 0.15% | 100% | 100%
Kimono | 0.00% | -0.02% | 0.00% | 100% | 100%
Seeking | -0.01% | -0.06% | -0.02% | 100% | 100%
EBUHorse | -0.02% | -0.09% | 0.05% | 100% | 100%
EBUGraphics | -0.01% | -0.07% | -0.07% | 100% | 100%
EBUWaterRocksClose | -0.02% | 0.07% | -0.01% | 100% | 100%
EBUKidSoccer | -0.01% | 0.07% | 0.19% | 100% | 100%
All | -0.01% | -0.02% | 0.04% | 100% | 100%

## Slide 6
A bug fix is proposed for the chroma intra mode mapping table using 4:2:2 format
Demonstrating how correct mapping is derived by example
Simulation results shown consistent coding gain
  AI : -0.03%
  RA: -0.01%
It is suggested to adopt this bug fix in the next version of VVC draft
Thanks NHK for crosschecking (JVET-P0915)
Summary

## Slide 8
predModeIntra | −14 | −13 | −12 | −11 | −10 | −9 | −8 | −7 | −6 | −5 | −4 | −3 | −2 | −1 | 2 | 3 | 4
intraPredAngle | 512 | 341 | 256 | 171 | 128 | 102 | 86 | 73 | 64 | 57 | 51 | 45 | 39 | 35 | 32 | 29 | 26
predModeIntra | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
intraPredAngle | 23 | 20 | 18 | 16 | 14 | 12 | 10 | 8 | 6 | 4 | 3 | 2 | 1 | 0 | −1 | −2 | −3
predModeIntra | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
intraPredAngle | −4 | −6 | −8 | −10 | −12 | −14 | −16 | −18 | −20 | −23 | −26 | −29 | −32 | −29 | −26 | −23 | −20
predModeIntra | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55
intraPredAngle | −18 | −16 | −14 | −12 | −10 | −8 | −6 | −4 | −3 | −2 | −1 | 0 | 1 | 2 | 3 | 4 | 6
predModeIntra | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72
intraPredAngle | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 23 | 26 | 29 | 32 | 35 | 39 | 45 | 51 | 57 | 64
predModeIntra | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 |  |  |  |  |  |  |  |  | 
intraPredAngle | 73 | 86 | 102 | 128 | 171 | 256 | 341 | 512 |  |  |  |  |  |  |  |  | 
Backup