## Slide 1: JVET-P0163 CE5-related: SAO encoder-only improvements
Presenter: Olena Chubach
Authors: Chen-Yen Lai, Ching-Yeh Chen, Tzu-Der Chuang, Olena Chubach, Yu-Wen Huang, Shaw-Min Lei

## Slide 2: Overall Summary
Applications of video encoders
  For real-time applications, one low-complexity encoder with low latency requirement is desirable and usually used
  For storage applications, a powerful encoder with picture-level optimization is used
SAO on/off tests under different encoding algorithms/conditions
  VTM6.0 uses CTU-level optimization in SAO
  Proposed one picture-level optimization encoding algorithm for SAO
YUV BD-rates | CTU-level optimization |  |  |  | Picture-level optimization |  |  | 
 | AI | RA | LB | LP | AI | RA | LB | LP
Under ALF-on | -0.04% | -0.13% | -0.24% | -0.26% | -0.15% | -0.29% | -0.52% | -0.52%
Under ALF-off | -0.36% | -0.78% | -1.21 % | -2.74% | -0.56% | -1.10% | -1.70% | -3.35%
YUV BD-rate is calculated using the same method as in AHG13.

## Slide 3: Applications of Video Encoders
For real-time applications (e.g. video recording, video conference, etc)
  Limited computation resources and low latency requirement, especially for mobile devices
For non-real-time applications (e.g. movie playback)
  Allow much higher computation resources and picture-level optimization
For different applications, different settings and encoding algorithms are used
In VTM6.0 CTC
  One picture-level optimization encoding algorithm is used for ALF
  One CTU-level optimization encoding algorithm is applied to SAO

## Slide 4: Picture-level Optimizations of SAO
Greedy SAO merge encoding algorithm
  Multiple CTUs of the same CTU row are grouped together to jointly optimize SAO parameters.
Picture-based SAO merge encoding algorithm
  A picture can be divided into regions aligned with CTU boundaries by a recursive quadtree (QT) splitting algorithm with a bottom up rate-distortion optimization (RDO) method.
  When a quadtree node has only one CTU in width or height, binary (BT) split can be applied for further split.
  Corresponding CTUs are grouped together to jointly optimize SAO parameters
After testing all CTUs, SAO picture-level on/off decision can be updated
  Allow changing the picture-level decision from on to off after SAO is tested for all CTUs in the picture by checking the picture cost.
X
X
X
X
Notes: Scan order is from top-left to bottom-right

## Slide 5: Simulation Results
The BD-rates of enabling SAO under different test conditions
  Implemented the encoding algorithm on top of VTM6.0
  Two kinds of encoding algorithms and w/wo ALF
YUV BD-rates | CTU-level optimization |  |  |  | Picture-level optimization |  |  | 
 | AI | RA | LB | LP | AI | RA | LB | LP
With ALF On | -0.04% | -0.13% | -0.24% | -0.26% | -0.15% | -0.29% | -0.52% | -0.52%
With ALF Off | -0.36% | -0.78% | -1.21 % | -2.74% | -0.56% | -1.10% | -1.70% | -3.35%
YUV BD-rate is calculated using the same method as in AHG13.

## Slide 6: Subjective View

## Slide 7
BasketballDrive_37_ldp_frame#28

## Slide 8
BasketballDrive_37_ldp_frame#28_saooff_alfoff

## Slide 9
BasketballDrive_37_ldp_frame#28_alfoff

## Slide 10
BQTerrace_37_ldp_frame#288

## Slide 11
BQTerrace_37_ldp_frame#288_saooff_alfoff

## Slide 12
BQTerrace_37_ldp_frame#288_alfoff

## Slide 13
Cactus_37_ldp_frame#60

## Slide 14
Cactus_37_ldp_frame#60_saooff_alfoff

## Slide 15
Cactus_37_ldp_frame#60_alfoff

## Slide 16
Video credit: JVET-P0639 provided by Huawei
BasketballDrill_CE5-3_3_2_QP37_LDP_NO_ALF vs. BasketballDrill_QP37_LDP_NO_ALF

## Slide 17: Conclusion
Proposed to improve SAO by encoder-only algorithm
Experimental results show that
  ALF is on and picture-level optimization is used for SAO: YCbCr BD-rate is 0.15%, 0.29%, 0.52%, 0.52% for AI, RA, LDB, and LDP
  ALF is off and CTU-level optimization is used for SAO: YCbCr BD-rate is 0.36%, 0.78%, 1.21%, 2.14% for AI, RA, LDB, and LDP
  Great subjective improvement when ALF is off
Given that SAO has low complexity and is deployed in more than one billion HEVC devices per year, keeping SAO is beneficial for VVC, especially for real-time low complexity encoding applications
Thanks to Samsung for cross-checking

## Slide 18
Thank You