## Slide 1
JVET-P0174
Non-CE4: Modifications of TPM and GEO
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
The blending and MV storage mask generation process is different between GEO and TPM:
For GEO, mask values are determined by calculating distance (ρ) from partitioning line of each sample in the GEO block.
For TPM, mask values are determined directly by simply comparing x and y coordinate values without calculating distance from partitioning line.
An illustration of distance calculation process of GEO

## Slide 3
Problem statement
 | TPM | GEO (140 modes) | GEO (64 modes)
# of supported PU size | 26 | 19 | 19
# of partitions/modes | 2 | 140 | 64
#of combination | 52 | 2660 | 1216
Mask storage cost | 60KB | 4,131KB | 1,889KB
TPM: If it is considered as a burden to store 60KB data, the mask can still be computed on-the-fly with little computation cost since the derivation process of masks are very simple.
GEO: Storage cost is pretty high for hardware design. It is preferred to derive mask values on-the-fly.
It might be a better design to (1) compute both TPM and GEO masks on-the-fly to save storage cost for both and (2) unify the process to avoid duplicate logic for mask calculation.

## Slide 4
Proposal
Following approach is proposed to unify GEO and TPM mask generation process:
GEO is enabled with 64 valid modes (CE4-1.2) and independent motion mask calculation process (CE 4-1.14).
Align blending and MV storage masks generation process of TPM to GEO.
  Blending and MV storage masks calculation of TPM reuses that of GEO.
  A second look up table (Table 2) is used to map an index (0 to 17, determined by width height ratio) to scaled value of sine (α) and cosine (α).
  Distance index of TPM is always set to 0.
idx | 0 | 1 | 2 | 3 | 4 | 5 | 8 | 11 | 12 | 13 | 14 | 15
Dis[idx] | 64 | 63 | 59 | 53 | 45 | 36 | 0 | -36 | -45 | -53 | -59 | -63
idx | 16 | 17 | 18 | 19 | 20 | 21 | 24 | 27 | 28 | 29 | 30 | 31
Dis[idx] | -64 | -63 | -59 | -53 | -45 | -36 | 0 | 36 | 45 | 53 | 59 | 63
idx | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
dis[idx] | -45 | -29 | -16 | -8 | -4 | -57 | -62 | -64 | -64
idx | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
dis[idx] | 45 | 57 | 62 | 64 | 64 | 29 | 16 | 8 | 4
Look-up table Dis for derivation of geometric partitioning distance for triangle partitioning mode.
Look-up table Dis for derivation of geometric partitioning distance for geometric partitioning mode.

## Slide 5
Simulation results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11% | -0.12% | -0.24% | 104% | 100%
Class A2 | -0.18% | -0.11% | -0.14% | 103% | 96%
Class B | -0.19% | -0.08% | -0.20% | 103% | 99%
Class C | -0.64% | -0.93% | -1.00% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.29% | -0.32% | -0.41% | 102% | 99%
Class D | -0.46% | -0.67% | -0.66% | 100% | 100%
Class F | -0.27% | -0.45% | -0.40% | 86% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.33% | -0.32% | -0.54% | 103% | 95%
Class C | -0.75% | -1.19% | -0.96% | 101% | 98%
Class E | -0.91% | -0.45% | -0.19% | 105% | 96%
Overall | -0.62% | -0.64% | -0.59% | 103% | 97%
Class D | -0.73% | -1.28% | -0.36% | 101% | 101%
Class F | -0.36% | -0.46% | 0.02% | 98% | 99%
Unification of blending and MV storage mask process of GEO and TPM

## Slide 6
Proposal
seq_parameter_set_rbsp( ) { | Descriptor
… | 
if(sps_geo_enabled_flag){ | 
is_geo_mode_signaled | u(1)
if(is_geo_mode_signaled){ | 
num_geo_mode_minus_1 | u(8)
for(i = 0; i <= num_geo_mode_minus_1; i++){ | 
geo_mode_idx | u(8)
} | 
} | 
} | 
… | 
} | 
The second part of this contribution proposes to use adaptive number of valid modes for GEO
GEO might create difficulty for hardware validation process (even for the simplified version of 64 modes). Allowing using only a selection of GEO modes instead of full sets to make hardware validation easier and it also benefits low cost encoder by reducing number of modes.
An illustration of syntax change for adaptive number of modes
Example syntax:
is_geo_mode_signaled = 1
num_geo_mode_minus_1 = 4
num_geo_mode_minus_1[0] = 0
num_geo_mode_minus_1[1] = 16
num_geo_mode_minus_1[2] = 32
num_geo_mode_minus_1[3] = 48

## Slide 7
7
Conclusion
This contributions proposes two approaches:
(1) Unify the blending and MV storage mask calculation process to avoid duplicate of logics with -0.29% luma coding impact on RA and -0.62% luma coding impact on LDB.
(2) Use adaptive number of valid GEO mode for the benefit of hardware validation and low cost encoder.

## Slide 8
8
Thank Huawei for cross-check